## Slide 1: eVoLP SA2 Status and Future Plan
SA2 Rapporteurs (Huawei)

## Slide 2: Goal
The document tries to list the major open topics of eVoLP after SA2#121 from SA2 point of view
It is used to trigger joint work among SA2 and SA4 on the upcoming MTSI SWG Teleconference on eVoLP on June 8.

## Slide 3: SA2 status
WI | Work Item | WP |  | 
FS_eVoLP | Study for enhanced VoLTE performance | 50 > 60% |  | 
Progress since SA2#121
  Three solutions for key issue 1 are documented in TR 23.759.
  LSs were sent to RAN2/SA4 on parameters for assisting RAN to optimize handover decision for VoLTE. SA4 needs more time for the reply.
  eVoLP will only focus on voice service and does not cover video service.
  Agree to choose a simple solution
Next steps:
  Study continues with the aim to conclude in Q3 also based on feedback from SA4.

## Slide 4: New Key Question from SA2 group
Question:
  when the UE is located in weak coverage and EVS-CA is within the negotiated codec code set, can we assume that the UE will switch to the most robust codec mode i.e. EVS-CA?
SA2 discussion
  Some companies like Huawei/Intel/ATT/China Telecom/China Mobile/QC/China Unicom/ZTE(?) agree that the UE should follow this behavior as the EVS-CA is designed for VoLTE weak coverage.
  This will benefit both UE/Network based solution as signaling exchange between UE/network and eNB can be reduced much, especially considering the signaling exchange between UE and eNB should be avoided as much as possible in weak coverage.

## Slide 5: Future plan for next SA2 meeting
SA2 suggest that both solutions be supported as the majority of SA2 see advantages with both UE- and Network-provided approaches.
  SA2 focus on network based solution ,aiming to conclude eVoLP in Q3
  SA2 inform RAN2 about the discussion outcome for UE based solution
Assuming that the UE will switch to the most robust mode, it is proposed to go with a simple solution i.e. UE or Network only provide robust index + other alternative parameters (which fully depends on SA4 discussion outcome).