## Slide 1: CMAF and CTA WAVE

## Slide 2: Different Players – single encoding and common delivery
CMAF
Content
Stand-alone HLS
HLS as HTML-5 video tag
Stand-alone DASH
DASH as HTML-5 video tag
HTML-5 MSE-based Type-3 player
CDN,
Broadcast, multicast
Application
DASH MPD
HLS M3U8
referencing
Platforms and Players
Content Offering
Manifest
Delivery

## Slide 3: Common Media Application Format (CMAF)

## Slide 4: ISO/IEC 23000-19 Interoperability and Conformance Code Points
CMAF Presentation Profile
Defines the minimum required Media Profiles and optional encryption schemes required in a Presentation of this Profile
CMAF Media Profiles and ISO BMFF Compatibility Brand
identify CMAF media sample and track format interoperability by specifying track and encoding constraints specific to a codec
Compatibility Brand for CMAF Addressable Objects
CMAF Addressable Objects for CMAF Tracks provide the ability to offer CMAF Tracks as physical resources to delivery and storage applications
CMAF Switching Set
identify CMAF Switching Sets that conform to Media Profile specified Switching Set constraints that enable seamless switching using a specified processing model

## Slide 5
Styp
cmfl
prft
emsg
moof
mdat
CMAF Chunk
CMAF Fragment
ftyp
cmfc
moov
CMAF Header
Styp
cmff
CMAF
Chunk
CMAF
Chunk
• • •
CMAF
Chunk
CMAF Track File
CMAF Segment
Styp
cmfs
CMAF Fragment
• • •
CMAF Fragment
CMAF Fragment
sidx
CMAF Fragment
• • •
CMAF Fragment
CMAF Fragment
CMAF Header

## Slide 6
CMAF Video Switching Set Generation
Audio Selection Set
Video Selection Set
Switching Set
Video content component A
Processing A
(Subsampling, etc.)
Processing B
(Subsampling, etc.)
Processing C
(Subsampling, etc.)
Encoding 1
Encoding 2
Encoding 3
Encoding 4
Encoding 5
Switching Set
Encoding parameters
Preprocessing parameters
Media content component properties
Encryption 1
Encryption 2
Encryption 3
Encryption 4
Encryption 5
Encapsulation1
Encapsulation 2
Encapsulation 3
Encapsulation 4
Encapsulation 5
Encryption Parameters
Resource
Generation 1
Resource Generation 2
Resource Generation 3
Resource Generation 4
Resource Generation 5
Encapsulation Parameters
Resource Location
Manifest
Video content component B
Audio content component A
Audio content component B
Switching Set
Switching Set
Video samples
CMAF External
CMAF Internal
CMAF Video Switching Set Generation
CMAF Audio Switching Set Generation
Subtitle Selection Set
Switching Set
Switching Set
Subtitle content component A
Subtitle content component B
CMAF Subtitle Switching Set Generation
Presentation 1
Presentation 2

## Slide 7: Video Media Profiles
Media Profile | Codec | Profile | Level | Color Coding | Transfer Characteristics | Max Frame Height | Max Frame Width | Max Frame Rate | CMAF File Brand
SD | AVC | High | 3.1 | BT.709 or BT.601 | BT.709 or BT.601 OETF | 576 | 854 | 60 | 'cfsd'
HD | AVC | High | 4.0 | BT.709 | BT.709 OETF | 1080 | 1920 | 60 | 'cfhd'
HDHF | AVC | High | 4.2 | BT.709 | BT.709 OETF | 1080 | 1920 | 60 | 'chdf'
HHD8 | HEVC | Main MainTier | 4.1 | BT.709 | BT.709 OETF | 1080 | 1920 | 60 | 'chhd'
HHD10 | HEVC | Main10 MainTier | 4.1 | BT.709 | BT.709 OETF | 1080 | 1920 | 60 | 'chh1'
UHD8 | HEVC | Main8 MainTier | 5.0 | BT.709 | BT.709 OETF | 2160 | 3840 | 60 | 'cud8'
UHD10 | HEVC | Main10 MainTier 10-bit | 5.1 | BT.709, BT.2020 | BT.709 OETF, BT.2020 OETF | 2160 | 3840 | 60 | 'cud1'
HDR10 | HEVC | Main10 MainTier 10-bit | 5.1 | BT-2020 | ST-2084 EOTF | 2160 | 3840 | 60 | 'chr1'

## Slide 8: Audio and Subtitle Track Profiles
Media Profile | Codec and Profile | Number of channels | Max Sampling Rate | File Brand
AAC Core | AAC-LC, HE-AAC or HE-AAC v2 | Mono or Stereo | 48 kHz | 'caac'
Media Profile | Format | Notes | File Brand
WebVTT | WebVTT, Version 1.0 | —pending normative reference https://w3c.github.io/webvtt/ | 'cwvt'
TTML IMSC Text | TTML W3C IMSC Version 1 | Text Profile http://www.w3.org/TR/ttml-imsc1/#text-profile | 'cttt'
TTML IMSC1 Image | TTML W3C IMSC Version 1 | Image Profile http://www.w3.org/TR/ttml-imsc1/#image-profile | ‘ctti’
CEA | CEA-608 and CEA-708 | Caption data is embedded in SEI messages in video track; multiple closed caption streams may be present | 'ccea'
More profiles are developed in Amendments as well as in external specifications