## Slide 1: [AMD_PRO-MED] Inband Session Repair for MBS and MBMS
Source: Qualcomm Incorporated
Agenda Item: 8.5
3GPP TSG SA WG4 #133-e online,, 18-25 July, 2025
S4-251245

## Slide 2: Background
address Gaps #2, #3, #4, and #5 in clause 5.9.5 by the candidate solution in clause 5.9.6 in TS 26.517 and possibly in TS 26.346:
On gap #2 identified in clause 5.9.5 of TR 26.802, both of the following signalling options are expected to be supported:
Using FDT parameters to signal the time when repairs can be requested using the Expires attribute).
Using LCT header information to signal the time when repairs can be requested using the B-Flag.
On Gap #3 identified in clause 5.9.5 of TR 26.802, the following signalling options exist in the FLUTE File Delivery Table (FDT):
Defining a new FDT extensions parameter to signal the availability time when the object needs to be released.
On gap #4 identified in clause 5.9.5 of TR 26.802, the execution of MBS object delivery and in-session unicast repair can run in parallel in the MBS Client. However, this should be validated if there are cases this is not the case and whether these cases need to be explicitly stated, for example reduced capability (RedCaP) UEs.
On gap #5 identified in clause 5.9.5 of TR 26.802, time synchronization can reuse functionalities defined in TS 26.346, but tighter synchronization that 1 second. This work is aligned with the findings and work in clause 5.11.3.6 of TR 26.802.
Support other relevant aspects resulting from stage-2.
This document primarily addresses Gap#2, but in much more detailed implementation
In-session unicast repair for MBS Object Distribution as introduced in clause 5.9 of TR 26.802

## Slide 3: In-Session Unicast Repair for MBMS and MBS
Both, MBMS (TS26.346) and MBS (TS26.517) define unicast post session repair, but the approach taken in MBMS was considered only partially suitable for MBS, and a better documentation was done.
Also note that Object Delivery in MBS (TS 26.517) relies on MBMS download delivery (TS 26.346)
As in-session repair is a new feature for both systems, two CRs are submitted
S4-251232 | CR | [AMD_PRO-MED] In-session Unicast Repair for MBMS Object Distribution | Qualcomm Incorporated
S4-251233 | CR | [AMD_PRO-MED] In-session Unicast Repair for MBS Object Distribution | Qualcomm Incorporated

## Slide 4: Definitions across different TSs
Defines a common set of procedures and protocols that can be mapped to both systems. This is proposed to be addressed in TS 26.517, clause 6.2.4.3
Define necessary FLUTE FDT extensions to support the delivery for individual objects in TS 26.346, clause 7.2.10.1 and 7.2.10.2 that are common to MBS and MBMS
Define abstract parameters that configure in-session repair and are configured through user service announcement in TS 26.517, 6.2.4.3.2.
Define a mapping of the parameters to MBMS TS 26.346 User Service Description, in particular to the Associated Delivery procedure fragment, in clause 9.5.1 of TS 26.346
Define a mapping of the parameters to MBS TS 26.517 User Service Announcement, in particular to Distribution Session parameters in clause 5.2.6 and object repair parameters in clause 5.2.8.
Define a mapping of the procedures to MBS (see clause 10.3 of TS 26.517) and MBMS (see clause 9.3.10 of TS 26.346)

## Slide 5: Core description is in TR 26.517, clause 6.2.4.3
For every object delivered in a FLUTE session, the object-delivery client needs to decide if, when, from where for unicast repair is initiated, and which data is requested.
The object-delivery client is supported by information provided in the service announcement and or the File element of the FDT, associated to this object, to make these decisions.
Decision if unicast is initiated:
  Determine whether the object delivery will be successful, see criteria in 6.2.4.3.4. If not, initiate unicast repair unless this happens to frequent.
  A service provider may restrict the number of unicast request attempts but not allowing more than repairMaxAttempts in a sliding window of 100 requests. (Note 100 is chosen, but could be a parameter). If the object delivery client has exhausted attempts, it shall not use unicast requests (see 6.2.4.3.3, step 2).
If decision is taken to, the question is when the request can be issued (see clause 6.2.4.3.2):
  An explicit signal File@RepairStart may be provided in the FDT
  The time may depend on user service announcement parameters, after the reception of the first packet or FDT@Expiry

## Slide 6: Core description is in TR 26.517, clause 6.2.4.3
Decision from where
  The repair location is selected based on the parameters in the User Service announcement repair locations
  The client randomly selects those
  Details see clause 6.2.4.3.3, step 3
  Note that for MBMS, the usage of Alternate-Location-1 is not yet supported for selecting locations, but could be considered. It would overwrite any information in the User Service Description.
Decision what to request
  The client may request byte ranges only
  The client may request entire object
  Decision is up to the client based on operation
  If the latter, the object request can directly be served to the application.
  (see 6.2.4.3.3, 4-6)
How to request is provided in details in clause 6.2.4.3.5
Continuation

## Slide 7: Potential updates beyond CRs
Create schema for FDT, MBMS User Service Description and MBS User Service Announcement
Potential updates to TR 26.802 to add some more details
Potential updates to TS 26.502 for stage-2 extensions (Parameters in User Service Announcement)
Potential updates to CT specs.