## Slide 1
3GPP SA4 EMM-EFEC Work Item
January 21, 2012

## Slide 2: Contenders: Summary

## Slide 3: Summary: EFEC for eMBMS QC position
Based on discussions and actions at SA4#71 RS+LDPC and RFC 6330 may provide improvements over the existing MBMS FEC.
Of these two codes, QC strongly believes that RFC 6330 is superior
  Licensing terms were made public to the IETF in 2011
    http://datatracker.ietf.org/ipr/1553/
    No impact to existing licensees, whereas the licensing status is less clear for the proposed alternatives
    QC has also made a licensing statement applicable to the RS+LDPC candidate: http://datatracker.ietf.org/ipr/1743/
    There is no licensing advantage in any of the other alternatives
  Open source and independent implementations of RFC 6330 exist
    http://www.mathworks.com/matlabcentral/fileexchange/39218-6330-fec-code
    There is no “open source” advantage in any of the other alternatives
  Performance of RFC 6330 is superior
    Only proposal that supports all features of existing code
    Only code that consistently improves over the existing FEC
    Download: best in memory usage & overhead for all cases; best for worst/relevant-case decode speed
    Streaming: least computational resources & and lowest overhead across all candidates

## Slide 4: Relevant Technical Criteria
Main Performance Metrics
  Transmission and Reception Overhead
    Rigorous simulation framework with LTE test cases => see TR26.947
    Overhead performance for the codes are non-distinguishable when using comparable source block sizes (some codes may require multiple symbols per packet for small source blocks, e.g. RFC5053 & LDPC)
  Required Decoding Memory and Decoding Speed
    Rigorous evaluation framework based on Galaxy S2 => see TR26.947
    Verification procedures done, results documented in S4-121460
    Selected relevant results on the next slide
  Comprehensive results, but some proponents customized their code parameters for each individual test case to achieve competitive results
Additional Relevant Technical Criteria
  Robustness and simplicity for many deployment scenarios
  Operational and deployment complexity
  Amount of necessary testing for interop and deployment
  Flexibility and versatility in the deployment
  Applicability to future use cases

## Slide 5: High level summary of RFC 6330
RFC 6330 transcends numbers
  RFC 6330 code should be appreciated for the simplicity, efficiency and versatility provided to applications & systems
  These aspects cannot be melted down to statistics
Simplicity and efficiency
  Code is completely defined by the specification – no undetermined parameters to be set – and it is a single code
  Predictable and excellent overhead in all conditions
  Predictable and excellent decoding speed in all conditions – even with reception of minimal possible to decode
  Defines a completely specified decoder performance along with example decoder. This enables to define a UE conformance point.
Versatility
  Support up to 56,403 source symbols per source block
  Strongly systematic – does not matter what mix of source and repair is received
  Fountain code – can generate any number of encoding symbols for a source block – on-the-fly
  Supports sub-blocking – allows decoding source block in small chunks to minimize decode memory and to enable Just-in-Time recovery

## Slide 6: Summary: RS+LDPC Technical Issues
RS+LDPC introduces technical problems into eMBMS, they are not problems with the existing RFC 5053 code.
Not a single code solution
  RS (RFC5510) and LDPC (RFC5170) are different codes
LDPC requires setting a variety of mandatory code parameters at the sender that fully specify code construction
  Code construction parameter settings are crucial for obtaining good performance (overhead, decode speed, flexibility)
  No guidelines provided for setting these code construction parameters for file delivery
  Code construction and number of encoding symbols to generate must be determined before transmission
LDPC not a strongly systematic code
LDPC not a fountain code
LDPC does not support sub-blocking
RFC 5170 does not provide any specification of a compliant decoder. There is no UE compliance possible based on RFC 5170.
LDPC is a significant step backwards from RFC 5053

## Slide 7: MBMS features not/poorly supported by RS+LDPC
MBMS-based repair service
  Whereas 5053 and 6330 are fountain codes that enable excellent support for an MBMS-based repair service, required setting of the code rate for RS+LDPC provides poor support
Low Memory Decoding
  Whereas the 5053 and 6330 sub-blocking enables low overhead with low memory decoding, the lack of sub-blocking in RS+LDPC requires higher overhead with low memory decoding
Low Latency Streaming
  Whereas the strongly systematic property of 5053 and 6330 enables sending source and then repair, RS+LDPC needs interleaving for best overhead => increased end-2-end streaming latency
HTTP-Based Repair Service
  Whereas the strongly systematic property of 5053 and 6330 enables broadcasting only repair to enable an efficient HTTP-based repair service, RS+LDPC can not broadcast repair only
Just-in-Time Recovery
  Whereas the 5053 and 6330 sub-blocking enables excellent Just-in-Time recovery, the lack of sub-blocking in RS+LDPC provides poor support for Just-in-Time recovery
Single Symbol per Packet
  Whereas the excellent overhead of 6330 enables sending a single symbol per packet, 5053 and LDPC require multiple symbols => less efficiency, more decoding complexity, less flexibility

## Slide 8: Code construction and testing issues
RFC 6330
  Code is completely specified – no code construction parameters
  477 code constructions total – one for each K’ value supported
RFC 5053
  Code is completely specified – no code construction parameters
  8,192 code constructions total – one for each K value supported
LDPC
  Code is not completely specified – multiple parameters must be set by application
  Number of code constructions is unknown, because code is underspecified
  Guesstimate – 32,000,000+ code constructions?
  No specification of how parameters are to be set for each use case
  No performance and overhead testing for each setting of parameters
    Testing LDPC to the same level as RFC 6330 has been tested, running 1 billion tests per day would take around 10,000 years

## Slide 9: Summary: Comparison to RFC5053
Criteria | RS+LDPC | Supercharged | 6330 code
Bandwidth efficiency for download delivery | = | + | +
Bandwidth efficiency for streaming delivery | =+ | + | +
Decoding speed for download delivery | -= | -- | =
Decoding speed for streaming delivery | + | -- | ++
memory usage for download delivery | - | -- | =
memory usage for streaming delivery | = | = | =
standardization status download | = | - | +
standardization status streaming | =(?) | - | =
single code | - | - | =
advanced use cases, flexibility | - | +- | +
IPR Licensing conditions | = (see IETF) | ??? | = (see IETF)
Open source reference SW | + (available) | - (not available) | + (available)
Test and Code Construction (8192) | -- (32,000,000+) | = (???) | + (477)
Legend: (+)+ (much) better than RFC5053, = equal, =+ once in a while better |  |  | 

## Slide 10: Detailed Feature Discussion

## Slide 11: Code construction and testing issue

## Slide 12: Raptor codes construction discussion
RFC 6330
  Code is completely specified – no code construction parameters
  477 code constructions total – one for each K’ value supported
  Number of code constructions minimized by design to allow extensive testing*
    All constructions have been thoroughly tested during design and verified post design
    Hundreds of millions of tests per construction
    Testing used hundreds of computers running for months
RFC 5053
  Code is completely specified – no code construction parameters
  8,192 code constructions total – one for each K value supported
  Number of code constructions allowed reasonably thorough testing*
For example, Appendix B of [1] describes the results of 40 billion tests for RaptorQ RFC 6330 and 33 billion tests for Raptor RFC 5053 that were run long after the designs were finalized.
[1] Amin Shokrollahi and Michael Luby (2011) "Raptor Codes”, Foundations and Trends® in Communications and Information Theory: Vol. 6: No 3-4, pp 213-322

## Slide 13: LDPC code construction discussion
LDPC code not completely specified – code construction parameters must be provided before encoding
  N1 = N1m3 + 3 sets source symbol degree
    Smaller N1 provides better decode speed, larger N1 provides reduced overhead
  B and max_n in conjunction with K sets code rate
    Smaller code rate provides more encoding symbols, larger code rate provides better decode speed and reduced overhead
  PRNG seed – determines properties of code construction graph
No guidelines provided for setting code construction parameters
  No guidance provided for file delivery or streaming in any specifications
  Device evaluations don’t provide these parameters
    N1 sometimes provided – but not in a consistent way
      Set to 7, 9, 10 for code overhead evaluations, set to 5 and 7 for file delivery decode speed performance – settings not provided for streaming results
    Settings of B and max_n not provided in any of the testing – code rate unknown
    PRNG seed is not provided in any of the testing
LDPC is underspecified – requires significant additional specification of how parameters are to be set for each use case

## Slide 14: Number of LDPC code constructions
Number of code constructions is unknown, because code is underspecified
Guesstimate – 32,000,000+ code constructions?
  Different construction for each value of K
    Evaluations used K up to 8,000
    RFC 5170 says supports K up to 500,000
    Guesstimate support up to K = 20,000?
  Different construction for each different code rate (max_n, B parameters)
    Evaluations did not specify rate of code used in results
    RFC 5170 does not specify rates of code to be used
    Guesstimate 40 different code rates? (5% increments up to 200% overhead)
  Different construction for each different source symbol degree (N1m3 parameter)
    Evaluations seem to have used 4 different settings (N1 = 5, 7, 9, 10, where N1 = N1m3 +3)
    RFC 5170 provides up to 8 different settings
    Guesstimate 4 different settings?
  Different construction for each PRNG seed value
    Evaluations did not specify how many seed values were used or how the seed values was chosen
    RFC 5170 provides up to 4,000,000,000 different seeds
    Guesstimate 10 different seeds used?
Testing LDPC to the same level as for RFC 6330, running 1 billion tests per day would take around 10,000 years
LDPC is undertested – requires significant performance and overhead testing for each setting of parameters

## Slide 15: LDPC code construction issues examples
Quotes from the openfec.org site announcing a new major release:
  “Solved a bug in the LDPC-Staircase matrix creation algorithm when N1 is even. This bug makes the codec non RFC5170 compliant (!). However there was no impact with odd N1 values. This means that with an even N1, an application using version >= 1.3 will not interoperate with an application using version <= 1.2”
    The openfec implementation was not compliant with RFC 5170 for years!
  “With LDPC-Staircase, when N1 is even, the latest repair symbol is often NULL. This property is now exploited at the decoder to generate it automatically and pass it to the decoder. When this property applies, there is no need to send this repair symbol. A new OF_CTRL_LDPC_STAIRCASE_IS_LAST_SYMBOL_NULL is added to check this property within an application, if desired (e.g. this optimization is added to eperftool).”
    LDPC as specified in RFC 5170 has design issues that are only being discovered years after the specification was complete – in this case when N1 is even the last repair symbol can never be used to help recover the source block – independent of the loss pattern of other symbols.

## Slide 16: MBMS-based repair service

## Slide 17: eMBMS-based repair service issue
RS+LDPC has poor support for eMBMS-based repair service (existing MBMS feature)
  There is a different code construction for each different code rate
  Once code rate is set – can’t generate more encoding symbols
  Poor code rate compromises
    Low code rate – more generated encoding symbols but poor overhead and decode speed performance
    High code rate – better overhead & decode speed performance but fewer generated encoding symbols
  Option A: choose code rate to support only original eMBMS session
    Set code rate high to generate encoding symbols sent in original eMBMS session
    Provides best overhead & decode speed performance
    No additional encoding symbols available for repair eMBMS session
  Option B: choose code rate to support both original and repair eMBMS session
    Set code rate low to generate encoding symbols sent in both sessions
    Additional encoding symbols available for repair eMBMS session
    Provides deteriorated overhead & decode speed performance
RFC 5053 and RFC 6330 provide excellent support for eMBMS-based repair service
  RFC 5053 and RFC 6330 are fountain codes
  Same code construction independent of how many encoding symbols generated
  Encoding symbols can be generated on-the-fly
  Additional encoding symbols are always available for repair eMBMS session
  No compromises
    Provide same excellent overhead & decode speed performance independent of repair eMBMS session

## Slide 18: eMBMS-based repair service
Time
Original eMBMS session
Transmit source + repair
eMBMS-based repair session
Transmit different
repair symbols
Feedback from UEs
triggers eMBMS-based repair session

## Slide 19: eMBMS-based repair service example
Overall configuration
  128 MB file partitioned into 13 source blocks
  Original eMBMS session: transmit Nt5 of encoding symbols, where Nt5 is configured for 5% loss
    Option of repair eMBMS session allows more conservative settings for original eMBMS session to save network bandwidth
RS+LDPC Option A
  Set code rate to generate Nt5 encoding symbols for original eMBMS session
  Transmit randomly all Nt5 encoding symbols in original eMBMS session
  Cannot support repair eMBMS session – no additional encoding symbols to transmit
RS+LDPC Option B
  Set code rate to generate Nt20 encoding symbols, where Nt20 is configured for 20% loss
  Transmit in the original eMBMS session a random Nt5 of the Nt20 encoding symbols
  Supports repair eMBMS session – up to Nt20 – Nt5 = 15% additional encoding symbols available
  Decoding speed and overhead from original eMBMS session are as if configured for 20% loss
RFC 6330
  Generate and transmit symbols for original eMBMS session
  Supports repair eMBMS session – as many encoding symbols as needed can be generated
  Decoding speed and overhead are independent of whether or not there is a repair eMBMS session

## Slide 20: Low Memory Decoding

## Slide 21: Low memory decoding issue
RS+LDPC provides poor support for low-memory decoding (existing eMBMS feature)
  Only provides support for decoding entire source block in RAM
    Decoding memory is proportional to source block size
  Poor source block compromises
    Use large source block size – best network efficiency but requires large decoding memory for all UEs
    Use small source block size – small decoding memory but has poor network efficiency
RFC 5053 and RFC 6330 provide excellent support for low-memory decoding
  Provides support for sub-blocking – decode source block one sub-block at a time in RAM
    Decoding memory can be an order of magnitude smaller than the source block size
    Enables Just-in-Time recovery (explained later)
  No compromises
    Use large source blocks – best network efficiency
    Decode one sub-block at a time – fast decoding using small memory

## Slide 22: Sub-block sending
…
…
…
…
…
Form source symbols
Source packets
Packet 1 for source block 1
Source block 1
Sub-blocks
Source blocks
Content file
Source block 2
…
…
…
…
…
Source packets
Packet 1 for source block 2

## Slide 23: Sub-block receiving
UE with less available memory
Decode one sub-block at a time
UE with more available memory
Decode all sub-blocks of source block at a time
RAM to decode one
sub-block
RAM to decode all
sub-blocks of a source block

## Slide 24: Low memory decoding example
Overall configuration
  128 MB file partitioned into 13 source blocks
  20% loss
RS+LDPC
  Decode one source block at a time
RFC 6330
  Send using 41 sub-blocks per source block
    each sub-block approximately 256 KB
  Decode one sub-block at a time

## Slide 25: Low Latency Streaming

## Slide 26: Low latency live issue
RS+LDPC provides poor support for low-latency live (existing eMBMS feature)
  Not strongly systematic code
    Reception of random mix of generated source and repair required for reasonable and consistent overhead and decode speed performance
  Sender must have entire source block and generate all repair symbols before sending random mix of source and repair symbols for source block
    For low latency live streaming – doubles minimal end-to-end latency of solution where source symbols are sent prior to repair symbols
RFC 5053 and RFC 6330 provide excellent support for low-latency live
  Strongly systematic code
    Received mix of source and repair not important for overhead and decode speed performance
  Sender can start sending source symbols of source block before entire source block is available
    For low latency live streaming – allows minimal end-to-end latency solution where source symbols are sent prior to repair symbols

## Slide 27: Sending strategy for low latency live
Time
RaptorQ sending strategy
Strongly systematic
Send source and then repair
Provides minimum latency sending
RaptorQ sending delay
LDPC sending strategy
Not strongly systematic
Source + repair randomly interleaved
Doubles the overall latency
LDPC sending delay

## Slide 28: HTTP-Based Repair Service

## Slide 29: HTTP-based repair service issue
RS+LDPC provides poor support for HTTP-based repair service (future eMBMS feature)
  Not a strongly systematic code
    Send random mix of source and repair in original eMBMS session
    Each UE experiences a different loss pattern and thus requests a different set of source symbols
    Source symbols requested by each UE differs based on pattern of source symbol loss
      Non-sequential random source symbols requested
    Low cache hit ratio to HTTP web servers due to differing source symbol request pattern from each UE
RFC 5053 and RFC 6330 provide excellent support for HTTP-based repair service
  RFC 5053 and RFC 6330 are strongly systematic
    Send repair symbols only in eMBMS session
      No source symbols sent in eMBMS session
      Recovery is just as reliable from reception of only repair symbols as any other mix
    HTTP request is for appropriate length prefix of source block or sub-block
      UE receives no source symbols from eMBMS session – can always be usefully combined with repair to decode
    High cache hit ratio to HTTP web servers due to same HTTP request pattern from all UEs

## Slide 30: LDPC HTTP-based repair service
LDPC random mix of encoding
Transmit over eMBMS
Multiple HTTP
requests and responses
Requests dependent on loss pattern
Low caching efficiency
Many packet-sized byte-ranges
LDPC decoding
FLUTE packaging

## Slide 31: RaptorQ HTTP-based repair service
RaptorQ repair symbols
Transmit over eMBMS
HTTP request and response
Prefix request independent of loss pattern
High caching efficiency
Single consecutive byte-range
RaptorQ decoding
FLUTE packaging

## Slide 32: HTTP-based repair service example
Overall configuration
  128 MB file partitioned into 13 source blocks
  20% loss
RFC 6330
  Send only repair symbols in original eMBMS session
  Send using 41 sub-blocks per source block
    each source block 256 KB
  Decode one sub-block at a time

## Slide 33: Just-in-Time Recovery

## Slide 34: Just-in-Time recovery
Data received during eMBMS reception is stored on the SD card
  Original multimedia data is never stored on the SD card
  SD card stores one copy of file – not two!
Multimedia content available immediately after reception
  Avoids FEC decode post-processing of file after reception
Just-in-Time recovery
  Based on user actions – player requests data to playback multimedia content
  Relevant data read from SD card, FEC decoded, provided directly to player
  Trick play response time
    Playback starts after one sub-block of data read from SD card and FEC decoded
    Size of sub-block and decode speed determines the response time

## Slide 35: Transmission
Minimize network resources – interleaved transmission of source blocks
Minimize UE resources – terminate reception as soon as decoding is possible
Multimedia
content
Block 1
Block 2
Block 3
Block 100
…
Outages
Interleaved
broadcast
…
…
…
…
…
…
Received
…
…
…
…
RaptorQ encode and interleaved transmission

## Slide 36: Just-in-Time recovery
Just-in-Time recovery avoids costly post-processing
Portions of multimedia never played back are never processed
Storage usage is minimized – avoids double the writes to SD card
Receiver
Broadcast
network
Write encoded interleaved
data as received
Read sub-block encoded data to RaptorQ decode and playback requested media in real-time
SD card
RAM
Player
Playback of requested media
Request playback of media

## Slide 37: Just-in-Time recovery advantages
Good user experience – media available immediately after reception
Minimizes UE CPU, I/O, and storage resources

## Slide 38: Just-in-Time decoding example
Overall configuration
  128 MB file partitioned into 10 MB source blocks – 13 total
  20% loss
RS+LDPC (no support for JIT)
  Post-processing: Decode one source block at a time and write back to SD card
RFC 6330 (support for JIT)
  Send using 41 sub-blocks per source block
    each source block 256 KB
  No post-processing
  Playback : read from SD card, FEC decode, provide to the application the relevant sub-blocks

## Slide 39: Just-in-Time recovery demo
Demonstrates
  Just-in-Time recovery (importance of sub-blocking to support this)
  Only repair symbols sent in the original eMBMS session
    Provides ability to efficient combine with HTTP-based repair service
    Provides ability to provide hybrid HTTP/eMBMS services
Demo parameters
  Elephant’s Dream – 91.3 MB file
  Partitioned into 10 source blocks (each of size 9.13 MB)
    Provides reasonable network efficiency
  Each source block is partitioned into 41 sub-blocks (each of size 223 KB)
    Read encoded data from SD card and decode sub-block when requested by app
  Original eMBMS session
    Transmit repair symbols only
    20% packet loss according to Markov model applied before reception

## Slide 40: Single Symbol per Packet

## Slide 41: Multiple symbols per packet discussion
Always one symbol per packet for RFC 6330
  Independent of source block size
Multiple symbols per packet for RFC 5053
  Number of symbols per packet depends on the source block size
  Causes multiple issues with current and future use cases
Multiple codes and multiple symbols per packet for RS+LDPC
  Which code to use depends on source block size
  Number of symbols per packet depends on the source block size
  Causes multiple issues with current and future use cases

## Slide 42: DASH/FLUTE streaming
  Multiple symbol packet derivation
    Set desired packet size
    Varying number of symbols per packet depending on file size
    Packet size <= desired size
  RFC 6330 packet derivation
    Set actual packet size
    One symbol per packet independent of file size
    Packet size = actual size

## Slide 43: DASH/FLUTE streaming – multiple symbols per packet
  FEC with multiple symbols per packet
    Segment 1 = 200 KB
      6 symbols per packet
      Symbol size = 212 bytes
      Actual packet size = 1272 bytes
    Segment 2 = 150 KB
      9 symbols per packet
      Symbol size = 140 bytes
      Actual packet size = 1260 bytes
    Segment 3 = 175 KB
      8 symbols per packet
      Symbol size = 160 bytes
      Actual packet size = 1280 bytes
    Segment 4 = 250 KB
      5 symbols per packet
      Symbol size = 256 bytes
      Actual packet size = 1280 bytes
  RaptorQ RFC 6330
    Actual packet size = 1288 bytes
    Symbol size = 1288 bytes for all segments
    Desired packet payload size for symbols = 1288 bytes
    800 Kbps average stream rate
    2 seconds segment duration
Different symbol size for each segment
is inefficient – reset and reinitialization
of decoder required
Decoding is more complex with smaller symbols
Actual packet size is
less than desired packet size
– loss in network efficiency
if filled with padding bytes

## Slide 44: Thanks!