## Slide 1
Tdoc S4-141060
SDP Parameters of EVS &
Session Negotiation Procedures
3GPP SA4#80bis
August 30-31, 2014, Helsinki, Finland
Agenda Item: 6
Source: Samsung Electronics Co., Ltd.
Document for: Discussion
Contact: Kyunghun Jung
E-mail: kyunghun.jung@samsung.com

## Slide 2
Header Control
CMR Control
Channel Control
AMR-WB IO Codec Mode Negotiation
Annex
Changing Network Environments
Representing Bit-Rates & Bandwidths
Bit-Rate Negotiation
Bandwidth Negotiation
Bi-directional Negotiation
DTX Control
SDP Offer/Answer Example
Content

## Slide 3
Header Control
Parameter | Location | Definition
header | TS 26.445 Definition | Specifies the type of EVS RTP payload header to be used in the session. header has a value from the set: 0 and 1. 0 and 1 represent header-less format and header-full format respectively. If not present, all formats are supported. When header-full format is used, one byte header-full format and two bytes header-full format can be used interchangeably in the session.
 | TS 26.114 Handling | When header is not offered for a payload type, the answerer may include header for the payload type in the SDP answer. When header is offered for a payload type which is accepted, the answerer shall not modify or remove header for the payload type in the SDP answer.
TS 26.114 Status | 
UE Support | Use
Mandatory | Optional

## Slide 4
Parameter | Location | Definition
cmr-off | TS 26.445 Definition | Indicates that Codec Mode Request (CMR) of RTP payload header is not used in the session.
 | TS 26.114 Handling | When cmr-off is not offered for a payload type, the answerer may include cmr-off for the payload type in the SDP answer. When cmr-off is offered for a payload type which is accepted, the answerer shall not remove cmr-off for the payload type in the SDP answer. If cmr-off is negotiated, the CMR bits for EVS primary mode, Primary mode rate and channel-aware configuration, in the received header-full payload formats shall be ignored.
TS 26.114 Status | 
UE Support | Use
Mandatory | Optional
CMR Control

## Slide 5
Channel Control
Parameter | Location | Definition
channel-send | TS 26.445 Definition | Specifies the number and relationship of audio channels to be used in the session for the send direction. channel-send has a value from the set: 0, 1, and 2. 0, 1, and 2 represent mono, dual-mono, and stereo respectively. If not present, mono is supported.
 | TS 26.114 Handling | When channel-send is not offered for a payload type, the answerer shall not include channel-recv for the payload type in the SDP answer. If offered, the value of channel-send shall not be modified when the answerer includes channel-recv for the payload type in the SDP answer. If a payload type including channel-send=1 or 2 is offered, at least a payload type not including channel-send or including channel-send=0 should also be offered.
channel-recv | TS 26.445 Definition | Specifies the number and relationship of audio channels to be used in the session for the receive direction. channel-recv has a value from the set: 0, 1, and 2. 0, 1, and 2 represent mono, dual-mono, and stereo respectively. If not present, mono is supported.
 | TS 26.114 Handling | When channel-recv is not offered for a payload type, the answerer shall not include channel-send for the payload type in the SDP answer. If offered, the value of channel-recv shall not be modified when the answerer includes channel-send for the payload type in the SDP answer. If a payload type including channel-recv=1 or 2 is offered, at least a payload type not including channel-recv or including channel-recv=0 should also be offered.
TS 26.114 Status | 
UE Support | Use
Mandatory | Optional

## Slide 6
AMR-WB IO Codec Mode Negotiation
Parameter | Location | Definition
mode-set | TS 26.445 Definition | Restricts the active codec mode set to a subset of all modes when EVS operates in AMR-WB IO mode, for example, to be able to support transport channels such as GSM or UMTS networks. Possible value is a comma-separated list of modes from the set: 0, ..., 8 (see Table 1a [XXX]). If mode-set is specified, it must be abided, and frames encoded with AMR-WB IO outside of the subset must not be sent in any RTP payload or used in codec mode request signal. [XXX] 3GPP TS 26.201 "AMR Wideband speech codec; Frame Structure", version 11.0.0 (2012-9), 3rd Generation Partnership Project (3GPP).
 | TS 26.114 Handling | 
TS 26.114 Status | 
UE Support | Use
Mandatory | Optional

## Slide 7
Annex A: Changing Network Environments
  Current procedures for session negotiation, like no mode-set in SDP offer, are defined in Rel-7, with only MTSI client in terminal and MGW in mind
  The lowest-end 3GPP access technology in TS 26.114 V12.6.0, EGPRS, can support the maximum bit-rates of AMR and AMR-WB in good channels
  As E-UTRAN and EPC were introduced to MTSI, SGSN and GGSN were replaced with a more generic term, PS Domain, from Rel-10
  In Rel-12, MTSI client in terminal using fixed access was introduced, which may require higher but fixed bit-rates and bandwidths, e.g., 64 kbps at WB
  In Rel-12, EVS was introduced, whose highest bit-rate is twice the transport capability of EDGE (maximum 61.85 kbps at MCS-9, no channel coding)
  EVS supports dual-mono (or stereo), whose parameters reflecting local situations need to be taken into account in session negotiation (SDP offer)
  Support of multi-channel necessitates asymmetric bit-rate/bandwidth negotiation, e.g., when only a UE is connected to a stereo headset

## Slide 8
Annex B1: Representing Bit-Rates & Bandwidths
Codec Type | Source Bandwidth (Hz) | Sampling Rate (samples/s) | Bit-rate (kbps)
Narrow Band (NB) | 20 ~ 4,000 | 8,000 (nb) | 5.9, 7.2, 8, 9.6, 13.2
Wide Band (WB) | 20 ~ 8,000 | 16,000 (wb) | 5.9, 7.2, 8, 9.6, 13.2, 16.4, 24.4, 32, 48, 64, 96, 128, AMR-WB Interoperable Mode (6.6~23.85)
Super Wide Band (SWB) | 20 ~ 16,000 (14,000*) | 32,000 (swb) | 13.2*, 16.4, 24.4, 32, 48, 64, 96, 128
Full Band (FB) | 20 ~ 20,000 | 48,000 (fb) | 16.4, 24.4, 32, 48, 64, 96, 128
  Each codec mode of EVS AMR-WB IO mode can be represented with 0, …, 8 as in the legacy AMR-WB
  To avoid confusion with EVS AMR-WB IO mode, and to save space in SDP, bit-rate in kbps can be used to represent the bit-rates of EVS Primary mode
  Representing bit-rate in kbps also increases readability, making (human) inspection of SDP easier
  With a large bit-rate range of 5.9-128 kbps, service plan may partition the range into smaller ranges for each payload type
  Bit-rates can be compactly represented as br1 when a bit-rate is used, and br1-br2 when equal to or more than two consecutive bit-rates are used
  When representing equal to or more than three consecutive bit-rates, br1-br2 will be more economical than br1, …, br2 or other expressions
  Multiple ranges of bit-rates can be offered with multiple payload types, each of which can be defined for radio, fixed, multi-channel, …
  With a large bandwidth range of nb-fb, the range may be partitioned into smaller ranges that match the bit-rates of each payload type
  Bandwidths can be compactly represented as bw1 when a bandwidth is used, and bw1-bw2 when equal to or more than two bandwidths are used
  When representing more than two bandwidths, bw1-bw2 will be more economical than bw1, …, bw2 or other expressions
  Bit-rates and bandwidths of EVS Primary mode need to be represented in a compact and consistent fashion, for send and receive directions separately

## Slide 9
Annex B2: Bit-Rate Negotiation
Parameter | Location | Description
br-send | TS 26.445 Definition | Specifies the range of bit-rate, in kilobits per second (excluding RTP, UDP, and IP overhead), to be used in the session for the send direction. Possible value is a hyphen-separated pair of two bit-rates, br1-br2, where br1 is smaller than br2. br1 and br2 have a value from the set: 5.9, 7.2, 8, 9.6, 13.2, 16.4, 24.4, 32, 48, 64, 96, and 128. 5.9 represents the bit-rate of source controlled variable bit-rate (SC-VBR) coding, and 7.2, …, 128 represent the bit-rates of constant bit-rate source coding. If a single bit-rate is used in the session, br-send is set to the bit-rate. If not present, all bit-rates are supported.
 | TS 26.114 Handling | When br-send is not offered for a payload type, the answerer may include br-recv for the payload type in the SDP answer. If br-send is offered for a payload type which is accepted, the answerer shall include br-recv in the SDP answer, and the br-recv shall be a subset of br-send for the payload type in the SDP offer.
br-recv | TS 26.445 Definition | Specifies the range of bit-rate, in kilobits per second (excluding RTP, UDP, and IP overhead), to be used in the session for the receive direction. Possible value is a hyphen-separated pair of two bit-rates, br1-br2, where br1 is smaller than br2. br1 and br2 have a value from the set: 5.9, 7.2, 8, 9.6, 13.2, 16.4, 24.4, 32, 48, 64, 96, and 128. 5.9 represents the bit-rate of source controlled variable bit-rate (SC-VBR) coding, and 7.2, …, 128 represent the bit-rates of constant bit-rate source coding. If a single bit-rate is used in the session, br-recv is set to the bit-rate. If not present, all bit-rates are supported.
 | TS 26.114 Handling | When br-recv is not offered for a payload type, the answerer may include br-send for the payload type in the SDP answer. If br-recv is offered for a payload type which is accepted, the answerer shall include br-send in the SDP answer, and the br-send shall be a subset of br-recv for the payload type in the SDP offer.
TS 26.114 Status | 
UE Support | Use
Mandatory | Optional

## Slide 10
Annex B3: Bandwidth Negotiation
Parameter | Location | Definition
bw-send | TS 26.445 Definition | Specifies the bandwidth to be used in the session for the send direction. bw-send has a value from the set: nb, wb, swb, fb, nb-wb, nb-swb, and nb-fb. nb, wb, swb, and fb represent narrowband, wideband, super wideband, and fullband respectively, and nb-wb, nb-swb, and nb-fb represent all bandwidths from narrowband to wideband, super wideband, and fullband respectively. If not present, all bandwidths are supported.
 | TS 26.114 Handling | When bw-send is not offered for a payload type, the answerer may include bw-recv for the payload type in the SDP answer. If bw-send is offered for a payload type which is accepted, the answerer shall include bw-recv in the SDP answer, and the bw-recv shall be a subset of bw-send for the payload type in the SDP offer.
bw-recv | TS 26.445 Definition | Specifies the bandwidth to be used in the session for the receive direction. bw-recv has a value from the set: nb, wb, swb, fb, nb-wb, nb-swb, and nb-fb. nb, wb, swb, and fb represent narrowband, wideband, super wideband, and fullband respectively, and nb-wb, nb-swb, and nb-fb represent all bandwidths from narrowband to wideband, super wideband, and fullband respectively. If not present, all bandwidths are supported.
 | TS 26.114 Handling | When bw-recv is not offered for a payload type, the answerer may include bw-send for the payload type in the SDP answer. If bw-recv is offered for a payload type which is accepted, the answerer shall include bw-send in the SDP answer, and the bw-send shall be a subset of bw-recv for the payload type in the SDP offer.
TS 26.114 Status | 
UE Support | Use
Mandatory | Optional

## Slide 11
Annex B4: Bi-directional Negotiation
Parameter | Location | Definition
br | TS 26.445 Definition | Specifies the range of bit-rate, in kilobits per second (excluding RTP, UDP, and IP overhead), to be used in the session for the send and the receive directions. Possible value is a hyphen-separated pair of two bit-rates, br1-br2, where br1 is smaller than br2. br1 and br2 have a value from the set: 5.9, 7.2, 8, 9.6, 13.2, 16.4, 24.4, 32, 48, 64, 96, and 128. 5.9 represents the bit-rate of source controlled variable bit-rate (SC-VBR) coding, and 7.2, …, 128 represent the bit-rates of constant bit-rate source coding. If a single bit-rate is used in the session, br is set to the bit-rate. If not present, all bit-rates are supported.
 | TS 26.114 Handling | br can replace br-send and br-recv in the SDP offer or SDP answer when an identical set of bit-rates are used for the send and the receive directions. br shall not be used with br-send or br-recv for the same payload type.
bw | TS 26.445 Definition | Specifies the bandwidth to be used in the session for the send and the receive directions. bw-send has a value from the set: nb, wb, swb, fb, nb-wb, nb-swb, and nb-fb. nb, wb, swb, and fb represent narrowband, wideband, super-wideband, and fullband respectively, and nb-wb, nb-swb, and nb-fb represent all bandwidths from narrowband to wideband, super-wideband, and fullband respectively. If not present, all bandwidths are supported.
 | TS 26.114 Handling | bw can replace bw-send and bw-recv in the SDP offer or SDP answer when an identical set of bandwidths are used for the send and the receive directions. bw shall not be used with bw-send or bw-recv for the same payload type.
TS 26.114 Status | 
UE Support | Use
Mandatory | Optional

## Slide 12
Annex C: DTX Control
Parameter | Location | Definition
dtx-off | TS 26.445 Definition | Indicates that discontinuous transmission (DTX) is not used in the session.
 | TS 26.114 Handling | When dtx-off is not offered for a payload type, the answerer may include dtx-off for the payload type in the SDP answer. When dtx-off is offered for a payload type which is accepted, the answerer shall not remove dtx-off for the payload type in the SDP answer.
TS 26.114 Status | 
UE Support | Use
Mandatory | Optional

## Slide 13
Annex D: SDP Offer/Answer Example
  This example shows the SDP offer when the session is initiated from MTSI client in terminal using fixed access, which supports AMR with the {12.2, 7.4, 5.9 and 4.75} codec mode set and AMR-WB with the {12.65, 8.85 and 6.60} mode set. In addition, EVS, G.722, and PCM codecs are supported.
  For EVS, RTP Payload Types 97 and 98 are defined, for example, to initiate a speech session with another MTSI client in terminal using fixed access supporting a bit-rate of 64 kbps or radio access supporting all bit-rates from 5.9 to 24.4 kbps.
SDP offer (IPv4)
m=audio 49152 RTP/AVP 97 98 99 9 100 0 8 a=tcap:1 RTP/AVPF a=pcfg:1 t=1 b=AS:80 b=RS:0 b=RR:2000 a=rtpmap:97 EVS/16000/1 a=fmtp:97 br=64; bw=wb; dtx-off; max-red=220 a=rtpmap:98 EVS/16000/1 a=fmtp:98 br-send=5.9-24.4; br-recv=5.9-24.4; bw-send=nb-swb; bw-recv=nb-swb; max-red=220 a=rtpmap:99 AMR-WB/16000/1 a=fmtp:99 mode-set=0,1,2; max-red=0 a=rtpmap:100 AMR/8000/1 a=fmtp:100 mode-set=0,2,4,7; max-red=0 a=rtpmap:9 G722/8000/1 a=rtpmap:0 PCMU/8000/1 a=rtpmap:8 PCMA/8000/1 a=ptime:20 a=maxptime:80
(1) SDP answer (IPv4)
m=audio 49152 RTP/AVP 98 b=AS:41 b=RS:0 b=RR:2000 a=rtpmap:98 EVS/16000/1 a=fmtp:98 br-send=13.2-24.4; br-recv=13.2-24.4; bw-send=nb-swb; bw-recv=nb-swb; max-red=220 a=ptime:20 a=maxptime:240
(2) SDP answer (IPv4)
m=audio 49152 RTP/AVP 97 b=AS:80 b=RS:0 b=RR:2000 a=rtpmap:97 EVS/16000/1 a=fmtp:97 br-send=64; br-recv=64; bw-send=wb; bw-recv=wb; dtx-off; max-red=220 a=ptime:20 a=maxptime:240