## Slide 1: Outline
  Fundamental benefits and disadvantages of scalable video coding
Comparison of SHVC vs SVC
Use cases of SHVC in different applications
SHVC coding performance

## Slide 2: The fundamental benefits and disadvantages of scalable video coding (1/2)
The benefits come from the compression advantage of layered coding utilizing inter layer prediction compared to “simulcast”.
Here, “simulcast” means that different versions of the same video content are encoded independently.
The benefits would only apply in scenarios where different versions of the same video content are necessary.
  They thus do not apply to one-to-one communications, such as video telephony, where only one version is needed for one video content
    Even when adaptive bit rate is needed, rate control can be used, thus still just one version of the video content
    There are corner cases where the network needs to do rate adaptation in order to react to immediate bitrate changes, for example if network buffers are overloaded. However, this requires deep integration of application layer technologies and network buffers and is therefore not a primary use case.

## Slide 3: The fundamental benefits and disadvantages of scalable video coding (2/2)
The benefits apply to one-to-many communications, including broadcast, streaming (live and VoD), and video conferencing where multiple receivers need different versions of the same video
  Here concrete benefits include bandwidth saving in “backbone” network (between the origin server and caches/proxies), or more programs/channels, or higher qualities for the same programs --- good for service providers as well as reducing backbone network congestion
    The fundamental disadvantages are higher bandwidth and higher decoding/decoder complexity for high-end users who only need the enhancement layer signal
    Thus whether use of scalable coding makes sense to the extent for (wide) deployment depends on how big are the benefits vs the disadvantage, business model, and so on
    One key aspect is whether the increased bandwidth and decoding/decoder complexity can be controlled to be non-significant
  Another concrete benefit is reduced storage size, which in today’s VoD environment can translate into significant cost reduction
  Does not apply much for long-tail contents consumed by few users, which are similarly as one-to-one

## Slide 4: SHVC vs SVC
Aspects |  | SVC | SHVC
Scalability features | Overall feature set | 3 (temporal, spatial, SNR) | 6 (temporal, spatial, SNR, bit depth, color gamut, hybrid codec)
 | Spatial scalability | Limited to 2x and 1.5x in Baseline | Arbitrary ratio, field picture in BL, downsampling filter flexibility, etc
Backward compatibility |  | AVC coded base layer only | HEVC or non-HEVC coded base layer
Decoder design | BL decoder | Requires new API design in the BL | No change to the base layer decoder
 | EL decoder | Cannot reuse AVC decoder | With no block level changes, easy to repurpose existing HEVC decoder products into SHVC decoder
Encoder design |  | Cross layer optimization complicates rate control | Easy to reuse existing HEVC encoder products
Splicing and random access |  | Decoders are required to be more intelligent than conforming decoders to utilize open-GOP RAPs and non-cross-layer aligned RAPs, and consequently IOP in this aspect is not guaranteed | Decoders are NOT required to be more intelligent than conforming decoders to utilize open-GOP RAPs and non-cross-layer aligned RAPs, and consequently IOP in this aspect is guaranteed

## Slide 5: SHVC in video broadcast (1/2)
Advantages:
  The fundamental benefits (for all contents: less bandwidth in the backbone network, more programs, or higher quality; less backbone network congestion; reduced storage size)
  Reuse of two HEVC 4K decoders in set-top boxes (which was said to be a standard feature for pic-in-pic function) to do 1080p-to-4K scalability almost for free (only a re-sampler and some firmware changes needed)
  Use of multi-layer SHVC to add more temporal sub-layers (i.e. to enhance frame rate) or layers in the future – a use case discussed in DVB
  Use of SHVC in order to add advanced video experience (HDR, BT.2020 color gamut)
  Support enhancement to legacy AVC devices as well (with AVC as the base layer, enhancement layers coded using SHVC)
  Other benefits, such as those documented for eMBMS in 3GPP TR 26.904 for SVC but applicable to SHVC as well
    Unequal error protection, layer-aware transmission for coverage and capacity improvements, graceful degradation, fast stream switching

## Slide 6: SHVC in video broadcast (2/2)
Disadvantages:
  The fundamental disadvantages (higher bandwidth and decoder/decoding complexities for high-end users who only need the enhancement layer signal
Ways to alleviate the disadvantages
  SHVC general encoding optimization
  More frequent IRAPs for lower layers, could potentially let high-end receivers have lower bandwidth than simulcast
  Apply UEP to the layered bitstream, where less channel coding redundancy is added to the enhancement layer, partially or fully offsetting the increased bandwidth of source coding
  Etc.

## Slide 7: SHVC in video streaming (1/2)
Advantages:
  The fundamental benefits (for popular contents: less bandwidth in the backbone network, more programs, or higher quality, less backbone network congestion; reduced storage size)
  Efficient delay optimization in live streaming based on DASH
    A currently popular low-latency live streaming solution is to simulcast multiple rates/qualities, and the receiver uses whatever that have been received and playable at a time based on the low-latency requirement and discard other data. Layered coding can potentially provide very good benefit compared to simulcast in this scenario.
  Improved cache hit ratio for adaptive streaming (DASH)
    Some detailed results can be seen from Section 6.1.3.7 of 3GPP TR 26.904

## Slide 8: SHVC in video streaming (2/2)
Disadvantages:
  The fundamental disadvantages (higher bandwidth and decoder/decoding complexities for end users)
Ways to alleviate the fundamental disadvantages
  Higher bandwidth for end users:
    SHVC general encoding optimization
    Different IRAP frequencies for different layers
    Duration between IRAPs larger than desired end-to-end latency
  Decoder and decoding complexities: more severe than other services due to the higher number of layers needed
    Decoder complexity: Less of an issue for SHVC compared to SVC because of the high-level syntax only design of SHVC
    Decoding complexity: Control of the inter-layer prediction chain length to trade-off between decoding complexity and compression efficiency

## Slide 9: SHVC in video conferencing (1/2)
Advantages:
  The fundamental benefits (less bandwidth in the backbone network, more participants, or higher quality; less backbone network congestion)
  Reduced end-to-end delay (improved user experience for a given end-to-end delay)
  Using 3 layers and unequal error protection, e.g.,
    Client 1 encodes at 1080p with 3 layers (1080p, 540p, 270p).
    Client 2 is on a high quality network with a powerful machine, and decodes all 3 layers, with a target output layer of 1080p
    Client 3 is on a lower bitrate network and/or lower CPU machine, and decodes 2 layers (540p and 270p).
    The base 270p layer is used for error resiliency and network adaptation when the 540p layer is occasionally lost or intentionally dropped.

## Slide 10: SHVC in video conferencing (2/2)
Disadvantages:
  The fundamental disadvantages (higher bandwidth and decoder/decoding complexities for end users)
Ways to alleviate the fundamental disadvantages
  SHVC general encoding optimization
  More frequent IRAPs for lower layers, could potentially let high-end receivers have lower bandwidth than simulcast

## Slide 11: SHVC common test conditions
Types of scalability tests include:
  Spatial scalability of 2x and 1.5x
  SNR scalability (1x spatial ratio, low quality to high quality)
  Combined scalability (1080p 8-bit BT.709 to 4K 10-bit BT.2020)
Test sequences:
  7 pairs of sequences for spatial and SNR scalability
  5 pairs of sequences for combined scalability
Coding configurations:
  All Intra, random access, low delay
  Random access is the most relevant for broadcast video applications and this set of results is provided

## Slide 12: Spatial scalability (HEVC coded base layer)
* In this and the next 3 slides: performance is measured against simulcast for both “BL+EL” and “EL only”

## Slide 13: Spatial scalability (AVC coded base layer)

## Slide 14: SNR scalability (HEVC coded base layer)

## Slide 15: Combined scalability (HEVC coded base layer)

## Slide 16: Compared to single-layer coding - Spatial and SNR scalability
Spatial ratio | 2x | 1.5x | SNR (1x)
Traffic | 24.0% |  | 20.1%
PeopleOnStreet | 18.8% |  | 13.8%
Kimono | 13.9% | 9.2% | 14.1%
ParkScene | 18.5% | 17.8% | 15.9%
Cactus | 22.6% | 20.4% | 16.8%
BasketballDrive | 17.6% | 13.9% | 12.2%
BQTerrace | 17.2% | 18.6% | 7.3%
Average | 18.9% | 16.0% | 14.3%
* In this and the next slide: performance is measured against single-layer coding of the higher-quality signal.

## Slide 17: Compared to single-layer coding - Combined scalability
Scalability type | Spatial, bit depth, and color gamut scalability | Color gamut scalability only
Birthday | 28.2% | 23.3%
BirthdayFlash1 | 21.5% | 27.5%
BirthdayFlash2 | 23.5% | 29.2%
Parakeets | 15.6% | 18.5%
Tablecar | 15.8% | 38.9%
Average | 20.9% | 27.5%