## Slide 1: S4-150058 Overview of HbbTV / DVB Interactivity
Paul Szucs, Sony Europe Limited

## Slide 2: HbbTV system overview

## Slide 3: Overview of DVB signalling framework
The (relevant) DVB specification (TS 102 809) provides a framework for the signalling and carriage of interactive applications or services in both broadcast and broadband networks, covering:
  Signalling interactive applications or services
    How the receiver identifies the applications associated with a service and finds the locations from which to retrieve them
    The signalling that enables the broadcast to manage the lifecycles of applications
    How the receiver can identify the sources of broadcast data required by the applications of a service
  Distributing the files of interactive applications or services
    Carriage in MPEG-2 DSM-CC Object Carousel or HTTP 1.1
  Synchronizing interactive applications or services to video or audio content
    „Do-it-now“ events or according to DVB timeline
    DSM-CC Stream Event, or XML equivalent
  Referencing video, audio or subtitle content from interactive applications or services
    URL scheme „dvb:“
Spec is independent of any particular technology for interactive applications or services
Spec enables a wide range of different application models depending on which of the optional features are selected

## Slide 4: Overview of HbbTV platform
The HbbTV specification (TS 102 796) provides a platform for signalling, transport, and presentation of enhanced and interactive applications designed to run on hybrid terminals that include both a DVB compliant broadcast connection and a broadband connection
The main uses of the broadcast connection are the following:
  Transmission of standard TV, radio and data services
  Signalling of broadcast-related applications
  Transport of broadcast-related applications and associated data
  Synchronization of applications and TV/radio/data services
The main uses of the broadband connection are the following:
  Carriage of both on-demand and live content
  Transport of broadcast-related and broadcast-independent applications and associated data
  Exchange of information between applications and application servers
  Applications are presented by an HTML/JavaScript browser

## Slide 5: HbbTV platform characteristics
The platform is open and is not based on a single controlling authority or aggregator; so services and content from many different and independent providers are accessible by the same terminal
Standard functions of the terminal are available to all applications; sensitive functions of the terminal are available only to trusted applications
Services and content may be protected
Broadcast applications can be presented on terminals which are not connected to broadband
Applicable to various types of terminals, such as IDTVs, STBs and PVRs
Both broadcast-related and broadcast-independent applications are supported
Video, audio and system formats for the broadcast channel are out of scope
Protocols for the broadcast channel not relating to interactive applications are out of scope

## Slide 6: HbbTV platform characteristics
The terminal browser environment is based on:
  OIPF Release 2:
    Volume 5 - Declarative Application Environment
    Volume 7 – Authentication, service protection and content protection
  TV functionality JavaScript API (OIPF Volume 5)
  CE-HTML (CEA-2014) (via OIPF Volume 5)
  W3C DOM2, CSS2, XHTML (via OIPF Volume 5 and CEA-2014)
Supported media formats:
  OIPF Release 2, Volume 2 – Media formats
    H.264/AVC video; HE-AAC audio; many optional formats
  MPEG-DASH and –CENC
    ISOBMFF live profile (applied to both on-demand and live content)
 Overview on next slide

## Slide 7: HbbTV V1.5 specification overview

## Slide 8: HbbTV terminal functional components

## Slide 9: HbbTV V2.0
New version of HbbTV specification will be published soon
New features:
  Migration to HTML5 and associated technologies
    (as specified by OIPF Web Standards TV Profile – Volume 5b)
  Companion screen funtionality
    App-to-app communications
    Remote app launch (based on DIAL)
    Synchronisation of apps and content across devices
  Media formats
    HEVC video via broadband
    Subtitles via broadband (EBU-TT-D)
    Refer to DVB DASH profile
  Ad insertion with VoD content
  Push-VoD
  User privacy features
  Multi-stream synchronisation
  (CI+ V1.4 – DRM in a CAM; CAM file system)