## Slide 1: HEVC Screen Content Coding extension for IMS-based telepresence
S4-160371
3GPP TSG SA4#88 meeting
18-22 April, 2016, Memphis, TN, USA
Qualcomm Incorporated
For discussion

## Slide 2: Screen sharing use case
3GPP TS 22.228 V13.3.0 annex G presents IMS-based telepresence use cases
One of the video streams can be screen or desktop sharing among the participants

## Slide 3: Screen Content – What is it?
Screen content includes graphics and text which can be mixed with camera-captured content, for example, in the following applications:
  Desktop screen sharing
  Text and graphics overlay

## Slide 4: Need for 4:4:4 in screen content (1)
Uncompressed
4:2:0
4:4:4

## Slide 5: Need for 4:4:4 in screen content (2)
Uncompressed
4:2:0
4:4:4

## Slide 6: Need for 4:4:4 in screen content (3)
4:2:0
4:4:4
Compressed text
Uncompressed text

## Slide 7: Need for 4:4:4 in screen content (4)
Chart: 
| 352213 | 263659 | 207726 | 159443 | 110477 | 82094 | 55753
V420 | 35.4184 | 35.3994 | 35.3707 | 35.2301 | 34.8817 | 34.5361 | 33.9593
V444 | 63.1943 | 59.2171 | 54.4025 | 50.6207 | 46.6406 | 42.1337 | 37.256
YUV PSNR vs bit-rate for HEVC compression
on 4:4:4 vs 4:2:0 domain
PSNR is calculated in 4:4:4 domain
CNN sequence
dB
bps
Chart: 
| 352213 | 263659 | 207726 | 159443 | 110477 | 82094 | 55753
Y420 | 67.3006 | 59.5561 | 55.3285 | 51.0549 | 45.8791 | 41.6952 | 36.3033
Y444 | 61.4978 | 57.2934 | 53.0577 | 48.8594 | 44.6971 | 40.2087 | 35.6006
Chart: 
| 352213 | 263659 | 207726 | 159443 | 110477 | 82094 | 55753
U420 | 35.4557 | 35.4392 | 35.4063 | 35.2676 | 34.8938 | 34.4637 | 33.9248
U444 | 63.2304 | 59.2965 | 54.6107 | 50.6561 | 46.3983 | 41.933 | 36.7559
U
Y
V
Chart: 
| 352213 | 263659 | 207726 | 159443 | 110477 | 82094 | 55753
YUV420 | 46.0582 | 43.4649 | 42.0352 | 40.5175 | 38.5515 | 36.8983 | 34.7291
YUV444 | 62.6408 | 58.6023 | 54.0236 | 50.0454 | 45.912 | 41.4251 | 36.5375
YUV
dB
dB
bps
bps
dB

## Slide 8: Coding Screen Content Efficiently
HEVC Screen Content Coding (SCC) extension
Is a ratified HEVC profile
HEVC SCC is built on top of HEVC Main 4:4:4 and Main profiles with additional tools for improving compression efficiency of screen content coding
It supports 4:2:0, 4:4:4 chroma colour formats and lossless mode coding

## Slide 9: Additional tools added to Main 4:4:4 and Main profiles
Intra block copy
  Inter prediction like method, where the current picture can be used as a reference for prediction
Palette mode
  Block reconstruction is performed from the colours specifically signalled for the current block or from the colours already signalled for the previously coded palette blocks
Adaptive Colour Transform
  In-loop color transform to accommodate various colour spaces

## Slide 10: Test sequences (1)
Text and graphics with motion (4:4:4 8 bits)
FlyingGraphics 1920x1080 60fps
Desktop 1920x1080 60fps
Console 1920x1080 60fps
WebBrowsing 1280x720 30fps
Map 1280x720 60fps
SlideShow 1280x720 20fps

## Slide 11: Test sequences (2)
Mixed content (4:4:4 8 bits)
BasketballScreen 2560x1440 60fps
MissionControlClip2 2560x1440 60fps
MissionControlClip3 1920x1080 60fps

## Slide 12: Performance of Screen-Extended Main 4:4:4 profile (1)
SCM-7.0 reference software
  Input is 4:4:4 chroma colour format, 8 bits
  Anchor is SCM-7.0 without SCC tools
  Test: all tools are enabled

## Slide 13: Performance of Screen-Extended Main 4:4:4 profile (2)
Data test set and configuration:
  HEVC SCC common test condition sequences for test & graphics with motion and mixed content
  Input is 4:4:4 chroma colour format, 8 bits
  Average on the set of sequences with the same resolution
 | All Intra |  |  | Random Access |  |  | Low delay |  | 
 | Y | U | V | Y | U | V | Y | U | V
1280x720 | -47.3% | -53.0% | -56.2% | -36.4% | -43.0% | -48.2% | -20.7% | -27.1% | -32.0%
1920x1080 | -66.2% | -69.4% | -69.4% | -49.4% | -55.1% | -55.0% | -34.7% | -41.2% | -40.8%
2560x1440 | -42.3% | -49.8% | -49.5% | -30.6% | -41.4% | -40.8% | -18.1% | -30.0% | -29.6%
Y, U, and V are colour components and –X% stands for bitrate reduction comparing to Main 4:4:4 profile
All intra is the configuration where all pictures are I-pictures
Random Access is the configuration with periodical I-pictures with GOP structure and B-pictures
Low delay is the configuration where all references are from the past and it targets low delay applications

## Slide 14: Performance of Screen-Extended Main profile (1)
SCM-7.0 reference software
  Input is 4:2:0 chroma colour format, 8 bits
  Anchor is SCM-7.0 without SCC tools
  Test: all tools are enabled

## Slide 15: Performance of Screen-Extended Main profile (2)
Data test set and configuration:
  HEVC SCC common test condition sequences for test & graphics with motion and mixed content
  Input is 4:2:0 chroma colour format, 8 bits
  Average on the set of sequences with the same resolution
 | All Intra |  |  | Random Access |  |  | Low delay |  | 
 | Y | U | V | Y | U | V | Y | U | V
1280x720 | -41.2% | -41.5% | -43.9% | -29.3% | -30.5% | -34.3% | -13.9% | -15.9% | -19.1%
1920x1080 | -57.2% | -57.1% | -57.0% | -38.7% | -40.3% | -40.2% | -24.8% | -27.4% | -27.2%
2560x1440 | -34.8% | -36.4% | -36.9% | -24.6% | -27.1% | -28.2% | -14.0% | -16.7% | -17.2%
Y, U, and V are colour components and –X% stands for bitrate reduction comparing to Main profile
All intra is the configuration where all pictures are I-pictures
Random Access is the configuration with periodical I-pictures with GOP structure and B-pictures
Low delay is the configuration where all references are from the past and it targets low delay applications

## Slide 16: Status of HEVC SCC Extension
Final draft International Standard (FDIS) stage in MPEG
HEVC SCC extension was also adopted as optional codec in Wi-Fi Miracast R2 specification draft
We believe that HEVC SCC extension with 4:4:4 is an important option and opportunity for 3GPP IMS Telepresence to address the emerging need for new type of applications to address highest quality and efficiency