## Slide 1
Source: Orange ( Beatrice Rouxel Orange, Frederic Desnoes Orange)
Support of CMCC and Fibercop
DP S5-260425: Concepts and use cases on NDT For Mobile networks – Alignment with IETF

## Slide 2: General statements
Our analysis is based on the comparison between 3GPP SA5 standardization efforts for NDT in comparison of IETF similar initiative.
[1] 3GPP TR 28.883 v0.2.0 (2025-11)
Study on management aspects of Netorwk Digital Twins; Phase 2 (Rel. 20)
[2] 3GPP TS 28.561 v19.1.0 (2025-12)
Management aspects of Network Digital Twins; (Rel. 19)
[3] 3GPP TS 28.312 v19.4.0 (2025-12)
Intent driven management services for mobile networks; (Rel. 19)
IETF: Network Digital Twin: Concepts and Reference Architecture
draft-irtf-nmrg-network-digital-twin-arch-11 (2025-07-07)
Our proposal is to introduce the relevant concepts and use cases in R20, either in 5GA if they are aligned with the new WID scope or in 6G.

## Slide 3: Dynamicity of NDT
In IETF
  The functional model aims to realize the dynamic evolution of network performance evaluation and intelligent decision-making“.
  "In the future, in addition to improving the generalization ability and interpretability of AI models, there is also a need to focus on how to improve the Real-time and interactivity of model reasoning based on data and control in NDT layer".
In 3GPP
  [1] § 5.8 UC #8: Using external data for NDT modelling[2] § 5.1 Control and LCM of NDTs.
  dynamic evolution of network performance topic is not covered.
Our proposal
  In the network modeling, information on the freshness of data and the operational status of equipment in the network should be added, so that the representation of the actual network with the NDT is as accurate as possible.
  It would also be necessary in network modeling to account for the real topology of the network dynamically, in order to take into account the evolution of the network’s performance, almost in real time.

## Slide 4: Twinning management
In IETF
  "Twining management involves various network components (e.g., controller, orchestration) and domains (security for ex.) from E2E, including , but not limited to, the following main technologies:
    Orchestration of twins
    Collaboration Management
    Conflict Detection and Resolution
    Energy-Efficient Twinning“
In 3GPP
  [2] § 4.4 NDT Life-cycle management & § 5.1 Control and LCM of NDTs
  [1] § 5.11 UC #11: Create and Execute NDT Job & 5.12 UC #12: Clarification of Suspension and Resumption capabilities for NDTJobs & 5.4 UC# 4: Enhancement for multiple collaborations
Our proposal
  orchestration of twins: it would be necessary to manage and organize several instances of twin models.
  energy efficiency in the NDT system: it would be necessary to add control in energy
  collaboration between several NDTs: it would be necessary to manage the coordination between several NDTs instances for the accomplishment of a task => use of autonomous agents? link between Autonomous Agents and NDT instances for the realization of an intent?

## Slide 5: New application scenarios / use cases
In IETF
  It is mentioned some application scenarios where NDT can be applied to solve different problems in network management and operation:
    Human training (need of a human-in-the-loop with the use of NDT to improve the operators performance: ex. cybersecurity incident handling)
    ML Training ("NDT simplifies the complete ML Lifecycle development by providing a realistic environment, including network topologies, to generate the data required in a well-aligned context...).
    Devops-Oriented Certification (use of NDT environment to verify the specific impacts of updates on service assurance and SLAs...)
    Network Fuzzing (use of NDT environment to identify vulnerabilities, bugs and zero-day attacks before production delivery in the production network).
    Network Inventory Management (use of NDT management as a means to ensure consistent representation and reporting of inventory component types).
In 3GPP
  "[1] § 5.2 UC #2: Improvement of data generation and §5.3 UC #3: Collaborate with ML training Producer to generate data[2] § 5.4 NDT support for data generation"
  "NDT support for ML training is introduced with data generation capability. "
Our proposal
  The 4 application scenarios"Human training", "Network Fuzzing", "Devops-Oriented Certification" and "Network Inventory Management" are not covered by 3GPP SA5 TS and TR=> can be added as Use cases in[2] § 5.2 NDT support for network automation and be handeled in [1].

## Slide 6: Thank You !