## Slide 1: ProSe Status Updates SA5#95bis 12-14 August 2014, Issy-les-Moulineaux (France)
Qualcomm Incorporated

## Slide 2: Introduction and Outline
SA2 Rel-12 work item successfully concluded at SA#64 (Jun 2014)
  TS 23.303 v12.1.0 is latest TS version after SA#64 approved CRs
  Rel-12 WID is marked 100% complete, and placed into maintenance list
SA3 Rel-12 work item is also concluded at SA#64
  TS 33.303 (S3-140975) is approved with no contention issue remaining
CT WGs has achieved 90% completion (Jul 2014)
  TS24.333 (OMA-DM MO); TS24.334 (PC3 interface); TS29.343 (PC2 for EPC-level disc); TS29.344 (PC4a); TS29.345(PC6/7)
Outline
  General
  Architecture
  D2D related
    Direct Discovery
    One-to-many Direct Communication
    ProSe impacts to EPC procedures
  EPC-level discovery
    EPC-support for WiFi-Direct

## Slide 3: General
Original ProSe WID SA2 scope considered the following features:
  Direct Discovery
    Open discovery (in coverage, consumer/commercial)
    Restricted discovery (in coverage, public safety and consumer/commercial)
    Restricted discovery (out of coverage, public safety)
  Direct Communication
    One-to-one communication (commercial/consumer)
    One-to-many communication (public safety)
    Support for ProSe UE-Network Relays (public safety)
  EPC support of ProSe Comm over WiFi (consumer/commercial)

## Slide 4: General (cont.)
The approved TS 23.303 Rel.12 provided stage-2 procedures for only the following features (due to time constraints):
  Direct Discovery
    Open discovery (in coverage, consumer/commercial and public safety)
    Restricted discovery (in coverage, public safety and consumer/commercial)
    Restricted discovery (out of coverage, public safety)
  Direct Communication
    One-to-one communication (commercial/consumer)
    One-to-many communication (public safety)
    Support for ProSe UE-Network Relays (public safety)
      Because of lacking the support in RAN WID
  EPC-level discovery (consumer/commercial)
  EPC support for WiFi-Direct (consumer/commercial) *
    * EPC support for WiFi-Direct setup can also be part of the EPC-level discovery

## Slide 5: ProSe Architecture
Main new functional node is the ProSe Function
New reference points
  PC2: ProSe Function- 3rd party app (only used for EPC-level discovery)
  PC3: UE-ProSe Function in HPLMN,
  PC4a: ProSe Function-HSS
  PC4b: ProSe Func – SUPL Locaiton Platform (SLP)
  PC5: UE-UE, for control and user plane
  PC6: Inter-PLMN ProSe Function to ProSe Function (HPLMN – LPLMN)
  PC7: Roaming ProSe Function-ProSe Function (HPLMN – VPLMN)
In this figure, UE A uses a subscription of PLMN A and UE B uses a subscription of PLMN B; UE A is roaming in PLMN C while UE B is not roaming.
    * The architecture is updated by CR approved at SA2#104
    (S2-142911)

## Slide 6: ProSe Architecture
The ProSe Function has the following sub-functions:
  DPF: Is used for UE provisioning and PLMN authorisation
  Direct discovery name mgt server: is used for open discovery for assignment/lookup of ProSe App. IDs/ProSe App. Codes
  EPC-level discovery Function: is used for performing proximity matching based on location info
Figure 4.4.1-1: UE to ProSe Function Interfaces for each sub-function
Figure 4.4.1-2: ProSe Function Interfaces to other network elements and PLMNs
    * The architecture is updated by CR approved at SA2#104
    (S2-142911)

## Slide 7: Common Functions – Service auth & provisioning
Service Authorisation & Provisioning
  UE interacts with DPF in HPLMN
  Indicates whether the UE is authorised for direct discovery and communication per PLMN
    Pre-authorised (only from HPLMN)
    Conditionally Authorised (from HPLMN and every Local PLMN)
  Uses OMA-DM
Additional Provisioning for PubS
  Provided from DPF in HPLMN
  Configures the UE to operate out of coverage
    Radio parameters
    Group ID
    IP multicast address
    Security container
  Uses OMA-DM
    * The architecture is updated by CR approved at SA2#104
    (S2-142911)

## Slide 8: Common Functions – service revocation
Service revocation
  Can be triggered by HSS or ProSe Func
  The ProSe Func can be in HPLMN, VPLMN or LPLMN
  UE is informed of the revocation by the ProSe Service Notification message immediately, or at next time communicating with the ProSe Func
    This is up to operator policy
  eNB is updated on the “ProSe Authorized” indication by MME, if S1 bearer is established
  This revocation is per UE subscription, not per ProSe App ID.
Figure 5.2.2.2-1: HSS triggered ProSe direct services revocation
Figure 5.2.2.4-1: ProSe Function triggered ProSe direct services revocation(roaming)

## Slide 9: Direct Discovery -General
General concept
  ProSe Direct Discovery is defined as the process that detects and identifies another UE in proximity using E-UTRA direct radio signals.
  Two types of ProSe Direct Discovery: open and restricted.
    Open is the case where there is no explicit permission that is needed from the UE being discovered
    Restricted discovery only takes place with explicit permission from the UE that is being discovered (not defined in rel.12)
  ProSe Direct Discovery can be a standalone service enabler that could for example use information from the discovered UE for certain applications in the UE that are permitted to use this information e.g. "find a taxi nearby", "find me a coffee shop".
UE Roles
  Announcing UE: The UE announces certain information that could be used by UEs in proximity that have permission to discover.
  Monitoring UE: The UE that monitors certain information of interest in proximity of announcing UEs.
Assumptions
  The UE can act as "announcing UE" only in the band designated by the serving PLMN but may act as a "monitoring" UE also in the resources of other PLMN(s) in the same area if authorised. These PLMNs are called Local PLMNs.

## Slide 10: Direct Discovery- General
Identities
  ProSe App. ID: The ProSe Application ID is an identity used for ProSe Direct Discovery, identifying application related information for the ProSe-enabled UE. Each ProSe Application ID could be globally unique, e.g. in case of open Direct Discovery, it unambiguously identifies a service across all 3GPP PLMNs
    Example:prose.commercialID.retail.shoe-store.zoe’s shoes.10298.mcc<mcc>.mnc<mnc>
  ProSe Application Code: The ProSe Application Code is associated with the ProSe Application ID and contained in the discovery message that is transmitted over the radio interface (on PC5) by a ProSe-enabled UE engaged in the ProSe Direct Discovery procedure. The ProSe Application Code is allocated per "announcing" UE and per application and has an associated validity timer that runs both in the ProSe Function and in the UE.
Concept of ProSe App. Code matching and partial matching
  ProSe Application Code matching all components of the ProSe App. Code. In ProSe Application Code matching, the "monitoring" UE shall consider it a full match, if both PLMN ID and temporary identity match with the corresponding contents of the Discovery Filter.
  A partial match is obtained if the PLMN ID matches fully and the temporary identity matches partially with the corresponding contents of the Discovery Filter.
Example ProSe App. ID tree for the commercial branch
PC5 message and ProSe App. Code
as defined by CT1 (TS24.334) and CT4 (TS23.003)
DiscoveryType (8bits)
PLMN ID
(3-23 bits)
Temp ID
(184 – (PLMNID) bits)
MIC (Security)
(32 bits)
ProSe App Code = 184 bits

## Slide 11: Direct Discovery – Basic steps
1. Service authorisation
  Provides a list of PLMNs that the UE is allowed to “announce/monitor”
2a. Discovery request (for announcing UE)
  Announce: UE sends a ProSe App. ID indicating what it wants to announce and gets a ProSe App. Code from the ProSe Function in HPLMN
2b. Discovery request (for monitoring UE)
  Monitor: UE sends a ProSe App. ID indicating what it wants to monitor and gets a Discovery Filter from the ProSe Function in HPLMN
3. Match report (for monitoring UE)
  Monitoring UE sends ProSe App. Code(s) it receives OTA to its HPLMN ProSe Function for checking and interpretation
  The HPLMN ProSe Function passes ProSe App.Code(s) to ProSe Function(s) of the PLMN that issued codes
  This ProSe functions checks ProSe App. Code(s) and if successful any meta-data to the HPLMN ProSe function of the monitoring UE
More details for the procedures in Annex

## Slide 12: Direct Discovery- Security
Integrity protection of OTA code, with network-side checking
  Verification of the MIC always happen at the HPLMN of the Announcing UE;
  Network provides current time to the UE at Discovery Request
  UE reports the time of the code match in the Match Report
    This is verified during the MIC check.
    * This is based on TS 33.303

## Slide 13: Direct Communication (one-to-many) -General
Applicability
  One-to-many ProSe Direct Communication is applicable only to ProSe-enabled Public Safety UEs and when authorised, can apply when the UE is served by E-UTRAN and when the UE is outside of E-UTRA coverage.
General concept
  One-to-many ProSe Direct Communication is connectionless.
    There is no signalling over PC5 control plane.
  There is no QoS support apart from priority handling.
  The radio layer provides a user plane communication service for transmission of IP packets between UEs engaged in direct communication.
  Members of a group share a secret from which a group security key may be derived to encrypt all user data for that group.
  Authorisation for one-to-many ProSe Direct Communication is configured in the UE by the ProSe Function using PC3 reference point.
  ProSe UE configuration parameters (e.g. including ProSe Group IP multicast addresses, ProSe Group IDs, Group security material, radio related parameters) are configured in the UE.

## Slide 14: Direct Communication (one-to-many)- transmission
1. UE is configured with the related information for one-to-many ProSe Direct Communication as defined in slide 7. The UE obtains the necessary group context (ProSe Layer-2 Group ID, ProSe Group IP multicast address) to transmit IP-layer transport of data, and also the radio resource related parameters used for the Direct Communication.
2. The originating UE finds the appropriate radio resource to conduct one-to-many ProSe Direct Communication. If the UE is "served by E-UTRAN" it always uses the resources signalled from the network. If the UE is not "served by E-UTRAN" it uses the appropriate radio resources for this purpose.
3. The originating UE sends the IP data to the IP multicast address using the ProSe Layer-2 Group ID as Destination Layer-2 ID.

## Slide 15: Direct Communication one-to-many - reception
1. UE is configured with the related information for one-to-many ProSe Direct Communication as defined in slide 7. The UE obtains the necessary group context (ProSe Layer-2 Group ID, Group IP multicast address) to receive IP-layer transport of data, and also the radio resource related parameters used for the Direct Communication.
2.The receiving UE listens to the allocated radio resource to receive one-to-many ProSe Direct Communication.
3.The receiving UE filters out the received packet based on the ProSe Layer-2 Group ID contained in the Destination Layer-2 ID and if it matches the Group IDs configured, delivers the packet to upper layers. The user plane packets will be delivered to the IP stack that filters the packets based on the Group IP multicast address.

## Slide 16: Direct Communication (one-to-many) - security
Per-group keys (PGK), provisioned into each member UE
  Traffic keys (PTK, PEK) are unique per UE
  UE layer 2 ID (Group member ID) is provided by network
    * This is based TS 33.303

## Slide 17: ProSe Direct Disc/Comm. impacts to EPC procedures
In certain cases (Type 2 Discovery, mode 1 communication) E-UTRAN needs be aware of whether a UE is capable and authorised for D2D service (Direct Discovery or Direct Communication) in order to be able to schedule resources, etc.
Therefore EPC needs to inform E-UTRAN whether a UE is capable and authorised to perform ProSe Direct Discovery, ProSe Direct Communication or both.
As a result of that the following changes are described in TS 23.303 in the EPC procedures described in TS 23.401:
  E-UTRAN Attach
    ProSe-enabled UE includes the ProSe capability indication as part of the "UE Network Capability" in the Attach Request message. MME stores this information for ProSe operation. ProSe capability can indicate whether the UE is capable of supporting one or more of the following: ProSe Direct Discovery, ProSe Direct Communication and act as a ProSe UE-to-Network Relay.
    MME may include a "ProSe authorised" indication in the S1 AP Initial Context Setup Request, indicating that the UE is authorised to use ProSe, if the MME is configured to indicate "ProSe authorised" to E-UTRAN.
  Service Request procedure
    MME may include a "ProSe authorised" indication in the S1 AP Initial Context Setup Request, indicating that the UE is authorised to use ProSe, if the MME is configured to indicate "ProSe authorised" to E-UTRAN.
  PS handover procedure
    Intra-E-UTRAN S1-based handover procedures for ProSe-enabled UE are performed with the following additions:
      The target MME includes a "ProSe authorised" indication in the S1-AP Handover Request message and/or SA1-AP Context Modification message, meaning that the UE is authorised to use ProSe.
    For X2-based handover, the source eNodeB includes a "ProSe authorised" indication in the X2-AP Handover Request message to the target eNodeB, or by MME in the Path Switch Request Ack message.

## Slide 18: EPC-level Discovery-General
Applicability
  EPC-level Discovery applies to non Public Safety UEs
  No roaming support for EPC-level Discovery in rel.12
General concept
  EPC-level ProSe discovery can be used independently or in conjunction with EPC support for WLAN direct discovery and communication when EPC support for WLAN direct discovery and communication is requested as part of the EPC-level ProSe discovery procedure.
  EPC-level Discovery is only used for restricted discovery in rel.12
  In rel.12 there are no procedures defined to use EPC-level Discovery as prelude of ProSe Direct Discovery
    Direct Discovery and EPC-level Discovery are independent features
Identities
  EPC ProSe Subscriber ID
  Application Layer User ID
  Application ID

## Slide 19: EPC-level Discovery- Overall procedure
1. UEs perform UE registration for ProSe with the ProSe Function residing in their respective Home PLMNs;
2. UEs perform application registration for ProSe with the ProSe Function residing in their respective Home PLMNs;
3. UE A makes a proximity request for UE B, i.e. requests that it be alerted for proximity with UE B (possibly indicating a window of time during which the request is valid). In response, ProSe Function A requests location updates for UE A and UE B. These location updates can be periodic, based on a trigger, or a combination of both. To request location updates for UE A, ProSe Function A contacts SUPL Location Platform (SLP) A. To request location updates for UE B, ProSe Function A contacts ProSe Function B, which requests location updates for UE B from SLP B;
4. The UEs' locations are reported to their respective ProSe Functions intermittently. ProSe Function B forwards UE B's location updates to ProSe Function A based on the conditions set by ProSe Function A. Whenever ProSe Function A receives location updates for UE A and/or UE B, it performs proximity analysis on UE A and UE B's locations;
5. When ProSe Function A detects that the UEs are in proximity, it informs UE A that UE B is in proximity and (optionally) provides UE A with assistance information for WLAN direct discovery and communication with UE B.
ProSe Function A also informs ProSe Function B, which in turn informs UE B of the detected proximity and (optionally) provides UE B with assistance information for WLAN direct discovery and communication with UE A.
More details for the procedures in Annex

## Slide 20: EPC support of WiFi Direct - General
Applicability
  Interworking with WiFi-Direct applies to non-Public Safety UEs
General concept
  EPC may decide to enable two or more ProSe-enabled WLAN-capable UEs to directly communicate using WLAN technology.
  This decision can be taken, when the EPC network supports EPC-level ProSe discovery and becomes aware that two or more UEs are in close proximity, or when the EPC network knows that UE-A requests to communicate with UE-B which is in close proximity of UE-A.
Identities
  WLAN Link Layer ID

## Slide 21: Interworking with WiFi-Direct - trigger
1. The ProSe Function decides to trigger UE-A and UE-B to establish a WLAN direct group under the control of the network.
2. The ProSe Function sends a WLAN Direct Group Setup Request (Assistance Information) to UE-A. The Assistance Information is a set of parameters which can expedite the establishment of the WLAN direct group and enables the EPC network to control the operating parameters of the WLAN direct group. The Assistance Information content depends on the WLAN technology. If UE-A accepts the request and the offered Assistance Information, it responds with a WLAN Direct Group Setup Response. This response may include parameters for the WLAN direct group proposed by UE-A (e.g. an operating channel).
When EPC support for WLAN direct discovery and communication is used in conjunction with EPC-level discovery, the assistance information for WLAN direct discovery and communication is provided as part of the Proximity Alert procedure.
3. The ProSe Function sends also a WLAN Direct Group Setup Request (Assistance Information) to UE-B. The Assistance Information in the request may take into account the parameters proposed by UE-A in step 2b.
4. The two UEs establish a WLAN direct group and may start communicating in WLAN direct mode.

## Slide 22: Interworking with WiFi-Direct – Assistance info
EPC needs to supply some or all of the following items as part of the Assistance Information:
  SSID: The SSID to use for Wi-Fi P2P operation.
  WLAN Secret Key: The pre-shared key to be used by UEs to secure their Wi-Fi P2P communication. This is used by UEs as the Pairwise Master Key (PMK).
  Group Owner indication: If set, the UE should implement the Group Owner (GO) functionality specified in the Wi-Fi P2P specification. The UE implementing this functionality essentially becomes an AP that transmits Beacons with the P2P Information Element and accepts associations from other Wi-Fi P2P devices or from legacy Wi-Fi devices (those not implementing the Wi-Fi P2P functionality). If not set, the UE should behave as a Wi-Fi P2P client that attempts to discover and associate with a GO.
  P2P Device Address of self: This is the WLAN Link Layer ID to be used by UE to advertise itself. A UE implementing the Group Owner and indicates the WLAN Direct device from which the GO should accept WLAN association requests. Association requests from all other WLAN devices should be rejected by GO.
  P2P Device Address of peers: This is the WLAN Link Layer ID to be used by UE to discover peer UEs. A UE implementing the Group Owner should accept WLAN association requests only from devices that are in this list.
  Operation channel: The channel on which Wi-Fi P2P discovery and communication should take place.
  Validity time: The time period during which the content provided in the assistance information is valid.

## Slide 23: Thank You