## Slide 1: Network Exposure for IoT Platforms
Catalina Mladin, Convida Wireless

## Slide 2: Background
CN service exposure functionality via SCEF/NEF was designed to provide a standardized exposure of network services/capabilities and reduce the complexity of a variety of 3rd parties accessing different 3GPP CN functionality.
Service usecases showing that the functionality provided by the exposure functions (e.g.in 23.682) is required at SCS/AS/AF have already been agreed in SEES and AESE Wis.
SA6 specifies common capabilities for a service enabler architecture in SEAL, in order to be utilized by multiple verticals and applications.

## Slide 3: What functionality is exposed via SCEF/NEF?
A set of APIs for accessing CN services has been defined since Rel-15
What can the Service Layer and Applications do with the APIs?
Access internal capabilities of the core network
  Location
  Reachability ….
Assist services that are already in the core network
  Sleep
  Communication Patterns ….
Coordinate its activity with the core network
  Network Congestion Reports
  Schedule Background Data Transfer …
Exchange Small Data Packets
  SMS
  Non-IP
The Cellular Core Network already knows a lot about the device. Network Applications should leverage network services whenever possible (thus asking the device to do less).
Application Servers, together with the Service Layer, provide underlying network abstraction along with the services to the customer facing Application and Devices, e.g. data storage, device management, location services, data analytics, charging, discovery, etc.
.. so that Application Servers are enabled to provide Value–add functionality, e.g.:
Deal with long sleep times or long transmission delays.
pre-plan UE activity whenever possible (e.g. background data transfers).
etc.
Why?

## Slide 4: How
By getting information from CN
The core network generally knows:
  where devices are located
  when they are in deep sleep
  when they are available
  when they lose connectivity
  when they are roaming
  when the SIM card is moved to another device
This is all information that Network Applications can get from the device.
However, we want to minimize signaling/messaging from the device.
It is more efficient to have Network Applications use Exposed Network Services to obtain this information.
By giving information to CN
The core network does not generally know:
  How often a device needs to be available
  how long it can buffer downlink data for sleeping device
  how much downlink data it should buffer for sleeping devices
This is all information that the Network can get from the device.
However, we want to minimize signaling/messaging from the device.
The Server can provide this information to the network

## Slide 5: Existing 3GPP work, stages 1-3
In 5G: NEF
    Stage 2: TS 23.502
    Stage 3: TS 29.522 (Nnef)
  “NEF is integrated with SCEF as a combined SCEF+NEF” (23.502, clause 5.2.6.12)
  “Procedure {xyz} as described in 29.122 shall be applicable in 5GS with […] description of SCEF applies to NEF” (29.522 clause 4.4)
    {xyz} applies to: Monitoring, Device triggering, Background Data Transfer, CP Parameter Provisioning, PFD Management, changing the chargeable party, AF session with required QoS, MSISDN-less Mobile Originated SMS, Network Configuration Parameters Provisioning, NIDD, RACS Parameter Provisioning, Enhanced Coverage Restriction Control
WIDs:
  SEES (Service Exposure and Enablement Support) (rel-13) SP-130505
  AESE (rel-13) SP-140704
  Under Rel-13 Features on Internet of Things (IoT)
In 4G: SCEF
    Stage1: 22.853
    Stage 2: TR 23.708, TS 23.621
    Stage 3: TS 29.122 (T8; SCEF-AS)

## Slide 6: SEAL & exposure functions
All SCEF/NEF APIs are currently exposed to AS. Therefore, exposure functionality via SEAL is useful for providing:
    VAL server implementation simplification and/or providing abstraction of functionality needed by multiple verticals or general-purpose servers.
    Optimizations/services to the CN, including consistency of AS influence on CN functionality.
    Capabilities for implementing the exposure functionality while allowing the requirement for PLMN operator service agreement to be maintained at SEAL provider level.
    For all cases, the choice of using the SCEF/NEF APIs directly by VAL Servers remains available.

## Slide 7: a. Exposure services across verticals
Example: Smart City platform which may include:
  V2X, FFApp, but also..
  IoT, Media, etc. … and may include
  Edge deployments
If several VAL servers in this deployment use location & group functionality from SEAL server (abstracted), why should they “learn 3GPP” to implement functions that require more CN knowledge?
VAL can use SCEF/NEF directly. Why use CAPIF exposure provided by SA6?
    Assumption: other SA6 services are being used, which justifies the use of CAPIF. Generally, when implementing other SA6 functionality, SEAL basic functions need to be implemented (although there is no mandate).
    By exposing via SEAL, we have the option of providing some value-add functions. At a minimum, the SEAL function is abstraction across multiple verticals. Transparent exposure remains available (as specified) when no value-add functions needed.

## Slide 8: b. CN resource optimizations or CN functional influence
Network Configuration Parameters (NCP) Provisioning, some monitoring, change of chargeable party, CP provisioning, etc. influence CN functionality or require CN resources. Add-on SEAL functionality around these capabilities can simplify VAL implementation and optimize CN influence.
Example: NW configuration for same UE can be affected by multiple AS/AFs and be provided though multiple mechanisms (NCP & monitoring). If those AS/AFs are part of the same platform leveraging SA6 services, achieving a unified and service-optimized configuration, before configuring the network, is optimal for both network and UE.
TS 23.682 : […] if the subscribed periodic RAU/TAU Timer was previously set by a different Monitoring Request […] for the same UE then, depending on operator configuration, the HSS either performs step 8 to reject the Monitoring Request with an appropriate Cause or accepts the request. If the HSS accepts this request, then it cancels the previously accepted Monitoring Request.

## Slide 9: c. Service agreement is preferred at SEAL provider level
Example: background data transfer
  End-user usecase agreed in SEES WID
  Pre-provisioned info about BDT policy is required (i.e. reference to a charging rate)
  We don’t want that pre-provisioning to be needed for each AS, if they belong to a common SEAL platform
  We want the SEAL to be able to perform BDT management as “group management” – UE groups, BDT window grouping, etc.

## Slide 10: Proposal
Proposal: Include capabilities to leverage the 5GS northbound interface in SEAL to ensure consistency in the use of the exposed 5GS capabilities
  To narrow scope:
    Start with features introduced by SEES and AESE, e.g. enabling IoT platforms. Add horizontal platform usecases as needed.
    Use criteria such as
      When AS implementation simplification or abstraction are needed - more than one vertical or “general purpose” AS
      When optimizations/services to the CN needed or when AS influence CN functionality
      When PLMN operator service agreement is preferred at SEAL provider level
  Requirements: 22.101 clause 29 on Service Exposure already covers everything, in conjunction with the SEES and AESE work.