## Slide 1: Transferring bearer pre-emption rate limitation information from MME up to the MC AS (related to S6-220008/R3-216196)
15.02.2022
Nokia

## Slide 2
TS 23.401 clause 5.4.1 Dedicated bearer activation
step 1 is triggered by an IMS/MC server request
RAN3 has agreed to introduce a new cause value for eNB to inform MME when the number of bearers to pre-empt exceeds the eNB’s processing limit, i.e. sent in step 7 (R3-216088)
Step 12. If the dedicated bearer activation procedure was triggered by a PCC Decision Provision message from the PCRF, the PDN GW indicates to the PCRF whether the requested PCC decision (QoS policy) could be enforced or not, allowing the completion of the PCRF-Initiated IP‑CAN Session Modification procedure
3GPP SA2: TS 23.401
General Packet Radio Service (GPRS) enhancements for Evolved Universal Terrestrial Radio Access Network (E-UTRAN) access

## Slide 3
TS 29.274 Create Bearer Response contains a RAN/NAS Cause at Bearer Context level
RAN/NAS Cause | CO | If the bearer creation failed, the MME shall include this IE on the S11 interface to indicate the RAN cause and/or the NAS cause of the bearer creation failure, if available and if this information is permitted to be sent to the PGW operator according to MME operator’s policy. If both a RAN cause and a NAS cause are generated, then several IEs with the same type and instance value shall be included to represent a list of causes. The SGW shall include this IE on the S5/S8 interface if it receives it from the MME.
i.e. the S1AP rejection cause reaches the PDN GW
3GPP CT4: TS 29.274
3GPP Evolved Packet System (EPS); Evolved General Packet Radio Service (GPRS) Tunnelling Protocol for Control plane (GTPv2-C); Stage 3

## Slide 4
How does the PGW (PCEF) inform PCRF the outcome of the “IP-CAN session Modification”?
TS 29.212 clause 4.5.12
If the RAN-NAS-Cause feature is supported and as part of any of the procedures described in this clause the PCEF receives from the access network some RAN/NAS release cause(s), ….., the PCEF shall also provide the received cause(s) in the Charging-Rule-Report AVP. If RAN-NAS-Cause feature is supported the PCEF shall provide the available access network information within the 3GPP-User-Location-Info AVP (if available), TWAN-Identifier (if available and Trusted-WLAN is supported), User-Location-Info-Time AVP (if available) and 3GPP-MS-TimeZone AVP (if available).
Charging-Rule-Report ::= < AVP Header: 1018 >
*[ Charging-Rule-Name ]
*[ Charging-Rule-Base-Name ]
[ Bearer-Identifier ]
[ PCC-Rule-Status ]
[ Rule-Failure-Code ]
[ Final-Unit-Indication ]
*[ RAN-NAS-Release-Cause ]
*[ Content-Version ]
*[ AVP ]
TS 29.213 specifies
If the RAN-NAS-Cause feature is supported and the PCRF received the access network information from the PCEF/BBERF due to bearer termination or unsuccessful bearer establishment/modification, the PCRF shall include in the RAR command the access network information within the 3GPP-User-Location-Info AVP (if available), TWAN-Identifier (if available and Netloc-Trusted-WLAN feature is supported) User-Location-Info-Time AVP (if available), 3GPP-SGSN-MCC-MNC AVP (if location info is not available) and/or 3GPP-MS-TimeZone AVP (if available). Additionally, if the PCRF received from the PCEF the RAN cause and/or NAS cause, TWAN cause or untrusted WLAN cause due to bearer termination, the PCRF shall provide the received cause(s) in the RAN-NAS-Release-Cause AVP in the RAR command.
A.11 Handling of RAN/NAS release cause values
If the P-CSCF is required by operator policy to provide the RAN/NAS release cause information, it includes this information in the corresponding SIP message as specified in 3GPP TS 24.229 [17] when received from the PCRF (see clause 4.4.4, 4.4.6.1, 4.4.6.2, 4.4.6.3 and 4.4.6.7).
3GPP CT3 TS 29.212 (Policy and Charging Control (PCC); Reference points)
3GPP CT3 TS 29.213 (Policy and charging control signalling flows and Quality of Service (QoS) parameter mapping)

## Slide 5
The MC service (IP-CAN Session modification) acts as an SCS/AS (or AF) via T8/N33 (29.122, using AsSessionWithQoS I assume) or via Rx/N5 (29.214).
In both cases (i.e. 29.122 and 29.214) the RAN-NAS-cause can be sent to the MC service server.
In 29.214 it is the RAN-NAS-Release-Cause AVP and in 29.122 it is the ranNasCause attribute, which both link to a definition of the cause in 29.212.
29.214 4.4.6.3 says (among others):
“If the RAN-NAS-Cause feature is supported and the PCRF received the access network information from the PCEF/BBERF due to bearer termination or unsuccessful bearer establishment/modification, the PCRF shall include in the RAR command the access network information within the 3GPP-User-Location-Info AVP (if available), TWAN-Identifier (if available and Netloc-Trusted-WLAN feature is supported) User-Location-Info-Time AVP (if available), 3GPP-SGSN-MCC-MNC AVP (if location info is not available) and/or 3GPP-MS-TimeZone AVP (if available). Additionally, if the PCRF received from the PCEF the RAN cause and/or NAS cause, TWAN cause or untrusted WLAN cause due to bearer termination, the PCRF shall provide the received cause(s) in the RAN-NAS-Release-Cause AVP in the RAR command.”
In 29.122 the ranNasCause attribute is in the FailureCause of the MonitoringEvent API (->Event Exposure), which can be subscribed by the MC service server.
3GPP CT3 TS 29.214 (Policy and charging control over Rx reference point)
3GPP CT4 TS 29.122 (T8 reference point for Northbound APIs)