## Slide 1: SEAL Registrar
Sapan Shah
Samsung

## Slide 2: VAL server registration
Received comments in previous meeting
  List all requirements/configurations from existing procedures which SEAL server needs
  Provide architecture requirement to have VAL server registers with SEAL server
Submitted contribution in SA6#50-e: S6-222116

## Slide 3: Location Management Server
Location reporting trigger can be fetched by SEAL location management client (SLM-C) or it can be made part of user profile.
  Ref: Clause 9.3.3.2
    “NOTE 1: The location reporting configuration information can be made part of the user profile, in which case the sending of the message is not necessary.”
  VAL server provides triggers to SEAL location management server (SLM-S) so that SLM-C can fetch the triggers
  But there is no procedure – how VAL server provides or updates user profile to set location triggers
Clause 9.3.3.2 Fetching location reporting configuration
  What if the location management client sends location reporting configuration request message to the location management server even before VAL server provides triggers for the UE?
  Location management server can provide default triggers and information required in the location report to the client. From where location management server will get such information?

## Slide 4: Group Management Server
Clause 10.3.3 - Group creation
  “During the group creation, the group management server creates and stores the information of the group. The group management server performs the check on the policies e.g. maximum limit of the total number of VAL group members for the VAL group(s).”
Clause 10.3.10.1 - Temporary group formation within a VAL system
  “The group management server checks whether temporary group formation operation is performed by an authorized VAL user, based on group policy. ”
Clause 10.3.6.1 - Store group configurations at the group management server
  “The group management server may have some pre-configuration data which can be used for online group configuration validation”
It is not specified from where the Group management server gets group document template, default values and policies.

## Slide 5: Configuration Management Server
Configuration management server deals with UE configuration, User Profile and Service data.
It provides configuration to the configuration management client on their request.
It is not specified from where the Configuration management server gets all configurations for all VAL servers.
Architecture requirement:
  [AR-4.5.2-a] The SEAL shall enable configuring service specific configuration data applicable to vertical applications.

## Slide 6: Identity Management Server
TS 33.434 – clause 5.2.3 Identity management functional model
  “In order to support VAL user authentication, the SIM-S shall be provisioned with the VAL user ID and VAL service IDs (usage of VAL user ID and VAL service ID is described in clause 7 of TS 23.434 [2]). ”

## Slide 7: Key Management Server
TS 33.434 - Clause 5.3.1 General
  “A VAL server is provisioned with an access token scoped for SEAL key management services and is provided with each and every key management request to the SKM-S. ”
TS 33.434 - 5.3.2 SEAL KM Request message
  “The format and content of a key management record is defined and securely provisioned into the SEAL KMS by the VAL application or VAL service owner/operator. ”

## Slide 8: Network Resource Management
Clause 14.3.2.6 Resource request (Unicast resource management with SIP core)
  “NOTE: When this information element is not included, the NRM server considers default VAL service requirement for the unicast resources.”
Clause 14.3.4.2.2 Procedure (Unicast QoS monitoring notification procedure)
  “If local MBMS is requested in step 1, the NRM server uses the local MBMS information provided by VAL server in step 1 or the local MBMS information configured locally in the NRM server to activate the MBMS bearers. ”

## Slide 9: Network Slice Capability Enablement
Clause 16.3.2.3 Procedure for VAL server-triggered and network-based network slice adaptation for VAL application
  “The NSCE server processes the request and triggers the network slice configuration per VAL UE within the VAL Application.”

## Slide 10: CAPIF for SEAL
From CAPIF perspective:
  The VAL server acts as CAPIF's API invoker as specified in 3GPP TS 23.222 [8].
  The SEAL server acts as CAPIF's API exposing function as specified in 3GPP TS 23.222 [8].
Procedure: Onboarding the API invoker to the CAPIF
  This API does not contain any API Invoker specific configuration
    Here API Invoker is VAL server
There is not procedure from CCF to share API invoker specific configuration to the AEF (i.e. SEAL server).

## Slide 11: Architecture Requirements
The SEAL shall enable the VAL server to register itself with SEAL server.
The SEAL shall enable the VAL server to provide service specific configuration data to SEAL servers applicable to vertical applications.

## Slide 12: Possible Options
Scenario:
  VAL Server-A wants to use SEAL Server-1 and -2.
  VAL Server-B wants to use SEAL Server-1, -2 and -3.
  VAL Server-A wants to use SEAL Server-2 and -3.
Option 1) Each VAL server registers separately to each SEAL server which it wants to use.
  Multiple registration (in this scenario: 7 registration message exchanges)
  Burden to maintain each registration separately.
Option 2) SEAL Registrar
  Less number of registrations to maintain (total 3 in this scenario)
  SEAL registrar can act as an entry point to the SEAL service provider domain and can implement any specific policies
  SEAL service provider can use the single entry point to collect all usage related data (which can be used for charging – not within scope of SA6)

## Slide 13: Conclusion
It is proposed to conclude and agree upon
  Architecture requirements (as shown in slide#11)
  Solution Option 2 (as shown in slide #12)