## Slide 1: SA6 Rel-19 SID Proposal： FS_eLSAPP: Study on enhanced application layer support for location services
May, 2023
Liping Wu, CATT

## Slide 2: Outline
Rel-19 SID/WID Slide Template: FS_eLSAPP
Annex A: Use cases for value-added location services
Annex B: Use cases for dual-access/Multi-USIM location services

## Slide 3: FS_eLSAPP: Study on enhanced application layer support for location services-1/4
Continuation or New Item: Continuation
  In R16 and R17, the SEAL has introduced the basic Location management architecture serving the vertical applications, including the function model, procedure, information flow and reference points, etc.
  In R18, the 5G Fused Location Service(5GFLS) is introduced and agreed to obtain the UE location information from more sources to further improve the LCS QoS (e.g. accuracy, latency) to meet the vertical application requirements.
Study Item/Work Item/Both: Both
Source of requirements:
  Leftover from R18 5GFLS SID: Value-Added Location Services
  Align with AF requirements specified by SA2(TS23.273 and TS 23.586)
  SA1 new requirements related to location services: Application enabler for UE location service over dual-access/network
Expected Output:
  SID: output is proposed to be a new TR
  WID: output is proposed to be a new TS, to be added to existing TS is also considered
Rel-19 SID/WID Proposal Slide Template

## Slide 4: FS_eLSAPP: Study on enhanced application layer support for location services-2/4
Anticipated start date/meeting: Aug,2023 SA6#56
Target Completion: Dec,2024 SA6#61, SA#104
Estimated TUs: 12 TUs (SID) + 8 TUs(WID)
Rapporteurship: Liping Wu, wuliping@cictmobile.com
Supporting IMs: CATT, ZTE, CMCC,vivo
Rel-19 SID/WID Proposal Slide Template

## Slide 5: FS_eLSAPP: Study on enhanced application layer support for location services-3/4
Description:
  Although in R16 and R17, the SEAL work has introduced the basic Location management architecture, and in R18 the 5GFLS is also been added to further improve the LCS QoS (e.g. accuracy, latency) to meet the requirements from vertical applications . However there are many value-added location service requirements from vertical applications cannot be met. Such as Location Alerting, Location tracing, History Trace request or playback, Heatmap, Location format mapping, Location information analysis, etc.
  The LMS functionalities should also align with the AF requests specified by SA2(TS23.273 and TS 23.586). Such as the Location service exposure, GNSS assistance data collection from AF, Ranging/Sidelink Positioning service requests from AF, etc.
  What’s more, SA1 has specified some new location related requirements in Rel-19. Such as UE location service over dual-access/network.
Goals:
  Identify the gaps between the service requirements for AF functionalities specified by SA2, new SA1 requirements, enabler for the value-added location service and the existing SEAL-LM architecture in application layer.
  Develop the SEAL-LM architectural enhancements mainly to support the above technical description based on the gap analysis.
  Study the key issue and related solutions for the enhanced location services.
Dependency on other working groups:
  SA2: The LCS expose function for AF is specified in TS 23.273 and TS 29.572. The Ranging/Sidelink Positioning function is specified in TS 23.586.
Impacts to 3GPP/Industry work if this is not accepted into Rel-19:
  Inconsistent work/functions for location services between SA2 and SA6.
  The value-added location services can’t be deployed and utilized in Industry.
Rel-19 SID/WID Proposal Slide Template

## Slide 6: Outline
Rel-19 SID/WID Slide Template: FS_eAPPLS
Annex A: Use cases for value-added location services
Annex B: Use cases for dual-access/Multi-USIM location services

## Slide 7: Use case 1: Geofencing&Location Alerting
The location management platform(e.g. LMS enhanced with location data analyzer) is monitoring the worker’s position constantly, if the worker strays into the dangerous areas(Electronic Fence area), there will be alarms triggered and the worker will be informed to leave the area quickly in time to protect their lives.
If the user’s position is different from the historical position or always keep still, an alarm will be triggered automatically to protect the safety of the user/equipment.
Location Management Platform
Electronic
Fence
Location
Alerting
Chemical Factory
Location data analyzer
Location Management service
Application Data analyzer

## Slide 8: Use case 2:Location information analysis
The location information analysis platform((e.g. LMS enhanced with location data analyzer) could analysis the customer’s location in the shopping mall and provides the customer’s stay period, visit frequency, hot spot shop, etc. to help the shopping mall to improve the business management level. E.g. some shops will be informed when the VIP customer arrived. Or customers will receive the promotion/coupons for all of shops in case they enter into the shopping mall.
To enable use case1 and use case2, the LM server may be enhanced to communicate with the internal “location data analyzer” or the outside “Application data analyzer”( e.g. just like the NWDAF specified in SA2) to meet the value-added service requirements.
Users’ Location information analysis platform
Shopping Mall
Monitor the customers’ location
Location data analyzer
Location Management service
Application Data analyzer
Notes: 23.586 ranging TR slidelink UE-UE

## Slide 9: Outline
Rel-19 SID/WID Slide Template: FS_eAPPLS
Annex A: Use cases for value-added location services
Annex B: Use cases for dual-access/Multi-SIM location services

## Slide 10: Use case: Dual-access/Multi-SIM location services for UE
LMC/UE may report location reports to the LM server over two 3GPP access through 3GPP core network. Two access could be e.g., one access using NR and another access using satellite, or two satellite access (LEO and MEO/GEO). And LMS may indicate LMC/UE the access type/network based on the service requests, UE capabilities, etc.
LMS
(FLF)
3GPP core network
Satellite
gNB
Multi-SIM devices associated to one person
LMS
(FLF)
3GPP
network system
If one person takes the mobile phone and wears the watch at the same time, both of them could report the person’s location information to the LMS separately. Then LMS could estimate them to get an accurate person’s location.
Further, there is no need for LMS to obtain the watch position separately, as the position for watch can be replaced by the position for mobile phone in case they are located in same place. And vice verse.

## Slide 11: Thanks!