## Slide 1: Discussion on AC registration's usefulness
Nishant Gupta
Delegate, Qualcomm

## Slide 2: Outline
Comparison between AC registration and EEC services subscription
Conclusions and proposal

## Slide 3: AC registration vs. EEC services subscription
! Not notifying the AC immediately risks resource wastage over EDGE-1/4 since the retrieved information tends to get stale due to factors such as UE mobility or EAS KPI changes.
 | AC registration | EEC services subscription
AC profile | Provides AC profile to the EEC | Provides AC profile to the EEC
Preferred ECSP information | Provides preferred ECSP information to the EEC | Provides preferred ECSP information to the EEC
Pre-fetch information over EDGE-1/4 | EEC can use the information provided in the registration to request information over EDGE-1 and EDGE-4. | EEC can use the information provided in the registration to request information over EDGE-1 and EDGE-4.
Notify AC | EEC cannot immediately notify the AC since AC registration does not provide notification related information. | EEC can immediately notify the AC
Optionality | Not a prerequisite for other EDGE-5 operations | AC must subscribe before sending ACR trigger requests over EDGE-5.

## Slide 4: Conclusion
AC registration and EEC services subscription are functionally equivalent
  except that the EEC can not notify the AC with just AC registration.
AC registration is not mandatory
  Neither it is a prerequisite for any other EDGE-5 operation; while EEC services subscription is.
AC registration is redundant and risks sharing stale information to the AC.
Proposal: Remove AC registration.