## Slide 1: Discussion on EAS bundles
Nishant Gupta
Delegate, Qualcomm

## Slide 2: Outline
Requirements from SA4
Co-deploy and Co-migrate
Proposals
Summary

## Slide 3: Requirements from SA4 (S6-230509)
All three scenarios correspond to valid uses.
Case 1 does not necessarily require co-deployment or co-migration. However, there may be application-specific state maintained in the UE that makes co-deployment and co-migration desirable.
Case 2 shows strong affinity between the two EAS instances and therefore a good reason to co-deploy and co-migrate them.
Case 3 is like Case 2, and the conclusion is identical.
EASs may not have similar KPIs and requirements

## Slide 4: Co-deploy
Requirement for co-deployment comes from the ASP, and should be shared with ECSP management system e.g., through the EAS profile.
KPI requirements may or may not be same for the bundled EASs.
Conclusion: EAS bundles may be spread across EDNs, and therefore registered on different EESs.

## Slide 5: Co-migrate
Case 1 – AC can provide the requirement for co-migration, since AC manages the EAS connections individually.
Case 2 – AC cannot provide co-migration requirement, since it is not aware of EASy. EASx needs to share the requirement. EASx can provide the requirement.
Case 3 – Either AC or EAS can provide the requirement.
Similar conclusions apply to coordinated EAS discovery, essential for coordinated migration.

## Slide 6: Proposal 1: EAS bundle types
Different deployment scenarios will have different requirements and different constraints, e.g., bundle requirements can be provided only by the EAS in case 2.
Proposal: Introduce ‘EAS bundle type’ in ‘Bundle information’ to identify the different scenarios
Proxy
Composite
Direct

## Slide 7: Proposal 2: Bundle requirements
For Direct bundles, only AC can provide bundle requirements
For Proxy bundles, only EAS can provide bundle requirements.
For Composite bundles, either AC or EAS can provide bundle requirements.
Proposal: Include bundle requirements in the EAS profile and consequently in the EES profile to support proxy and composite bundles.

## Slide 8: Proposal 3: ACR involving multiple S-EESs
Once EAS bundle and bundle’s requirements are known:
  In case of ‘Direct bundles’ and ‘Composite bundles’
    AC/EEC are aware of bundled EASs, their registrar EESs, and bundle requirements.
    AC/EEC can trigger ACR detection with all EESs involved in the EAS bundle.
  In case of ‘Proxy bundles’
    EASx is aware of other bundled EASs and the bundle requirements
    EASx can trigger other EASs to trigger ACR detection with their registrar EESs.
Proposal: Add appropriate description in the specification explaining AC/EEC and EAS behavior for handing ACR. No other change is required.
Trigger ACR detection
Trigger to initiate ACR detection
Trigger ACR detection

## Slide 9: Summary
Different deployment scenarios have different requirements and different constraints.
Proposal 1: Introduce ‘EAS bundle type’ in ‘Bundle information’ to identify the different scenarios
In certain deployments, only EAS can provide EAS bundle information.
Proposal 2: Include bundle requirements in the EAS profile and consequently in the EES profile.
AC/EEC and EAS can ensure that the ACR is detected for all EASs that are part of the EAS bundle.
Proposal 3: Add appropriate description in the specification explaining AC/EEC and EAS behavior for handing ACR. No other change is required.