## Slide 1: Options for CAS to EAS ACR for CESless Architecture
Yonatan Shiferaw
KPN

## Slide 2: Background
Clause 8.8.2A Updates procedures for the scenarios in TS 23.558 for ACR between EAS and CAS
  For an ACR from EAS to CAS, DNS based solution is used to discover CAS.
  But for an ACR from CAS to EAS, the rich SA6 way of discovering EAS should be used rather than DNS.
EES is essential for utilizing SA6 specified rich way of Rel-17 T-EAS Discovery (TS 23.55)
  EES plays a key role in the discovery procedures as discovery requests are sent to an EES whether the request originates from EEC, S-EAS or S-EES (when the T-EES is different).
  Therefore, for CAS to use the Rel-17 SA6 specified EAS discovery methods and utilize EDGE-14, it needs to know the EES before the discovery.
  The solutions to address this are captured in TR 23.700-98 Clause 7.25.2.2.6.
Configuring the CAS with EES endpoint information (like in TS 23.558 clause 8.4.3.2.2) will not work because there is no fixed EES for CAS and the EES changes with the mobility of the UE.

## Slide 3: Options for CAS to know the EES
For the CAS to trigger an ACR it needs to know both the EES endpoint and the UE Identifier to use for discovery and ACR triggering.
  Option 1: Retrieves the EES via the AC by triggering service provisioning in the EEC and receiving back the EES endpoint and UE Identifier. Regular S-EAS decided ACR scenario can be used where the CAS acts as an S-EAS to the provisioned S-EES.
  Option 2: the old EES where the EEC was connected to before moving to the CAS is used for the CAS as S-EES. The CAS retrieves this old S-EES along with UE Identifier via the AC. After this, Regular S-EAS decided ACR scenario can be used where the CAS acts as an S-EAS to the old S-EES. When the EEC is unreachable because it moves back to a different EDN, the SEAL notification service can be used to send notifications to the EEC.

## Slide 4: Proposals
Option 1: S6-231918 which was postponed last meeting. This option works also when the EEC moves from CAS to EEC for the first time.
  When triggered by the CAS via the AC the EEC performs Service Provisioning and shares the EES (called the S-EES) endpoint along with the UE ID to the CAS.
  The CAS performs discovery on the S-EES using the UE ID and performs ACR.
Option 2: S6-231917 and S6-231919 works when the EEC has moved from an Edge to a CAS and now returning to an Edge.
  The old S-EES endpoint information and the UE ID is shared via the AC to the CAS. The CAS then connects to the old S-EES and performs discovery. (S6-231919 )
  If the EEC moves back to a different EDN, the EEC may not be reachable to the S-EES. Therefore, it is proposed to have the option of using the SEAL notification service to send notifications to the EEC .
  The EEC subscribes to the SEAL notification service and receives UE ID to share with the CAS before it moves to the CAS. (S6-231919)