## Slide 1: MSGin5G Message Delivery to MSGin5G UE
Jerry Shih
Jerry.shih@att.com
Liu Yue
liuyueyjy@chinamobile.com

## Slide 2: UE state transition
UE is connected to its hosting MSGin5G Server to access MSGin5G services.
A UE is either registered with its hosting MSGin5G Server for MSGin5G service or not.
The UE states are synchronized both on the MSGin5G UE and its hosting MSGin5G Server.

## Slide 3: Message delivery at MSGin5G Server
UE needs to register with its hosting MSGin5G Server for message delivery.
MSGin5G Server starts message delivery procedure when the UE state is registered.
When UE state is not registered the MSGin5G Server will
  Inform the UE a message is waiting, if supported (i.e. initiates a device trigger request via the SCEF/NEF) and available
  Check if S/F is requested by the sender:
    If YES, queue the message and wait for the next delivery opportunity.
    If NO, drop the message or apply local implementation specific.
MSGin5G Server message delivery could be further refined (granularity) with optional “communication availability” information provided by the UE during registration and the MSGin5G Server will schedule the message delivery based on this information.
If message delivery failed, the MSGin5G Server will:
  Discard the message or apply local implementation if S/F was not requested, or
  Apply S/F procedure and wait for the next delivery opportunity.
MSGin5G Server sends the delivery report back to the sender, if requested.

## Slide 4: Message delivery flow at the MSGin5G Server
When message delivery failed, a re-try will take place. How many failed re-tries before stops delivery attempt is local implementation.

## Slide 5: Summary
Add slide 4 flowchart to Clause 7.3 (new) as informative information.
Modify clause 8.3.3 accordingly.