## Slide 1: SA6 Rel-19: Discussion on Network enabler for XR services
Oct, 2023
Shaowen Zheng (CMCC)

## Slide 2: Outline
Background and motivation
Potential use case
Potential Objective

## Slide 3: Background and motivation
SA1
R17: tactile and multi-modal communication service
R18: FS_Metaverse
R18: XRM
R18: FS_SmarTAR
R18: MeCAR
R18: SR_MSE
R16: FS_5GXR
R17: FS_ 5GSTAR
provide policy(ies) for flows associated with an application
apply 3rd party provided policy(ies).
precise location triggered information provisioning,
management of the spatial anchor
management of the digital assets
...
AF information provisioning: common ID, PDU Set related assistance information including PDU Set QoS parameters, Burst periodicity, Description of Service Protocol.
Network information exposure: congestion level information, Data rate, delay difference and round trip delay of QoS flow, Estimated bandwidth.
  XRM in SA2 studies the key issues, solutions on how to support XR and advanced media services from 3gpp architecture perspective. SA4 focus more on the application layer interaction between the UE and video/audio media service. However, to enable a variety of XR services not limited to video/audio communications , specific support by network enabler layer based on the 3GPP system may be required.
SA4
SA2
Notes: SA4 的关系；
对比

## Slide 4: The tactile and multi-modal communication service
The tactile and multi-modal communication service may include multiple types of flows from multiple type of dervices, e.g. video/audio stream, and haptic or sensor data for more immersive experience
Requirement from 22.261 for tactile and multi-modal communication service:
  The 5G system shall enable an authorized 3rd party to provide policy(ies) for flows associated with an application. The policy may contain e.g. the set of UEs and data flows, the expected QoS handling and associated triggering events, other coordination information.
  The 5G system shall support a means to apply 3rd party provided policy(ies) for flows associated with an application.
Possible objective:
    Support for 3rd party policy provisioning and management to provide policy(ies) to the 5GC for flows associated with the XR services for information extraction and provisioning to the 5GC. (such as Multi-modal Service ID， PDU set related information provisioning)
    Apply 3rd party provided policy(ies) for control of flows associated with an application (e.g., PDU/flows coordination, delay difference handling, QoS scheduling, buffering, transmission quality guarantee etc..)
    Guarantee seamless XR streaming over 3GPP or non-3GPP access(e.g., device connecting to the 5G network directly and undirectly), and including aspects of data pre-processing, or triggering user plane management like MA-PDU and/or Multi path utilization etc;
Notes:   Customer Premise Equipment/UE
  extract the PDU Set related information in the RTP header)
  Provisioning of associated XR Services information in the 5GC with the help of an enabler, such as Multi-modal Service ID provisioning;
  Utilization of 3rd party provided policy(ies) for control of flows associated with an application (e.g., PDU/flows coordination, delay difference handling) (可以基于SEALDD已有的服务，比如是redundant transmission， bandwidth control， data transmission quality guarantee，或者SA2的 redundant transmission, PDU set identifier based, ECN/congestion information based solutions 或者自己的QoS scheduler. Based on the, something more could be done.

## Slide 5: Immersive Live concert
Large amount of computing resouces is needed to perform real-time processing for audio, video, and interactive data, etc. Considering different customers will use terminals e.g. XR glasess with different brands and different processing capabilities, some of the glasses will not have enough computing resources to perform the real-time rendering. Through split rendering, most of the computing work task can offload to the network, the high speed and low latency transmission provided by 5G system can cooperate with the edge cloud side for real-time rendering, and combine with the local optimized rendering of the XR terminal side to provide the immersive and unbounded XR experience.
Table 7.6.1-1 KPI Table for additional high data rate and low latency service
Use Cases | Characteristic parameter (KPI) |  |  | Influence quantity | 
 | Max allowed end-to-end latency | Service bit rate: user-experienced data rate | Reliability | UE Speed | Service Area(note2)
Cloud/Edge/Split Rendering(note 1) | 5ms(i.e. UL+DLbetween UE and the interface to data network) (note 4) | 0,1 to [1] Gbit/s supportingvisualcontent(e.g. VR based or high definition video)with 4K, 8K resolution and up to120 frames per second content. | 99,99 % in uplink and 99,9 % in downlink (note 4) | Stationary or Pedestrian | Countrywide
Requirement from SA1:
Requirement for SA6:
  Whether and how the enabler could help to meet the high data rate and low latency requirement of XR service via spliting the computing and/or rendering task based on the collected location and network status
Possible objective:
  Split computing, principle of computing task/content splitting, steering to enable split rendering, split modeling etc. (maybe based on the EDGEAPP architecture)
  KPI guarantee, and XR services related information measurement and exposure based on the enhancement of SEALDD (e.g. traffic periodicity, Packet Delay Variation among the associated flows etc.);
Notes: 丢包
资源预留
整形；
这种情况需要考虑，EAS bundle以后，有不同的requirement怎么办，
比如说，可能一个EAS还能被原来的EAS服务，但是两个EAS要求严格的时延，类似XR业务，所以要综合考虑如何进行bundle EAS relocation
有没有一种情况是，同一个XR业务，但是不同的EAS服务，然后split computing??

## Slide 6: Potential objectives
Identify architecture requirements and solutions for architecture enhancement of SEAL/SEALDD to support the XR services;
Identify key issues, and solution recommendations to enable capabilities for XR services including:
Abstraction of provisioning processes to help 3rd party provide policy(ies) to the 5GC for flows associated with one or more XR services, etc.
Apply 3rd party provided policy(ies) at Application enabler layer for control of flows associated with an application, and/or among multiple applications;
Information measurement, exposure and KPI guarantee for XR services based on the enhancement of SEALDD (e.g. traffic periodicity, Packet Delay Variation among the associated flows etc.);
Notes: XR service 打卡看看
分一分哪些是XR specific
动态的分离渲染可行性；实现上

## Slide 7: Added Value from SA6
SA4 focuses on the media processing aspect (i.e., the codec, rendering, etc.), and the application layer transport mechanism (i.e., the RTC etc.), and SA2 focuses on the transmission based on 5G connection with little knowledge of the service(s).
What SA6 could provide as value-added services including but not limit to:
  Help with multi-service coordination, by coordinating the traffic flows that has dependency. For example, to coordinate the robotic control data and the camera output.
  Help to provide a consistent service experience on devices with varying capabilities by providing more transmission guarantee services in the SEAL/SEALDD, which could lighten the burden of the transmission path monitoring and adaptation of the application in the user device.
SA4 scope
enabler for XR service
5GC
PCF/NEF
UE 1
VAL 2
UPF
CAPIF
XR client
SEALDD
client
5G Msd
VAL 1
SA2 scope
SA6 scope

## Slide 8: Estimated TU Calculation
template
Meeting | FS_AEXRS (SID) | AEXRS(WID) | Note
SA6#55 (May) | SID Proposal |  | 
SA6#56 (Aug) | SID Proposal |  | 
SA6#57 (Oct) | 1TU |  | 
SA6#58 (Nov) | 1TU |  | 
SA6#59 -Adhoc(Jan) | 1TU |  | 
SA6#59 (Feb) | 1.5TU | WID proposal | 
SA6#60 (Apr) | 1.5TU | 1 TU | Overlap with Study and work item
SA6#61 (May) | 1TU (Study completes) | 1 TU | 
SA6#62 (Aug) |  | 1 TU | 
SA6#63 (Oct) |  | 1 TU | 
SA6#64 (Nov) |  | 1 TU | 
Total | 7 TUs | 5 TUs | 12TUs

## Slide 9: Thanks