## Slide 1: Discussion on protection zone configuration
Catalina Mladin
Delegate, Convida Wireless LLC.

## Slide 2: Background
Solution #4 of the eV2X App2 study (i.e. 3GPP TR 23.700-64 clause 6.4) is for UE initiated request for VRU zones and has the following eval:
    “This solution addresses KI #1 and aspects of KI #2 and provides a procedure for a VAL client on a cyclist UE to request the creation of a dynamic protection zone via the VAE client. The VAE server checks with a VASS to authorize the request and if authorized, the VASS creates a protection zone based on the information provided by the VAE client. After the creation of the protection zone, the VAE server monitors the UE’s mobility information and updates the protection zone accordingly. If the VAE server detects the presence of other vehicular UEs in the updated protection zone, the VAE server sends a notification alert to the vehicular UE and includes V2P communication configuration information.
    Further agreement is needed for the scenario of this solution where UEs can initiate VRU protection zone creation.”
…and the following related conclusion:
    “For key issue#1, solution#2 is considered and solution#4 can be considered based on the agreement on the use of protection zones.”

## Slide 3: VRU protection zone Use Case
Provide complete trip planning for someone using a wheelchair.
Wheelchair + rider act as VRU in relationship to large vehicles.
At the same time, at various points (e.g. steps 4, 5, 6) the operator requires use of vehicular capabilities such as VRU high-risk zone to alert of pedestrian/bicyclist in vicinity (step 5), road hazard determination (steps 4, 6), etc.
Source: System Requirements Specification (SyRS) Atlanta Regional Commission ITS4US Deployment Project (https://rosap.ntl.bts.gov/view/dot/60127).
In addition to usecases and requirements, the document specifies that ‘the vision of the project is to provide users complete trip functionality with directions, conditions, and status on the links between trip legs that are personalized based on the user’s profile, while connecting the user to CV infrastructure to provide safer trips and more transportation network awareness.’

## Slide 4: Protection zone vs. VRU high-risk zone
VRU = Vulnerable Road User
VRU high-risk zone has not been defined explicitly,. It is defined implicitly by the ITS system, and as such (so far) it is relative to the ITS System, e.g., RSUs.
This usecase calls for a zone defined relative to and managed by the VRU, which would act to protect the VRU.
Alternative terminology proposed in study phase:
  Dynamic VRU high-risk zone
  UE-triggered dynamic VRU high-risk zone
  Protection zone
Alternative proposed now:
  Define “protection zone” as UE-specific and mapped to one or more dynamic VRU high-risk zone . Add “UE-triggered” as needed to clarify the functionality where the trigger is relevant.

## Slide 5: Highlights of associated contribution
Targets 3GPP TS 23.286 for Rel-19 as TEI-19
Aligned with 3GPP TR 23.700-64 solution 4, including pre-condition for “policy allowing support of UE protection zone configuration and support of UE/VRU-initiated requests.”
Reuses existing 5GS and SEAL LMS functionality for VRU high-risk zone
Terminology used:
  “protection zone” for requests within SA6 service layer. Adds definition/ clarification in text, as needed for awareness.
  “VRU high-risk zone” reused everywhere where existing functionality can be leveraged (e.g., notifications)

## Slide 6: Summary
SA6 is kindly asked to:
  Provide guidance on terminology
  Agree to work on the normative phase of this Rel-18 solution as part of TEI-19
  Discuss and agree to the related contribution.
  Thank you!

## Slide 7: Other resources
PROSPECT: PROactive Safety for PEdestrians and CyclisTs https://wayback.archive-it.org/12090/20190615063554/https://ec.europa.eu/inea/en/node/2806
ITS Action Plan (Action 3.4–Safety and comfort of the Vulnerable Road User): https://transport.ec.europa.eu/system/files/2016-09/2011_05-safety-and-comfort-vulnerable-road-user.pdf
SOTERIA (Systematic and orchestrated deployment of safety solutions in complex urban environments for ageing and vulnerable societies) https://soteriaproject.eu/