## Slide 1: Application Traffic Management in SEALDD - discussion
Catalina Mladin
Convida Wireless, Lenovo

## Slide 2: Introduction
…. Previously, on SA6 channel 10… … discussions on:
Support for deployments where the ATSSS feature is not available
Support for vertical/ASP/ECSP/3rd party tailored ATSSS rules configuration
Now, a new look at:
Value proposition of the usecases
Q/A highlights
New proposal for SEALDD work (SEALDD-ATM)

## Slide 3: SEALDD-ATM w/ATSSS NOT available
Use-case:
  User is at home and can use both 3GPP (path A) and non-3GPP (non- MNO provided, path B).
  UPF does NOT have ATSSS Proxy ( i.e. use of 3GPP access A1 or A2 determined based on policies and/or user input, no steering or splitting between accesses).
  The device uses first access path B. ATM determines that the 3GPP path is available and preferable (e.g. better security, reliability). ATM provides configuration to switch* from non-3GPP path B to 3GPP path A.
  Assuming single non-3GPP modem, this is switch from path B to path A1.
  The functionality is based on E2E measurements (i.e. SEALDD), not just UE-UPF.
* NOTE: assumed to also include steering/ splitting

## Slide 4: Value of Path B to Path A switch
Switch from path B to path A is where the MNO can receive the most benefits.
Further, if splitting is supported at ATM, UE can end up using NG-RAN access path (i.e. A1) and non-3GPP (i.e. B) simultaneously. Later, if ATM determines that the MNO-controlled non-3GPP access path (i.e. A2) is better than B. (e.g. after UE moves), SEALDD ATM provides configuration to switch from path B to 3GPP path A2
In this case, MNO can offer value-add services via NG-RAN (with more security, reliability, etc. than path B), for part of the traffic.
Without the SEALDD ATM switch from path B to path A mechanism the MNO doesn’t even compete in the space. This is the case for IoT platforms where the preference is given to non-3GPP accesses for many reasons. The only way to show competitiveness in the space is having path B to path A split, switch etc. which would bring more subscribers, not just more traffic into the network.

## Slide 5: Value of Path A to Path B switch
Switching the path from 3GPP (path A) to non-3GPP (path B) seems unacceptable to MNOs on the surface.
But: seamless switches between MNO controlled accesses (NG-RAN and non-3GPP, i.e. A1 and A2 ) can be enabled by MNO via ATSSS. If ATSSS is not deployed it is likely that the MNO financial advantage to offload seamlessly, to maintain continuity (e.g. via satellite) or to do splitting is not great.
However, the MNO has no visibility or recourse when subscriber or ASP force move from path A to path B.
Enabling Path A to Path B switch opportunities gives MNO visibility and more control over the switch, and recourse with the opposite path change.

## Slide 6: SEALDD-ATM coexistence with ATSSS
Business use-case:
  User is at home and can use both 3GPP (path A) and non-3GPP (non- MNO provided, path B). ATSSS is available in the 3GPP deployment.
  The device uses initially path B (E2E). ATM determines that a 3GPP path is available and preferable (e.g. better security, reliability). ATM provides configuration to switch from path B to 3GPP path A.
  The functionality is based on E2E measurements (e.g. SEALDD), not just UE-UPF.
  Once on path A, the existing/ SA2 ATSSS mechanism provides steering/ switching/ splitting between paths A1 and A2.
  Further, if splitting is supported above by ATM:
    The device can end up using access paths A1 (NG-RAN) and B (non-3GPP E2E)
    Later, if ATM determines that 3GPP A2 path is better than B. (e.g. after UE moves) ATM provides configuration to switch from path B to 3GPP path A2 (using an ATSSS split between A1 and A2)

## Slide 7: SEALDD-ATM optimization of ATSSS
SEALDD-ATM configurations are provided by ASPs, ECSPs, 3rd parties with an abstracted view of the network and its configuration.
The SEALDD-ATM Server can provide input to CN based on these higher-level configurations to allow MNOs to determine what are the fine-grained goals of the ASPs and to determine optimal ATSSS configurations, new services to provide to meet ASP needs, etc.
Optimal ATSSS policy, when matched to ASP ATM configuration, delivers best services for both ASP and MNO
Any MNO can keep limiting ATSSS configuration methods to the existing set, no traffic changes can be done without MNO agreement.

## Slide 8: Q/A Highlights
What is the ATM value-add compared to ATSSS
  SEALDD-ATM is based on E2E measurements and affects E2E traffic, unlike the UE-UPF path of ATSSS.
  For MNOs: allows to offer 5GS services in cases which may otherwise not use their network. Within 5GS traffic can be offloaded to alternate access technologies in MNO control via ATSSS.
Why implement SEALDD-ATM in SA6 in addition to ATSSS in SA2?
  SA6 already has a traffic management functionality: SEALDD
  SEALDD co-exists with and/or leverages other underlying CN mechanisms, e.g. redundant transport.
Why should an ASP deploy SEALDD-ATM in the data network if they are not using 3GPP network (on path B)?
  Because use of path B (non-3GPP, not MNO-controlled) is occasional for the UE. ASP wants to take advantage of 3GPP services when available because of their reliability, security, etc.
  Because the ASP deployment (e.g., IoT platform) is used by many UEs, and at a given time only some use non-3GPP/non-MNO path.

## Slide 9: Proposal
SA6 agrees to study SEALDD-ATM functionality within SEALDD WID.
  TR work can be included in the WID and parallelized.
  Final specifications will be part of SEALDD.
  Associated SEALDD WID update proposal has been submitted.
Thank you!