## Slide 1: Discussion on: Multi-Access APP Application enablement for Multi-Access Services
8 April, 2024
Yicong Liu, Zhe Zhou (China Telecom)

## Slide 2: Motivations
The Transmission Capability Requirement from Application Services is increasing much faster than the Network deployment and upgrading. (e.g. Higher Resolution Video/Sound, Higher accurate Spatial information, .etc)
The Transmission Reliability Requirement from Application Services is increasing much faster than the Network deployment and upgrading. (e.g. Real-time spatial information, low latency video stream)
The Coverage Requirement from Application Services is increasing much faster than the Network deployment and upgrading. (e.g. 5G+LTE / PLMN+NTN / PLMN+NPN)
An Application can provide more complex functions and services with collecting more diversified information. (e.g. Auto Driving, XR/Metaverse, High quality live stream)
Application enablement for Multi-Access will play an important role to improve Transmission Capability for increasing Applications(APP Services) Requirements
  The application enablement for Multi-Access could coordinate with Multi-Access function in Core Network, and maximize the utility of 5G/Beyond 6G connectivity capability for various application services.
  The Core Network usually does not monitor every application and can not predict the upcoming application services requested/responsed by the UE/APP Host. The application enablement will help to supply this ability.

## Slide 3
Complex Live Stream (2D/3D/XR) :
Example Use cases
Bullet chatting / bullet screen:
When a UE requests a live stream, activating an application, the UE will request ‘Multi-Access’ service enabler offered by the Application host, providing the Multi-Access Capability information. The Application Host will settle services in different accesses (e.g. the video in 5G path, the bullet chat in LTE path) or steer partial services in another path (e.g. steer upcoming bullet chat from LTE to 5G if suffering the chat explosion)
Live Special Effects / Screen stitching :
When an application service detects a new service with high transmission requirement (e.g. a live special effects triggered, tiktoker/youtuber request higher resolution live stream), the application host could settle these services on a new path or steer partial services (e.g. live chat) to another path, releasing network resources for the upcoming services.

## Slide 4
UAV complex information transmission (Auto Driving/Advanced driver-assistance system) :
Example Use cases
Video information
Vehicle information
(e.g. battery/ location/ velocity)
Cargo information
Navigation information
Drone information
Radar information
Navigation information
Auto Driving:
When a UE (a car) requests auto driving service to an application service, there are different information, with mass data, should be exchanged between UE and host (e.g. video information, navigation information, radar/lidar information, vehicle information .etc). The Application Host and UE can settle different information in different application traffics (e.g. video information in 5G path and navigation information in NTN path).
Low altitude freight:
When an application service (e.g. auto freight) is coordinating with one or more UE(s) (e.g. drones), the application server can split different information in different path (e.g. NTN+4G/ 5G+NPN), or steer some information to another path for service continuity or release transmission resources.

## Slide 5
Business / Industrial Services:
Example Use cases
Enterprise Campus/ Industrial or Business park:
When a UE in the industrial park would like to request services from the business host, there might be different types of data to be transfered (e.g. private business data, public data). UE data could be classified into insensitive one and private one, while the latter could be transfer by NPN in order to enhance its security.

## Slide 6
Potential Objectives
Application Enablers:
  a. Study the impacts to application enablers for supporting Multi-Access, such as:
  i) Indicate application service setlement.
  ii) Support application information exposure from application.
  iii) Exposure of Multi-Access information.
  iv) Support Multi-Access in Enable Layer.
  v) Support Multi-Access in Notification Management.
  Identify key issues, deployment models and develop solutions for application enablers with Multi-Access based on impacts identified in 1.a.
Mission Critical:
  Study the impacts of usage of Multi-Access for Mission Critical services, including:
  Potential awareness of the Multi-Access usage to provide better user experience
  Identify key issues, deployment models and develop solutions for Mission Critical services with Multi-Access based on impacts identified in 2.a.

## Slide 7: Proposal
China Telecom is proposing a new SID to study application enablement for Multi-Access Services.
It is proposed to agree to SID and start the study from upcoming meeting.