## Slide 1
Discussion on Support for legitimate use of digital asset by non-owner verticals
Jingwen Liu
China Mobile

## Slide 2: Outline
Requirement
Scenario introduction
Solution summary
Procedures
  Creat ownership evidence
  Apply for usage right
  Usage control

## Slide 3: Requirement
There is a open issue in KI#2 (Exposure of user sensitive information) as following：
  - How to ensure appropriate usage of user consent at the enabler layer to support localized mobile metaverse services in 3GPP specified networks? Especially how to ensure the legitimate use of user sensitive information like digital assets in the case of usage by non-owners.

## Slide 4: Scenario Introduction
The reasons for prioritizing addressing the usage across verticals are:
  1. Many verticals have a high demand to purchase the right to use digital assets with commercial value, because certain digital assets are difficult to produce or the verticals have no right to produce.
  2. Individuals have the need to authorize usage right of digital assets(i.e. avatar) to businesses.
    Example: ref. TR 22.856 section 5.24. Singer authorized his avatar to a company as the brand ambassador.
owner of digital asset
(e.g.designer and implementer of the avatar)
virtical business
(e.g.game company)
purchase the avatar usage right and use as game character
virtical users
(e.g. Game users)
disaplay and use the avatar
usage right authorization

## Slide 5: Solution summary
The goal of the solution
Support for legitimate use of digital asset by vertical business
  Protect the owner's ownership: 1. Others can not use is without authorization; 2. The others can only use it within the scope of authorization;
  Protect the user's usage right: all users of the vertical application can use it in the mobile metaverse during the validity period of the usage right
  Key point of the solution
  MMES in the enable layer is selected as the control point, which is neutral and has high credibility. The implemented functions are:
  Creat digital asset ownership evidence for the owner
  Receive usage right request and handling authorization
  Control the usage of digital asset during the use of virtical users
MMES
owner of digital asset
(e.g.designer and implementer of the avatar)
virtical business
(e.g.game company)
virtical users
(e.g. Game users)
①
②
③

## Slide 6: Solution summary
  The whole process of digital asset file conversion and delivery
render engine
Owner
User
MMES
MMEC
available file
VAL server
VAL client
converted file
converted file
reconvert
converted file
protection information
In order to prevent the virtical application using expired digital asset and secondary selling by verticals, VAL server should not have the available files of digital assets. Therefore MMES convert digital files into a converted file and give it to VAL server. The converted file can not be used directly.
Why convert file?
terms：
converted file: the file that obtained by converting the digital asset file, which can not be used directly.
available file: the file of digital asset which can be used directly.
protection information: a set of data that needed to convert and reconvert the file.

## Slide 7: Procedure(1/3)
creat digital asset ownership evidence
Owner’s MMEC
1.digital asset registration request
MMES
2.double check the ownership (optional)
3.creat digital asset ownership evidence
4.response
terms
ownership evidence: the information used to prove ownership of the digital asset.

## Slide 8: Procedure(2/3)
apply for digital asset usage right
Owner’s MMEC
2.usage right confirmation request
MMES
3.confirmation result
VAL server
1.apply for usage right
4.converts the available file into an converted file.
creates usage right information.
5.responce
terms：
usage right information: the information about the usage right authorization, it includes the expiration time of usage right, applicant, etc.
available file
protection information
computational methods
converted file
What is “convert file”?

## Slide 9: Procedure(3/3)
digital asset usage right control
VAL client
2.digital asset using request
MMEC
MMES
4.protection information request
3.check whether has protection information locally
5.protect information
available file
protection information
computational methods
converted file
What is “reconvert file”?
6.reconvert the file
VAL server
1.converted file

## Slide 10: Thanks