## Slide 1: Discussion on common EAS discovery for roaming and federation
Huawei, Hisilicon
Yajie

## Slide 2
Scenario description
Scenario clarification: EAS discovery
  For Roaming and federation, edge node sharing case, several kind of EAS may be deployed in the PLMN/ECSP’ service area
  EAS#1, EAS#2 and EAS#3 share the same EASID, however provide service to different PLMN/ECSP’ user
Consider that different PLMN/ECSP’s User can be in same group for certain application service, thus the following issue may happen:
  If EAS#1 are select as common EAS to provide service to group#1, then the UE#2 may not be able to obtain service from EAS#1.
  If EAS#2 are select as common EAS to provide service to group#1, then the UE#1 may not be able to obtain service from EAS#1.
UE#1
UE#2
PLMN#A
PLMN#B
ECS
EES
EAS#1
EAS#2
EAS#3
EAS#1: can only provide service to PLMN#A’s User
EAS#2: can only provide service to PLMN#B’s User
EAS#3: can provide service to both PLMN#A and PLMN#B’s User
UE#1 and UE#2 are in the same group
Group#1
PLMN#B
Notes: https://aws.amazon.com/ec2/autoscaling/faqs/?nc1=h_ls

## Slide 3
Scenario description
Scenario clarification: EES discovery
  For Roaming and federation, edge node sharing case, several kind of EES may be deployed in the PLMN/ECSP’ service area
  EES#1, EES#2 has the EAS#2 and EAS#3 which share the same EASID, however provide service to different PLMN/ECSP’ user
Consider that different PLMN/ECSP’s User can be in same group for certain application service, thus the following issue may happen:
  If EES#1 are select as common EES to provide service to group#1, then the UE#1 may not be able to obtain EAS address information which can provide service to UE#1
UE#1
UE#2
PLMN#A
PLMN#B
ECS
EES#1
EAS#2
EAS#3
EES#1: has the EAS which can only provide service to PLMN#B’s Use
EES#2: has the EAS which can only provide service to both PLMN#A and PLMN#B’s User
UE#1 and UE#2 are in the same group
Group#1
PLMN#B
EES#2
Notes: https://aws.amazon.com/ec2/autoscaling/faqs/?nc1=h_ls

## Slide 4
Way Forward
The service provisioning procedure and the EAS discovery procedure should be enhanced:
  The service provisioning procedure should be enhanced with group PLMN/ECSP information, so that the EES determination can be based on EAS allowed PLMN/ECSP information and group PLMN/ECSP information
  Similarly, the EAS discovery procedure should also be enhanced with group PLMN/ECSP information, so that the EAS determination can be based on EAS allowed PLMN/ECSP information and group PLMN/ECSP information
Notes: Observation#1
#2
Way forward

## Slide 5: The end