## Slide 1: Enhancement for migration
Ericsson

## Slide 2: Sequence for migration (fig. 10.1.1.2-1)
Observation 1: Migration happens only at the application layer
Observation 2: The MC service user is still connected to the SIP core of its home MC system

## Slide 3: 5.2.9.3 SIP core / IMS utilization
Migrated MC service users should utilise the SIP core / IMS of the partner MC system.
NOTE 1: The above recommendation ensures the security policy of the partner MC system is not compromised and ensures service‑level delay requirements are consistently met (which are especially at risk when the SIP core / IMS of the primary MC system and the SIP core / IMS of the partner MC system are far apart from a geographical point of view).
Where connectivity and security policies allow, the same SIP core / IMS can be utilised to connect to the primary MC system and one or more partner MC systems.
NOTE 2: Whether the same SIP core / IMS can be utilised to connect to the primary MC system and a partner MC system is left to business agreements between MC service providers, and is outside the scope of the present document.
For each partner MC system, MC service UEs of MC service users enabled for migration shall be provisioned with:
- configuration that controls whether the MC service UE shall connect to the SIP core / IMS of the primary MC system or a different SIP core / IMS (i.e. SIP core / IMS of the partner MC system); and
- where a different SIP core / IMS to the primary MC system's SIP core / IMS is to be connected to then the MC service UE shall also be configured with:
- configuration required for the MC service UE to access the SIP core / IMS; and
- credentials required for the MC service UE to register with the SIP core / IMS.
Editor's note: It is FFS how the MC service UE connects to the SIP core / IMS of the partner MC system to access MC services in the partner MC system.
FQDN of the SIP Proxy (P-CSCF) or its IP address (cl. 5.1.1.0 of TS 23.228)
Which credentials/ parameters?
FQDN: Fully Qualified Domain Name

## Slide 4: Background from TS 23.228 and TS 33.203
The necessary parameters to initiate registration to IMS system:
  The IMS private user identity (IMPI)
  One or more IMS public user identities (IMPU)
  The home network domain name used to address the SIP REGISTER request
  Any authentication key
In addition, the FQDN of the SIP proxy (P-CSCF) or its IP address
FQDN: Fully Qualified Domain Name

## Slide 5: Question
Question 1: how to provide the MC service client with SIP access information and credentials to register at the SIP core/ IMS of the partner MC system?

## Slide 6: Background from TS 33.203
IMS AKA achieves mutual authentication between ISIM (UICC card) and the home network
The identity used for authenticating a subscriber is the IMS private user identity (IMPI)
The HSS and the ISIM share a long-term key associated with the IMPI
The ISIM is capable of securely store one IMPI only (the IMPI of the primary MC system)

## Slide 7: Observations
An MC service UE is attached to only one PLMN at a time
An MC service UE is registered to only one SIP core/IMS network at a time
The IMPI of another IMS network (other than the primary MC system) is not included in the ISIM`s of the MC service UE
In case of migration: the IMPI (and necessary parameters to initiate SIP registration at the partner MC system) are missing

## Slide 8: Question
Question: how to provide the MC service client with SIP access information and credentials to register at the SIP core/ IMS of the partner MC system?

## Slide 9: Background from TS 23.228 and TS 23.203
For UEs supporting only non-3GPP access, if neither ISIM nor USIM is present, but IMC is present, the necessary information is stored in the IMC (clause 4.3.3 of TS 23.228)
IMC shall not be used if ISIM or USIM is present (clause 9 of TS 23.203)
TS 33.180 allows for MC service users over non-3GPP access (e.g., control room) to use SIP digest mechanism (clause 6.2.1 of TS 33.180)

## Slide 10: Background from TS 23.228 and TS 23.203
SIP digest achieves mutual authentication between the UE and home network
The identity used for authenticating a subscriber is the IMPI
The HSS and the UE share a password associated with the IMPI
FQDN of the SIP proxy (P-CSCF) or its IP address needs to be known

## Slide 11: Thank You!