## Slide 1
Discussion
Study on 5GSAT_Ph4_App enhancements
Basavaraj (Basu) Pattan, Samsung

## Slide 2: 5GA Proposal Overview: 5GSAT_Ph4-App
Background/Motivation
  5GSAT_Ph3_App did not fully specify Rel-19 satellite features.
  Satellite related new requirements from Rel-20
SI+WI
  To resolve open issues from Rel-19 and to address new requirements from Rel-20, a study is required
Continuation topic to resolve the gaps and enhacements
Objectives
  Rel-19 leftovers
    UE-Satellite-UE communication
    Regenerative Payload
TUs required: 10-12 TUs
Dependency on other WGs
  SA2 for Rel-20 features
    Resilient notification - MT call failure
    Emergency communication
  Rel-20 enhancements
    Multi-orbit
    IMS Voice over GEO satellite
    Sharing Satellite ID to UE
    Mission Critical support

## Slide 3: Detailed 5GA Proposal: 5GSAT_Ph4-App Rel-19 Leftovers
UE-Satellite-UE communication
TR 23.700-01 Key issue #6
Scoped only to IMS applications
Signalling to ground but data packets between UEs via Satellite
Identify and specify consumers of such UE-Sat-UE communication
Regenerative Payload
UPF onboard satellite is not supported by SA2 for NGSO, only gNB onboard NGSO satellites is specified
However, SA6 assumes UPF onboard satellite for supporting EAS and EES onboard satellite
Sharing Satellite ID to UE
SA2 defined Satellite ID only for GEO
SA6 Service Provisioning and Discovery solutions expect EEC, EES and ECS to know Satellite ID
SA2
EAS
EES
SA6

## Slide 4: Detailed 5GA Proposal: 5GSAT_Ph4-App Rel-20 Enhancements (SA6 scope is TBD)
Multi-orbit
18 (out of 24) use cases of are related to multi-orbit
Multi-orbit use cases – Service continuity, Mobile Base Station Relays (MBSR), Traffic switching, Vehicular communication, Combined TN and NTN multi-orbit services, Wide-area MC, etc
IMS Voice over GEO Satellite
All media types - voice, data, and video supported since Rel-17 but practical only for NGSO
GEO Challenges – Transmission delay, Codec bitrate, Call setup time
Consider MC PTT call setup and floor control
Emergency Communication and Resilient notification - MT call failure
Emergency communication - emergency notification message broadcast in the area based on the received location information
Resilient Notification: a highly reliable mechanism that delivers notifications directly to user devices, such as smartphones, when in poor conditions in satellite access.
 | UE to serving satellite propagation delay [ms] |  | UE to ground max propagation delay [ms]
 | Min | Max | 
LEO | 3 | 15 | 30
MEO | 27 | 43 | 90
GEO | 120 | 140 | 280

## Slide 5: Way forward proposal
Based on the background, we proposed to agree (S6-250250) to study on the following
  5GSAT_Ph3_App did not fully specify Rel-19 satellite features.
  Satellite related new requirements from Rel-20
We propose to study:
  To resolve open issues from Rel-19 and to address new requirements from Rel-20, a study is required
Dependency on other WGs: SA2

## Slide 6: Thank you !