## Slide 1: Initial thoughts on temporary MC service UE disable
Sivasubramaniam (Ram) Ramanan & Mythri Hunukumbure
UK Home Office

## Slide 2: 3GPP Requirements (TS 22.280)
6.13.4 Access control
[R-6.13.4-001] The MCX Service shall support suspending or disabling of access from an MCX UE or an MCX User to the MCX Service.
[R-6.13.4-002] An MCX User who has a profile that has been deleted or suspended shall be prevented from using that MCX Service User Profile to access the MCX Service.
[R-6.13.4-003] The MCX Service shall provide a mechanism to temporarily disable an MCX UE remotely by the MCX Service Administrator or an authorized MCX User.
[R-6.13.4-004] The MCX Service shall only allow a user to affiliate to or select an enabled MCX Service Group (i.e., not disabled).
[R-6.13.4-005] A temporarily disabled MCX UE, which has limited access capability per Mission Critical Organization policy, shall be able to be re-enabled by the MCX Service Administrator or an authorized MCX User.
[R-6.13.4-006] The MCX Service shall provide a mechanism to re-enable a temporarily disabled MCX UE by the MCX Service Administrator or an authorized MCX User.
[R-6.13.4-007] The MCX Service shall provide a mechanism to permanently disable an MCX UE by the MCX Service Administrator or an authorized MCX User.
[R-6.13.4-008] The permanently disabled MCX UE shall remove all MCX Service User Profiles stored in the MCX UE.
[R-6.13.4-009] The permanently disabled MCX UE shall have no access to MCX Services.
[R-6.13.4-010] The security solution for the MCX Service shall minimize the impact of a compromised MCX UE on other MCX UEs.

## Slide 3: Device and service access
MC service UE: A UE that can be used to participate in one or more MC services and recording admin and replay services.

## Slide 4: Levels of limited access (or services)
Permanent – disables UE/removes application (deletes MCX)/other data
  wiping (factory reset) a device to remove all managed applications and data and takes the device back to a factory state as if new.
Temporary – ?
  temporarily disable a device or parts of the (service) capability of a device,
  the ability for the device to be easily or quickly returned to operational state again if needed

## Slide 5: Useful requirements
Accessible through MCX service
24 x 7 availability through control rooms/dispatcher
Remotely disable or re-enable MC UE access
Which (or if any) MCX features need to kept alive, needs further study

## Slide 6: Summary
Need to clarify disabling MC UE versus MCX service UE access capability
Need to establish what is within the scope of MCX standards