## Slide 1: Temporary MC service UE disable
Mythri Hunukumbure & Sivasubramaniam (Ram) Ramanan
UK Home Office

## Slide 2: Summary of Requirements
A - Our MC users require that ALL MCX services on the UE, including MCX log-in, should be disabled. Public telephony services in the device should not be disabled.
  We will support a solution where individual MC services can be kept alive, if it also has the option to disable all the MC services.
B - A single MC user can have multiple devices. User should be able to identify the lost device in a human readable manner, when reporting.
  MC UE label with the MC user ID can be a useful way to report lost devices in this scenario.
C - Some devices may be in common use and multiple users will have access to these.
  The link between the MC User ID and device ID will change and this should be dynamically updated. A user who reports the loss of a device should not have his MC user credentials disabled.
  If a solution is developed based on user authentication and authorisation tokens, the requirement in C-I should be supported.

## Slide 3: Main points for developing a solution
A unique, persistent device ID shall be linked to the ‘current’ MC user ID in a Database/ Table within the MCX system and this should be dynamically updated.
When a device is reported as lost/stolen:
  The device shall be marked as ‘disabled’ in the MCX system and any attempt to log-in or use MCX services through this device should be blocked.
  If the device is accessible and logged in, the MCX log-off should happen. Some or all of the MCX clients in the device shall be remotely disabled.
If a disabled device is recovered and needs re-enabling:
  The device shall be marked as ‘enabled’ in the MCX system and any attempt to log-in and use MCX services through this device should be allowed.
  The MCX clients in the device shall be remotely re-enabled.

## Slide 4: Responses to comments received in pre-meeting

## Slide 5: Access tokens related solution
Rather than using a device ID, use the ‘client ID’ defined in TS 33.180 for controlling authentication and authorisation.
  The refresh time of the ‘access token’ can be shortened, so any device (or client) needing disablement will not have the tokens refreshed at the next time period.
  This ‘way around’ is linked to ID management in TS 33.180, Open ID Connect in Annex B
Our view:
  Authentication, authorisation processes and access tokens in TS 33.180 are specifically linked to a MC service ID (User ID) and will not actually provide device disable. Can this approach meet the requirements B and C on multiple devices per user and multiple users on single device? Will another MC user on the same device have another ‘client ID’?
  If timers for refreshing are set too low, this will cause problems when MC users have to move in and out of coverage frequently. ESN wants to set common timers on most devices and does not want to keep changing these.

## Slide 6: Keeping some MCX capabilities active
In TETRA, the ‘stun’ feature retains the localization capability. This used to be ESN preference also, to retain MC location. Why are we now requesting that ALL MCX capabilities to be disabled? In addition, Ambient Listening could also be retained.
Our view:
  The SA1 requirements clearly say capabilities shall be retained as per UO policy. For ESN we would want all MC capabilities to be disabled in our solution. ESN will use the EMM capabilities to track/locate disabled devices. If a solution allows each client to be disabled individually, then any combination of clients can be kept working or disabled.
  For features like AL to be active, the solution needs to go deeper than the MCPTT service client, to keep only AL active. This is not something ESN wants (at least at this stage).

## Slide 7: Keeping MCX clients registered
The MCX client should always stay registered with the relevant server. Trying to disable the client functionality should not be in the standards domain. Any solution should only address the server side.
Our view:
  If a solution can be found on the server side that meets our requirements, we can consider this. However, there are other comments on the need to keep some clients (or features) active while others are disabled.
  The clients do not have to be connected all the time to the servers. MC devices can move in and out of coverage and the clients will then renew their connections with the servers.
  At least some form of forced ‘log-off’ from the disabled device is needed. If a device is stolen while the MC user is logged-in, all the MC media cached in the device will be accessible to the intruder.