## Slide 1: A few thoughts on migration and communication continuity after a user has migrated
Jerry Shih
AT&T

## Slide 2: Migration (23.280 clause 5.2.9)
Migration provides means for the MC service user to obtain MC services from a partner MC system. As the MC service client receives one or multiple user profiles for the MC service user from its primary MC system (as described in clause 10.1.4.3). Each user profile contains a list of partner MC systems that the user is permitted to migrate to, along with necessary access information to facilitate service authentication, hence, facilitate migration to the partner MC system.
Upon a successful service authorization for migration, i.e., once the MC service user is authorized to migrate to a partner MC system, its primary MC system marks the user as migrated, is informed of the target partner MC system, and records the corresponding MC service ID of the migrated user provided by the partner MC system. Further details are described in clause 10.6.3.

## Slide 3: 10.1.1.2 MC service configuration for migration to partner MC system

## Slide 4: 10.1.4 MC service user profile
one MC service ID associates with multiple MC service user profiles but only one is active for a MC service per UE at any time.  The MC service UE should download ALL enabled MC user profiles for that MC service user and select one (maybe use default) to be active for the service. 10.1.4.2.8/10, 10.1.4.3, 10.1.4.6,
The MC service user may have one or more specific MC service user profiles defined for use in migration cases, whereby there may be more than one MC service user profiles defined for migration for that MC service user e.g. so that different MC service user profiles can be applied in different partner MC systems. No need to download a profile for migration, 10.1.4.3.2 (configuration management client to retrieve the MC service user profile for the migrating MC service user from the partner MC system) is not needed?
The appropriate MC service user profile for migration for the relevant partner MC system will be provided to the partner MC system by the procedure (modify 10.17.5 or a new procedure)
For both the cases of MC service on the primary MC system of the MC service user, and MC service when migrating to a partner MC system, only one MC service user profile per MC service client is active at a time. Basic principle.
MC service user profile information (all available ones) is downloaded to the MC service UE. The MC service user profile configuration may include more than one information exchange e.g. the configuration management server may provide the MC service UE with a list of some or all enabled MC service user profiles to allow the MC service user to select one (where the list may contain a subset of the MC service user profile information sufficient for the MC service user to distinguish which MC service user profile to select).
When an MC service user is receiving MC service in its primary MC system, the MC service user profile provisioning in the UE is initiated by the configuration management client (e.g. upon MC service user authentication or on reconnect to the MC service), or initiated by the configuration management server (e.g. due to role change or organization change).
For a migrating MC service user, the MC service user profile provisioning in the UE is initiated when the MC service user attempts to migrate to a partner MC system, and requests the MC service user profile from a nominated configuration management server in the partner MC system, prior to requesting service authorization from a partner MC. Why need to download it from partner MC system when the MC service user profiles are already available on the UE? Update maybe okay due to changes to the partner local policy (after validated by the primary).
The partner MC system may require that the MC service user profiles for migrating MC service users have parameters imposed by that partner MC system according to its operating and security policies.
The partner MC system applies any necessary modifications to the MC service user profile received from the primary MC system of the MC service user in accordance with its local requirements. This local profile will be stored, and will be provided to the configuration management server in the partner MC system in order to distribute it to the configuration management client of the migrating MC service user. This modified profile may be sent to the primary MC system of the migrating MC service user so that the primary MC system can validate the modified profile before it is provided to the migrating MC service UE.
The modified MC service user profile will subsequently be provided to the MC service server in the partner MC system when the migrating MC user attempts service authorization. New procedure?

## Slide 5: Time sequence of a Migration
Before migration
  Primary MC system prepares for the migration user profile with Partner MC system (10.17.5)
    (Partner assigned) MC service ID, access information for partner MC system required for initial UE configuration to access an MCPTT system, as defined in table A.6-1 of 3GPP TS 23.280 etc.
    Should the Primary MC system share the migration user profile with Partner MC system at this time, using CSC-17 on CMS-CMS? If not when?
    At this time both the Primary and Partner MC systems know a user may/could migrate .
During migration
  MC system initiated (with location information), MC system selects the appropriated user profile and starts the migration process (user involved/informed?).
  User initiated. Need to get authorization from Primary MC system and (selected by who?) migration user profile.
  User logs onto the Partner MC system (auth/auth at the Primary MC system by which functional entity MC service server? How?) and uses the MC services in the migration user profile. (share the migration user profile with Partner MC system with possible changes for local policy).
  Migration user profile maybe updated by both Primary and Partner MC systems through CMSs (CSC-17).

## Slide 6: Migration user profile
No specific definition, assume it is a copy of the user profile in A.3? Or is it created on demand?
  The key is the first two parameters in table A.3 (MC service ID, KMSUri for security domain of MC service ID)
  When the user profile is used at home, the MC service ID is assigned by home MC system, while it is used at migration it is assigned by the Partner MC system, new home MC system.
In a user profile, there is a list of the Partner MC systems a user can use this profile.
The MC service ID assigned by the Partner MC system needs to be stored per Partner MC system.
It has to be downloaded (retrieved with CMC) to the UE before migration happens. (new procedure); if it is not the same user profile that is being used.
The migration user profile is identified by the MC user profile index in a user’s Primary MC system database (could cover more than one Partner MC systems), so to point to the right Partner MC system info we need the (index + Identity of Partner MC system), this needs to be communicated to the client?
This profile needs to be shared with the Partner MC system for potential modifications for local policy. (new procedure) over CSC-17 but when? Should be before migration.
Needs to remember where the “home” (Primary MC system) is and possibly the MC service ID at home. (new) where to keep it, cannot be the dynamic data on the client.

## Slide 7: Potential Changes for Migration
Update user profile with personal migration needed information OR define new one for migration? CRs in this meeting.
Add a procedure for user to ask for migration and retrieve the proper user profile before migration. Need new CR.
Determine when and how (home or at Partner network) the migration user profile should be downloaded to the user UE. Need new CR.
Add a procedure to share migration user profile with Partner MC system. Need new CR.
Clause 10.1.6.1 can be replaced by 10.17.5 or clarify
Potential impacted clauses:
  23.280: 10.1.1.2, 10.1.4.1, 10.1.4.2.1 (need index?), 10.1.4.3.2, 10.18.2.2(?),
  Service TSs: NA other than CRs in this meeting?

## Slide 8: 10.16.2 Migration during an ongoing group communication
The MC service client requests de-affiliation from MC service groups. The MC service groups are either defined in the primary MC system (see clause 10.8.4.2) or the partner MC system (see clause 10.8.4.3).
After migration to the partner MC system, the configuration management client triggers retrieval of the MC service user profile used within the partner MC system (see clause 10.1.4.3.2).
The MC service client requests affiliation to MC service groups. The MCPTT groups are either defined in the primary MC system (see clause 10.8.3.1) or the partner MC system (see clause 10.8.3.2 or clause 10.8.3.2a).
If any of the received group calls are ongoing in the partner MC system, the partner MC system shall initiate a late-entry procedure towards the MC service client. If any of the received group calls are taken place in the primary MC system but not yet in the partner MC system, the affiliation by the migrated MC service UE triggers the late-entry procedure which then includes the MC service UE and the partner MC system into the group call.
The migration user profile needs to be available even before migration starts
Client needs to remember which groups were terminated due to migration and use the new MC service ID to join
How the partner MC system knows the new MC service ID?

## Slide 9: 10.16.4 Migration during an ongoing private communication
no need for this procedure as it can just be a new private call to the same user after migration.

## Slide 10: Issues on continue communication during migration
The migrated MC service ID needs to be provisioned in the group management server
How to communicate/share the ongoing communications to the partner MC system