## Slide 1
SA6 SID Application user consent enabler
(FS_COCOA) for Rel-20
Including alignment with GSMA OPG and CAMARA and interoperability with CAPIF RNAA
Ericsson, AT&T

## Slide 2: Main points
COCOA enabler does not change the existing CAPIF RNAA (embedded RO authorization management in the OAuth 2.0 flow), currently handled by CCF Authorization Function
COCOA is a new standalone enabler for application user consent (app-user consent) that can be used standalone
  agnostic to the API exposure Frameworks
  agnostic to 3GPP technology generations (4G, 5G, …)
COCOA enabler Study (FS_COCOA) aims to determine the use cases that offer a suitable experience to the users in conjunction with the consumption of applications
  e.g., some user surveys revealed that users hate to be interrupted when accessing an application, to go over consent forms, this causes friction for the user when buying goods, etc
CAPIF in Rel-20 can integrate with COCOA enabler once COCOA architecture is ready, in parallel with CAPIF internal RO authorization

## Slide 3: What COCOA enabler does NOT address
The specification of a storage for app-user consent data (but it may identify some requirements)
The regulatory aspects for the app-user consent data, security aspects (SA3 remit)
The FE means (client app on UE, web portal, operator server, etc) used by the user to provide consent remains highly operator-specific
  It follows same approach as in GSMA OPG, where these are left as differentiator for the operators
OSS/BSS app-user consent provisioning aspects for the COCOA enabler

## Slide 4: What COCOA enabler addresses
Use cases, study KIs and recommend solutions, requirements and enabler architecture to (non-exhaustive list) :
  Explore business relationships between main actors and determine the application user consent scenarios that need to be addressed (federation, aggregation, etc)
  Expose management interfaces for the app-user consent data: create, update (including revoke), check/query, get app-user consent data (per app, bulk)
  Trigger the capture of app-user consent from the consent granting user/subscriber (user roams into a different country/regulation, expiry of consent, operator change of policies, etc)
  Apply Consent-related policies (e.g., related to the different Authorization Servers from different exposure partners and business relationships) to the app-user consent data management operations
  Notify interested entities (e.g. sub-not) of app-user consent data changes

## Slide 5: General Information
CAPIF RNAA (= OAuth 2.0 with embedded RO authorization management)
CAPIF RNAA
extended the previous CAPIF OAuth 2.0 authorization to add RO ID and embed the management of application user consent (named “RO authorization”) inside the RNAA flow
  CAPIF Authorization Function was tasked with dual role of OAuth 2.0 Server role + Consent Manager role
Terms: RO authorization
– remains as the term referring to the user consent for applications handled together with the OAuth2.0 (i.e., OAuth 2.0+Consent management are handled together inside the CCF Authorization Function)

## Slide 6: General Information
CAPIF RNAA
- Extended the previous CAPIF OAuth 2.0 authorization to add RO ID and embed the management of application user consent (named “RO authorization”) inside the RNAA flow
  CAPIF Authorization Function was tasked with dual role of OAuth 2.0 Server role + Consent Manager role
Terms : App-user consent
– the agreement of a user/subscriber provided to the operator, to expose their data from the 3GPP domain to applications for specific purposes. This agreement can be revoked at any time.
Exposure Framework Z (non-CAPIF)
COCOA enabler
Typically the Exposure Frameworks provide:
Consumer (API invoker) authentication and
Consumer (API invoker) authorization (most used is OAuth 2.0-based) consolidating different input/criteria : operator policies, AC (R/TBAC), where applicable also checking app-user consent
COCOA Enabler
Operator Platform (GSMA OPG)
Operator Platform (GSMA OPG)
Exposure Framework Y (non-CAPIF)
Exposure Framework X for BSS (non-CAPIF)
Exposure Framework W, hyperscaler (non-CAPIF)
Authorization Server
NEF

## Slide 7: Background: SA6 SID
S6-252068 [was S6-251425]

## Slide 8: Additional material for FS_COCOA SID
Supporting material:
S6-252069
S6-252070
Previous FS_COCOA SID supporting material
S6-251425.zip (SID Goteborg)
S6-251249 (DP)
S6-251246 (Supporting material)

## Slide 9: Backup slides
Application user consent handling in
GSMA OPG and CAMARA

## Slide 10: GSMA OPG.02 v9.0 Annex G.4.1 : User opt-in
Notes: OPG.02 Section 4.11.1:
“If there is no associated Consent Record, the OP signals the Consent Manager to start the capture of the Consent from the end user (Step 8). Once the Consent is requested (Step 9), the result of that operation is stored in the Consent Manager (Step 10). If the consent is not granted by the end user (for instance the user does not agree with sharing its information for the signalled Purpose of data processing) the authorization process fails and the access to the personal information resources is denied. If the consent is granted an Authorization Code sent back (Step 11,12) which can be later exchanged for an operator Access Token (Step 13). Upon reception of NBI API call carrying the operator Access Token in Step 14, the OP decrypts the Access Token and forwards the request to receive a response which is sent back.”

## Slide 11: GSMA OPG.02 v9.0 Annex G.4.2 : Federated environment

## Slide 12: Overlay SA6 CAPIF Consent architecture on GSMA OPG.02 case (1)
v
v
Oauth 2.0 Authorization Server
v
RO Authorization Management
Authorization Function
v
No ROF on UE
CAPIF Core Function
In OPG the Consent Mgr is outside the Exposure Platform (OP)
Notes: OPG.02 Section 4.11.1:
“If there is no associated Consent Record, the OP signals the Consent Manager to start the capture of the Consent from the end user (Step 8). Once the Consent is requested (Step 9), the result of that operation is stored in the Consent Manager (Step 10). If the consent is not granted by the end user (for instance the user does not agree with sharing its information for the signalled Purpose of data processing) the authorization process fails and the access to the personal information resources is denied. If the consent is granted an Authorization Code sent back (Step 11,12) which can be later exchanged for an operator Access Token (Step 13). Upon reception of NBI API call carrying the operator Access Token in Step 14, the OP decrypts the Access Token and forwards the request to receive a response which is sent back.”

## Slide 13: Overlay SA6 CAPIF Consent architecture on GSMA OPG.02 case (2)
v
Oauth 2.0 Authorization Server
v
RO Authorization Management
CCF in CSP domain 1
v
No ROF mandated on UE
Authorization Function
CAPIF Core Function in CSP domain 2
In OPG the Consent Mgr is outside the Exposure Platform (OP)

## Slide 14: CAMARA
https://github.com/camaraproject/IdentityAndConsentManagement/blob/r2.1/documentation/CAMARA-API-access-and-user-consent.md

## Slide 15: CAMARA Scenario 1: Authorization code

## Slide 16: CAPIF Authorization overlay on CAMARA Scenario 1
v
Oauth 2.0 Authorization Server
v
RO Authorization Management
Authorization Function
v
No ROF on UE
CCF in CSP domain
In CAMARA the Consent Master is outside the API Exposure Platform

## Slide 17: CAMARA Scenario 2: CIBA flow (Backend flow)

## Slide 18: CAMARA Scenario 2: CIBA flow (Backend flow)
v
Oauth 2.0 Authorization Server
v
RO Authorization Management
Authorization Function
v
No ROF on UE
CCF in CSP domain
In CAMARA the Consent Master is outside the API Exposure Platform

## Slide 19: CAMARA Scenario 3: Client credentials
https://github.com/camaraproject/IdentityAndConsentManagement/blob/r2.1/documentation/CAMARA-Security-Interoperability.md