## Slide 1: Discussion Paper on SID proposal of application enablement for Ambient IoT services
CATT
Wu Liping

## Slide 2: Outline
Motivation
Proposals
SA2 progress

## Slide 3
SA1(TS 22.369) has identified the service requirements of Ambient IoT , includes 6 aspects:
  Communication;
  Positioning/location;
  Management;
  Collected information and network capability exposure;
  Charging;
  Security and privacy
Potential SA6 impacts based on above SA1 service requirements：
  Collected information and network capability exposure:
    Subject to user consent, operator policy and 3rd party request, the 5G system shall be able to obtain data from Ambient IoT devices (e.g. sensor data) and provide it to a trusted 3rd party via the 5G network.
    Subject to user consent, operator’s policy and 3rd party request, the 5G system shall provide information about an Ambient IoT device or a group of Ambient IoT devices (e.g. position) to the trusted 3rd party via the 5G network.
    The 5G system shall enable an authorized 3rd party to instruct the 5G network to trigger a group of Ambient IoT devices in an specific area and which action the Ambient IoT devices need to perform when triggered (e.g. send ID, receive further information, send measurement value).
Potential SA6 impacts based on SA1 requirements
Notes: 周期管理、数据采集、不同组管理及操作、复杂任务的管理、签约归属权的转移、终端区域数量TR 22840：
    [PR 5.3.6-003] The 5G system shall support a mechanism to interface a 3rd party application to manage and operate on the Ambient IoT devices.
    [PR 5.29.6-1] Based on operator policy, the 5G system shall provide means for a trusted third party to request the permanent disabling of an Ambient IoT device to communicate with the 5G system.
    [PR 5.29.6-2] Based on operator policy, the 5G system shall provide means for a trusted third party to request the deletion of any digitally stored information of an Ambient IoT device.
    [PR.5.27-003] The 5G network shall be able to trigger Ambient IoT devices. The 5G system shall enable an authorized 3rd party to instruct the 5G network in which area, which group of Ambient IoT devices needs to be triggered and which action the Ambient IoT devices need to perform when triggered (e.g. send ID, receive further information, send measurement value).
    [P.R.5.1.6-002] The 5G system shall support to provide collected information from Ambient IoT devices to the trusted 3rd party.
    [PR.5.21.6-004] The 5G system shall be able to expose the identities and relative positioning results of Ambient IoT devices to a trusted third party. The 5G system shall be able to provide a mechanism to expose the information collected from an Ambient-IoT device to a trusted 3rd party.
    NOTE: The request from 3rd party can include the requested Ambient IoT device identity, the requested service area to find the Ambient IoT device, the requested information of an Ambient IoT device includes position information.
    [P.R.5.12.6-003] The 5G system shall be able to provide information of a specific Ambient IoT device to the trusted 3rd party.
    [P.R 5.13.6-005] The 5G system shall support transferring data collected from Ambient IoT devices to a trusted 3rd party.
    [PR.5.20.6-001] The 5G system shall support communication with Ambient IoT device with 3rd party application server.
    [PR 5.22.6-2] The 5G system shall provide a mechanism for a 3rd party application to write user data to and to read user data from an Ambient IoT device.

## Slide 4
Potential SA6 impacts based on the market needs and the operator’s view：
  Based on some operators’ view, the AIoT enabler layer could be an AIoT management platform to support the application server’s complex requirements.
  The AIoT management platform is mainly responsible for the management of AIoT devices and the aggregation /processing of AIoT devices data. It may include the registration, configuration, status monitoring and maintenance management of various types of devices. And also contain data cleaning, format unification and standardization processing which providing a reliable foundation for the data analysis of the subsequent application layer.*
Potential SA6 impacts based on market needs
VAL services
(Logistics, Factory)
AIoT Enabler/
AIoT management platform
SA2 capabilities
Exposure
Service requests
Enabler Layer
Network layer
Application Layer
Exposure
(*): The sentences come from CMCC, “white paper on typical scenarios and technical solutions of 5G-A Ambient Internet of Thing”.
Notes: 周期管理、数据采集、不同组管理及操作、复杂任务的管理、签约归属权的转移、终端区域数量TR 22840：
    [PR 5.3.6-003] The 5G system shall support a mechanism to interface a 3rd party application to manage and operate on the Ambient IoT devices.
    [PR 5.29.6-1] Based on operator policy, the 5G system shall provide means for a trusted third party to request the permanent disabling of an Ambient IoT device to communicate with the 5G system.
    [PR 5.29.6-2] Based on operator policy, the 5G system shall provide means for a trusted third party to request the deletion of any digitally stored information of an Ambient IoT device.
    [PR.5.27-003] The 5G network shall be able to trigger Ambient IoT devices. The 5G system shall enable an authorized 3rd party to instruct the 5G network in which area, which group of Ambient IoT devices needs to be triggered and which action the Ambient IoT devices need to perform when triggered (e.g. send ID, receive further information, send measurement value).
    [P.R.5.1.6-002] The 5G system shall support to provide collected information from Ambient IoT devices to the trusted 3rd party.
    [PR.5.21.6-004] The 5G system shall be able to expose the identities and relative positioning results of Ambient IoT devices to a trusted third party. The 5G system shall be able to provide a mechanism to expose the information collected from an Ambient-IoT device to a trusted 3rd party.
    NOTE: The request from 3rd party can include the requested Ambient IoT device identity, the requested service area to find the Ambient IoT device, the requested information of an Ambient IoT device includes position information.
    [P.R.5.12.6-003] The 5G system shall be able to provide information of a specific Ambient IoT device to the trusted 3rd party.
    [P.R 5.13.6-005] The 5G system shall support transferring data collected from Ambient IoT devices to a trusted 3rd party.
    [PR.5.20.6-001] The 5G system shall support communication with Ambient IoT device with 3rd party application server.
    [PR 5.22.6-2] The 5G system shall provide a mechanism for a 3rd party application to write user data to and to read user data from an Ambient IoT device.

## Slide 5: Use case 1: AS asks for different types of devices
Use Case 1:
  Application server(retail store app) triggers the inventory request which expects to receive the notification about the number of different types of goods in a specific area.
Retail store APP
gNB
AIoT Devices
(e.g. foods, fruits)
AIoT Enabler
Expose:
- List of AIoT devices ID for all of goods.
5GC Core
Expose:
List of AIoT devices ID and numbers for different type of goods (foods, fruits)
Inventory Request
- Including only the target area
Application enabled layer
Network layer
Notes: AIOT enabler needs to clarify the goods based on different device ID then computing their numbers.
AIOT enabler may receive the device data from different 5GC core, the aggregation for these device ID may be needed.
The NEF may send multiple reports to AF/enablers. So AIOT enabler needs to aggregate the info.

## Slide 6: Use case 2: AS asks for the notification
Use Case 2:
  Application server(retail store app) triggers the inventory request which expects to receive the notification about when the goods need to be increased/decreased.
Retail store APP
gNB
AIoT Devices
AIoT Enabler
Expose:
- List of devices ID
5GC Core
Expose:
Delta change of devices
Notification: The number of goods are above/below the threshold and the goods need to be increased/decreased.
Inventory Request
Including the threshold of notification (e.g., the minimum number of goods)
Periodical reporting triggers
Network layer
Application enabled layer
Notes: AIOT enabler needs to compute the device’s numbers and compare if they are above/below the threshold of notification

## Slide 7: Use case 3: Monitoring the status of AIoT devices
Use Case 3:
  Application server(Logistics app) triggers the inventory request which expects to receive the AIoT device’s trajectory/route in a period.
Logistics APP
gNB
AIoT Devices (e.g. TV)
AIoT Enabler
Expose:
- List of devices ID and the related location (reader location instead in Rel-19)
5GC Core
Expose:
List of devices ID, the device’s trajectory/route, the predicted location
Warning if the device location is inconsistent with its trajectory/route
Inventory Request
Including the specific AIoT device’s ID
the optional trajectory/route request for the target device
Network layer
Application enabled layer
Notes: AIOT enabler needs to monitor and store the devices’ location from SA2 exposure and generate the device’s trajectory/route

## Slide 8: Outline
Motivation
Proposals
SA2 progress

## Slide 9: Proposals for Rel-20 FS_AIoT_APP
Proposed Objectives
  1. Identify the service impacts to the application enabled layer from SA1 use cases and/or the application server’s requirements.
  2. Study new architecture or enhancements on existing SA6 application enablers for supporting Ambient IoT services in application enabled layer based on bullet 1.
    Expose the value-added service/information of Ambient IoT devices to the consumer
      Study how to enrich the processing (e.g., classification, aggregation) of the collected Ambient IoT device data.
      Study how to utilize the exposure from other working group (e.g., SA2) and provide the value-added Ambient IoT device information to the consumer (e.g., application server).
    Management of Ambient IoT devices
      Study how to further manage the Ambient IoT devices (e.g., monitoring the status of Ambient IoT devices) when the application enablers acting as a management platform for the Ambient IoT devices.
  3. Identify potential key issues and related solutions, to satisfy the architectural requirements and enhancements identified in bullet 2.
  NOTE : The objectives 2 depends on the progress from SA2 in Rel-19.

## Slide 10: Outline
Motivation
Proposals
SA2 progress

## Slide 11
SA2 latest progress since SA2#168
The WID for Ambient IoT in SA2 in Rel-19 has been endorsed and the progress is 65% after SA2#168 (April meeting).
The normative work includes:
  Architectures to support Ambient IoT;
  Identification, Subscription, Registration and Connection management;
  Support of Ambient IoT Services (inventory and command)
The normative work in Rel-19 will be finalized in May meeting as planned.
Meeting | Date | Planned TU’s | Actual TU’s | Action plan
SA2#166-Ad Hoc-e | Jan 2025 | 1 | 1 | Start the normative work. Meeting agreed TS skeleton, Scope, Definition, Architecture model and concepts, and Functional description.
SA2#167 | Feb 2025 | 1.5 | 1.5 | Continue with the normative work. Meeting agreed additional Functional description, inventory and command procedures, and NF services.
SA2#168 | Apr 2025 | 2 | 2 | Continue with the normative work, addressing several FFS for AIoT features, AIoT procedures and NF descriptions.
SA2#169 | May 2025 | 2 |  | Continue and finalize the normative work.
Notes: And some potential SA6 work based on SA2 related normative work is as follows:
Exposure for AIoT services to AF: How AF utilizes the exposure of AIoT device information and exposes to the application server;
Information provided by the AF: AIoT service type, Information for AIoT reader selection, Information about the target AIoT device(s) or Information to be used for resource allocation.