## Slide 1: Discussion on 6G proposals
China Mobile

## Slide 2: Background
SA1 has already started studying 6G Use Cases and Service Requirements, with the main discussion focusing on: System and Operational Aspects, AI, Integrated Sensing and Communication, Ubiquitous Connectivity, Immersive Communication, Massive Communication, Industry and Verticals；
In addition to topic that has been/ is discussed topics, the following new topics are proposed to be studied:
  SID proposal on study the task-oriented service orchestration enabler layer
  SID proposal on study the support of AI agent in application enabler layer

## Slide 3: Outline
SID proposal on study the task-oriented service orchestration enabler layer
SID proposal on study the support of AI agent in application enabler layer

## Slide 4: Summary of SA1 requirement
[PR 6.5.6-1] Based on operator policy, the 6G network shall be able to support secure means to expose its services to the authorised third-party AI agent by intent if needed.
[PR 6.12.6-1] Subject to operator’s policy, the 6G network shall be able to expose information from the network to authorized 3rd party AI agents by means suitable for prompt augmentation.
Observation: Driven by the rapid development of AI, AI-related topics are dominating SA1 discussions(in addition to system and Operational Aspects), prompting the need for innovative methods in information exchange and service exposure. To address these challenges, flexible and dynamic service exposure methods, like MCP and A2A, are being considered, with the expectation that they will support dynamic semantic interaction and autonomous task-oriented collaboration (including task decomposition and resource contention resolution), making them appropriate for dynamic collaboration scenarios.
Chart: 
| AI和算网融合 | 系统增强 | 通感一体 | 泛在连接 | 沉浸式通信 | 大规模通信 | 垂直行业 | 其他
提交 | 28 | 73 | 38 | 19 | 23 | 8 | 21 | 18

## Slide 5: Proposal
It is proposed to have a SID on study the task-oriented service orchestration enabler layer, with the following potential objectives:
  Investigate the architecure for a task-oriented enabler layer
  Mechanism to support for intent requirements translation into network task
  Network task classification, spliting
  Network service, information involking, orchestration and exposure
  Basic task (e.g.network optimization) and customized task
UE
VAL
client()
6GS
Vertical application enable layer(s)/SEAL
EDGE Computing
CAPIF
Northbound APIs
CAPIF APIs
task-oriented service orchestration enabler layer
Vertical application server(s)
CN
Management Domain

## Slide 6: Outline
SID proposal on study the task-oriented service orchestration enabler layer
SID proposal on study the support of AI agent in application enabler layer

## Slide 7: What is AI agent
Al Agent defined in TR 22.870
Al Agent: an automated intelligent entity capable of e.g interacting with its environment, acquiring contextual information, reasoning, self-learning, decision-making, executing tasks (autonomously or in collaboration with other Al Agents) to achieve a specific goal.
Figure 02
Optimus Gen2
Unitree Robotics GO2
Embodied AI agent
Multi- modality
Autonomy
Heterogeneous
Collaboration
DeepSeek
Apple
Intell.
DouBao
Virtual AI agent
Personal AI assistant
Changes in information element
Group of AI agents associated with user#3
Group of AI agents associated with user#2
UAV
Group of AI agents associated with user#1
robotic dog
Butler Robot
Multiple AI agents are dynamically networked based on specific tasks
Changes in grouping mode
Changes in Traffic direction
North-South traffic
（Client-Client，Client-Server）
East-West traffic
（e.g. Agent- Agent）
Text， Voice，Video
AI mdel, Token, Feature Vector

## Slide 8: Motivation and Challenges
The increasing demand for computing capabilities
Embodied AI agent needs to offload computing to the network
Difficulty in data/information collection and storage
Provide capabilities for data/information collection, storage, and sharing
Collaboration of multiple AI agents faces challenges
The processing capabilities of different AI agents vary greatly, and the environment dynamically changes,
Requirements for multi-dimensional capabilities
Plenty use cases about AI agent has been discussed in TR 22.870
  Use case#1: End-to-End AI for connected cars
  Use case#2: 6G AI Agent Collaboration with Third-Party AI using LLM
  Use case#3: AI-agents communication
  Use case#4: 6G system assisted AI agent service
  Use case#5: Collaborative AI Agents
  Use case#6: Network knowledge as part of Retrieval Augmented Generation for Generative AI
Notes: reference definition

## Slide 9: Summary of SA1 requirement
[PR 6.2.6-1] The 6G network shall be able to provide computing resource in the operator managed data network (e.g. edge compute domain, service hosting environment) for AI services.
[PR 6.5.6-1] Based on operator policy, the 6G network shall be able to support secure means to expose its services to the authorised third-party AI agent by intent if needed.
[PR 6.7.3-1] Based on user consent and operator policy, the 6G system shall provide a suitable means for an AI agent application on UE to invoke some 3GPP services.
[PR 6.6.6-1] Based on regulatory requirements, operators’ policy and user consent, 6G network shall support trusted network access for 3rd party AI agent and support a mechanism to expose 3rd party AI agent’s attributes (e.g., related users, sensing capabilities, AI capabilities) to other 3rd party AI agents.
[PR 6.6.6-2] Based on regulatory requirements, user consent, operators’ policy and agreement with authorized 3rd party, the 6G network shall be able to support security identification for 3rd party AI agents provided by authorized 3rd party associated with a user (e.g., AI agents belonging to a customer).
[PR 6.8.6-1] The 6G system shall support hosting of large amounts of AI agent applications managed and controlled by the 6G core network and/or multiple AI Agent applications on a UE.
[PR 6.8.6-2] The 6G system shall support secure interoperability between AI Agents and between AI Agents and applications to achieve a collaborative task.
[PR 6.12.6-1] Subject to operator’s policy, the 6G network shall be able to expose information from the network to authorized 3rd party AI agents by means suitable for prompt augmentation.

## Slide 10: Proposal
It is proposed to have a SID on study the support of AI agent in application enabler layer, with the following potential objectives:
  AI agent management(Cross-domain, Cross-vendor)
  Service provisioning：
    new services: intent-requirement translation, Ai agent behaviour monitoring, etc.
    Enhanced services: Agent grouping, Data transmisssion enhancement
  Application enbaler Information exposure (Knowledge, AI agent attribute, etc.)