## Slide 1: Split AI/ML Operation Involving Multiple AIMLE Clients: Use cases and solution option
Yonatan Shiferaw
KPN

## Slide 2: Outline
Introduction
Multi-Client Split AIML Operations
Use cases
Common Issue
Solution Proposal

## Slide 3: Introduction: Key Issue
In TR 23.700-83, key issue 4 introduces Support for Split AI/ML Operations Involving Multiple AIMLE clients.
In this presentation we present the use-cases which involve multi-UE split AI/ML operations, common issues , and proposed solution.

## Slide 4: Multi-Client Split AIML
Concept – difference from Federated Learning:
  Client Centric: Whether collaborating or not the emphasis of split AIML is on clients whose model need to be split between them and nodes in a pipeline.
  Resource Constraint Devices: Offload part of their model (layer) while keeping at least the first layer on the device itself.
  Training/Inference: partial part of the model in the client until a layer called cut layer where the cut layer outputs are sent to server to finish the rest of the training or inference.
  Optimization: on ensuring service continuity during mobility the client can’t simply be replaced.
  Device Constraints: Different UEs with varying device constraints need to be considered to optimally split the model layers.
Training Process:
  Data Sharing: Share the data of subsequent layers while processing raw data in the initial layers at the device.
  Propagation: Forward and backward propagation occur across multiple layers distributed among the UE and the rest of the network nodes.
Use Case:
  Suitable for devices with limited computational resources that want to collaborate in training and inference.

## Slide 5: Use case 1: Enhanced Smart City Surveillance with Mobility
Scenario:
  Surveillance cameras, both stationary and mobile, capture video footage.
Data Transmission:
  Raw video data processed on the cameras, with subsequent layers sent to an edge server for immediate processing
Split Learning:
  AIML split operations enable real-time surveillance and threat detection for public safety.
  Shared pipeline allows collaborative data processing based on resource power, improving surveillance and threat detection.
Mobility Management:
  Pipeline adjustement based on the mobility and resources of the cameras in the pipeline.
Benefits:
  Enhanced Public Safety: Rapid detection and response to security threats.
  Efficient Resource Utilization and Energy Saving: Optimized use of computing resources.
  Improved Mobility Management: Ongoing surveillance coverage with moving units.

## Slide 6: Use case 2: Collaborative Autonomous Driving
Scenario
  A group of autonomous vehicles (AIMLE clients) collaborating by sharing and processing data together.
  One example is shared Local Dynamic Map (LDM) which vehicles collaboratively update while using locally.
Data Transmission
  The raw data is processed locally and sent for subsequent layers in the edge server for immediate processing.
Split AI/ML Operations:
  AIML split operations enable real-time collaboration to optimize driving conditions (e.g., efficient routes).
  Shared pipeline among vehicles enhances optimization, rather than relying solely on individual data.
  Edge server collaboration reduces computational burden and allows collaboration without sharing sensitive data.
Service Continuity:
  Pipeline adjustment when a vehicle changes service area and joins or leaves the shared pipeline.
Benefits:
  Fuel Efficiency: Optimized routes and minimized gaps contribute to reduced fuel usage.
  Traffic Management: Coordinated vehicle actions help ease congestion.
  Enhanced Safety: Faster reaction times lead to a lower risk of accidents.

## Slide 7: Common Issue in All Use Cases: Mobility and Edge Service Area Changes
Scenario:
  UEs (User Equipment) such as autonomous vehicles and surveillance cameras can move and change Edge service areas.
Impact:
  Pipeline Redistribution: The pipeline need to be redistributed according to the resources of the UEs in the pipeline.
Key Points:
  Dynamic Adjustment: Pipeline is adjusted as clients move and change service areas.
  Resource Optimization: The pipeline should be adjusted based on the computing resources of the clients in the pipeline.
Result:
  Service Continuity despite clients join and leave and changes service area due to mobility.

## Slide 8: Solution Proposal
Our solution proposal re-uses and updates and adds additional procedures to clause 8.14 Support for Split AI/ML Operation in TS 23.482 and 8.24 AIMLE context transfer in TS 23.482.
The solution addresses the common issues by:
  Having a pipeline created an AIMLE client when there is no pipeline created found during discovery.
  Have a AIMLE clients join a pipeline when it finds an already created pipeline during discovery.
  Re-adjusting and sending updated pipelines when AIMLE clients join, leaves, or move to different service area.

## Slide 9
Thank you!