## Slide 1: TR 23.947Guidelines for Application Enablement usage and alignment with External Organizations
David Artuñedo
<WI Rapporteur, Telefónica>

## Slide 2: Outline
Deployment Topology
Roles in CAPIF
Discovery Processes
Operational Phases
  CAPIF Onboarding Phase
  EDGEAPP API Publications
  EDGEAPP Registrations
  Runtime Flow
Summary

## Slide 3: Deployment Topology
This TR describes a single operator, single PLMN, single CAPIF Administrative Domain deployment, with one CCF (CAPIF Core Function) managing API onboarding, publication, and access control.
Components:
CCF (CAPIF Core Function): The central registry and policy enforcement point for API providers and invokers in the CAPIF domain.
ECS (Edge Configuration Server): The operator’s edge control-plane entity for registering, tracking, and steering UEs to appropriate edge sites.
EES (Edge Enablement Server): One per edge site (EESA, EESB), managing EAS registrations, handling EDGEAPP EAS Discovery requests, and enforcing service authorization.
EAS (Edge Application Server): One per edge site (EASA, EASB), hosting application services and potentially a SEAL Server.
EEC (Edge Enablement Client): Runs on the UE, interacts with EES/ECS for edge service discovery and selection, and with CCF for CAPIF API access.
EAC (Edge Application Client): Runs on the UE, consumes services from an EAS via the EEC.
SEAL Server: Runs inside an EAS, exposing SEAL APIs for security, group management, or other capabilities.
EASDF (EAS Discovery Function): Optional DNS resolution service to map EAS FQDNs to optimal IP endpoints, used during EDGEAPP discovery.

## Slide 4: Deployment Topology
CORE DATACENTER
EDGE NODE A
ECS
EES-A
EAS-A (SEAL)
EES-B
EAS-B (SEAL)
CCF
Transport Network
Access Network
UE 1
EEC-1
EAC-1
UE 2
EEC-2
EAC-2
EASDF
gNB
gNB
NEF

## Slide 5: Roles in CAPIF
Entities will play one or combination of roles in CAPIF domain
EES and EAS are dual-role CAPIF participants:
  API Provider (AEF): Expose their own APIs (Edge services, SEAL APIs) via CCF.
  API Invoker: Consume APIs from ECS, other EES/EAS, or SEAL services in other sites.
  They register twice in onboarding — once as a provider, once as an invoker.
ECS is an API provider in CAPIF (control-plane services).
EEC is a CAPIF Invoker — it performs API discovery and token requests on behalf of EACs.
EACs are not CAPIF invokers — they rely on the EEC to get service endpoints and tokens.
SEAL Servers don’t onboard directly into CAPIF — their APIs are published as part of their host EAS’s CAPIF provider registration.
NEF is an API provider in CAPIF (exposing 5G Core APIs)

## Slide 6: Two Discovery Processes
There are two Discovery processes involved
1. EDGEAPP EAS Discovery (which Edge Aplication Server to use):
EEC sends EAS_Discovery_Request to the serving EES (two options).
Request may include filters: service type, location, features, KPI hints.
EES authorizes the request and returns a filtered list of matching EAS instances.
(Optional) EES queries EASDF to resolve the EAS FQDN to an optimal IP before returning.
EEC selects the most suitable EAS.
2. CAPIF API Discovery (how to call it):
EEC (or EAS acting as an invoker) queries the CCF for API definitions and policies of the chosen provider.
Requests a CAPIF access token scoped to that provider and specific APIs.
Receives endpoint references, OpenAPI specs, and authorization tokens.
Rule: Run EDGEAPP EAS Discovery first, then CAPIF API Discovery for the chosen EAS.

## Slide 7: Operational Phases
CAPIF Onboarding Phase
1. Onboarding (CCF)
All CAPIF entities register with the CCF according to their role(s).
EES, EAS, ECS register as Providers (AEFs).
EES, EAS, and EEC register as Invokers.
The CCF establishes identities, credentials, and trust anchors for secure operation.

## Slide 8: Operational Phases
EDGEAPP API Publications
2.1 API Publication
Each API provider publishes its APIs to the CCF (CAPIF_API_Publish_Request).
SEAL APIs are published through the hosting EAS’s provider registration.

## Slide 9: Operational Phases
EDGEAPP Registrations
2.2 EES & EAS Registration in ECS
EESs & EASs are registered as API Invokers to consume ECS APIs
EESs and EASs Discover ECS APIs
ECS registers EES and EAS instances in the edge inventory (EDGEAPP control-plane, not CAPIF).

## Slide 10: Operational Phases
Runtime Flow
3. Runtime Flow
App Request: EAC requests a service from EEC.
EAS Discovery (EDGEAPP):
  Synchronous EEC → EES: EAS_Discovery_Request(...)
  Subscribe/Notify EEC → EES EAS_Discovery_Subscribe (...)/EAS_Discovery_Notify (…)
EEC discover EAS APIs in CAPIF and request token
EEC Creates Application context
EAC Invokes EAS (SEAL) API

## Slide 11: Operational Phases
Runtime Flow
4.CAPIF API Discovery:
EEC → CCF: CAPIF_API_Discover_Request (providerId=EAS)
EEC → CCF: CAPIF_API_Access_Token_Request (scopes=...)
EEC forwards endpoint + token to EAC (pass-through) or keeps token for proxy calls.
EAC → EAS: API request with token.
EAS validates token via CAPIF trust chain.

## Slide 12: Summary
Deployment Topology for guiding the examples
CAPIF Roles are defined and explained for each EDGEAPP & SEAL entity
Both CAPIF Discovery and EAS Discovery process are explained and combined
Operational flow explain several phases: CAPIF Onboarding Phase for EDGEAPP & SEAL entities, EDGEAPP API Publications in CFF, EDGEAPP entities Registrations in ECS & Runtime Flow to show API Consumption from UE