## Slide 1: CAPIF_Ph4 Discussion paper on discovered service API operations
Linked to S6-253131: CAPIF_Ph4 Key Issue Discovered service API operations
Fogus, Apple, Telefonica, UMA

## Slide 2: Key Issue Motivation
Expand the way that a CAPIF API invoker consumes Service APIs from a CAPIF API provider (3GPP standardized or not) so it can send information to the CAPIF API provider.
E.g., a third-party application that interacts through CAPIF with the core network functions (e.g., NEF, NWDAF), feeds the network core with data and/or requests for some actions from the network core.

## Slide 3: CAPIF_Publish_Service_API
The CAPIF publish service APIs, as defined in 3GPP TS 23.222 [2], allow API publishing function via CAPIF-4 and CAPIF-4e reference points to publish and manage published service APIs at the CAPIF core function
*The direction of the arrows depicts the direction of the information flow

## Slide 4: CAPIF_Discover_Service_API
The CAPIF discover service APIs, as defined in 3GPP TS 23.222 [2], allow API invokers via CAPIF-1/1e reference points to discover service API available at the CAPIF core function.
*The direction of the arrows depicts the direction of the information flow

## Slide 5: CAPIF_Discover_Service_API
To discover service APIs available at the CAPIF core function, the consumer (e.g. API invoker) shall send an HTTP GET message with the API invoker Identifier or CAPIF core function Identifier and query parameters to the CAPIF core function as specified in clause 8.1.2.2.3.1 (TS 29.222)

## Slide 6
The Service API information includes only the supported Service API operation(s), but no means to describe an associated required message body. This limits the usability of the Service API from the CAPIF API invoker.
Practically the API provider can make GET HTTP requests; but POST, PUT and PATCH requests cannot be conducted since the body of the discovered Service API is not known to the API invoker
CAPIF_Discover_Service_API
*The direction of the arrows depicts the direction of the information flow
GET
HTTP calls

## Slide 7
The Service API information includes only the supported Service API operation(s), but no means to describe an associated required message body. This limits the usability of the Service API from the CAPIF API invoker.
Having information related to the Service API body, the CAPIF API invoker can create calls towards the CAPIF API provider that include requests for an action or data (though POST, PUT, PATCH HTTP calls)
CAPIF_Discover_Service_API
Example: Feed NWDAF with data from third party application
Third party application
NWDAF
(or NEF which communicates with NWDAF)
POST, PUT, and PATCH HTTP calls
*The direction of the arrows depicts the direction of the information flow

## Slide 8: Discovered Service API operations
Way forward
Apply the changes required, so that the CAPIF API invoker (the piece of code that implements the invocation) gets information of the body of the discovered Service API. Thus, it can send information to the API invoker automatically (i.e., the related HTTP calls (e.g., PUT, POST) are done a) without any manual search for the actual API structure from the API invoker programmer and b) with guaranteed compatibility with the actual API implementation* of the Service API from the API Provider
*implementation-wise specificities/ deviations might apply even for standardized APIs, e.g., attributes are missing, not fully supported etc.

## Slide 9: Solution for current implementations - Option 1: Take advantage of the Vendor extensibility feature
[Clause 7.11 – 3GPP TS 29.222]..The query parameters used in GET requests in the CAPIF APIs shall be extensible with vendor-specific query parameters as specified in clause 5.2.13.3 of 3GPP TS 29.122..

## Slide 10: Recap on the extensibility feature in CAPIF
Data models (used in Publish)
  Extend the information element with vendor specific fields
  Fields have specific naming schemes:
Using the 6-digit IANA-assigned enterprise code "vendorSpecific-010415": {
...
}
Using domain name "vendorSpecific-3gpp.org": {
...
}
Using URN "vendorSpecific-urn:3gpp:example": {
...
}
Query Parameters (used in Discover)
  Provisioning of vendor-specific query parameters to support additional vendor-specific filtering criteria
  A vendor-specific query parameter shall be encoded as follows:
query parameter name: "vend-spec-<query parameter name>”
query parameter value encoded as JSON object
  "target"
  "value"

## Slide 11
Using the URN representation
  vendorSpecific-urn:body:<resource_name>:info
    The underlined are required keywords so that it can be easy to distinguish among actual vendor-specific objects
Data structure (three options are proposed*)
  url : URL to a swagger describing the API OR
  schema: JSON describing the API OR
  ref: Documents describing the API (e.g. Technical Specifications)
  *The three option are given as a workaround for bodies that are too large and also for matters of completeness (e.g. to have a reference what each parameter describes)
Solution for current implementations - Option 1: Take advantage of the Vendor extensibility feature

## Slide 12: Implementation Paradigm (for the NEF Traffic Influence API)