## Slide 1: N6 delay considerations
Walter Featherstone
Apple

## Slide 2: Outline
Present triggering and use of N6 delay within the core network
  TS 23.501 / TS 23.548
Present example of use of UE to PSA UPF delay within the core network
  TS 23.502 / TS 23.503 Session with QoS
Highlight EDGEAPP service KPIs are defined as e2e
Present EDGEAPP use of AF influence on traffic routing
  Highlight opportunity to leverage N6 delay

## Slide 3: Application Function influence on traffic routing, clause 5.6.7 of TS 23.501
Table 5.6.7-1: Information element contained in AF request
  Information Name: Indication of considering N6 delay
  Applicable for PCF or NEF: Indicates that N6 delay should be considered (NOTE 9).
  Category: Optional
  NOTE 9: When the Indication of considering N6 delay is provided, N6 delay measurement information as part of EDI, as described in Table 6.2.3.4.1 of TS 23.548 needs to be used to perform measurements.
  For each information element mentioned above in the AF request, the detailed description is as follows:
  17) Indication of considering N6 delay. This is used to trigger the N6 delay measurement and indicate that N6 delay measurement, if available, should be considered by the SMF to (re)select the PSA UPF(s) or trigger EAS(es) (re)discovery.

## Slide 4: N6 Delay Measurement and Reporting, clause 5.8.2.23* of TS 23.501
The candidate UPF(s) may be configured by the SMF, as described in clause 4.4.3 of TS 23.502, to measure the N6 delay for the connection between the UPF and measurement endpoint(s) in the DN (represented by one or more IP address(es)).
AF provides the information to support N6 delay measurement via EAS Deployment Information Management as described in clause 6.2.3.4 of TS 23.548. SMF retrieves the EDI information to configure the candidate UPF(s) for the N6 delay measurement.
AF may trigger the N6 delay measurement by providing Indication of considering N6 delay measurement through AF influence as described in clause 5.6.7.
*See backup for full clause text

## Slide 5: Selection of an UPF for a particular PDU Session, clause 6.3.3.3 of TS 23.501
The following parameter(s) and information may be considered by the SMF for UPF selection and re-selection:
  …
  N6 delay between the candidate UPF(s) and measurement endpoint in the DN as specified in clause 5.8.2.23.

## Slide 6: EAS Deployment Information Management, clause 6.2.3.4 of TS 23.548
EAS Deployment Information management refers to the capability to create, update or remove EAS Deployment Information from AF and the distribution to the SMF or to the I-SMF in case I-SMF based Local Offloading Management applies. The NEF is in charge of the management of EAS Deployment Information which may be stored in UDR.
Table 6.2.3.4-1 Description of EAS Deployment Information
NOTE 4: A measurement endpoint can be used for delay measurements representing a single EAS IP address or a range (IPv4 subnet or IPv6 prefix) of EAS IP addresses. SMF provides the measurement endpoint information together with Network Instance information to the candidate UPF(s) to perform N6 delay measurements.
NOTE 5: The N6 delay measurement assistance information is utilized when AF traffic influence request includes indication of considering N6 delay as defined in clause 5.6.7.1 of TS 23.501.
NOTE 6: Some examples of the measurement protocol(s) considered for N6 delay measurements are listed in clause 5.8.2.23 of TS 23.501 .

## Slide 7: EAS Deployment Information Management, clause 6.2.3.4 of TS 23.548
The AF provides non-PDU Session specific EAS Deployment information to 5GC via the procedure defined in this clause.
2. ... The NEF derives DNN and S-NSSAI from the AF Service Identifier if not received explicitly and translates received External Application Identifier to Application Identifier known inside MNO domain. If there is an existing EAS address information for a DNAI configured via OAM, NEF also ensures that any EAS IP address range Information per DNAI in EAS Deployment Information does not contradict with the existing information.

## Slide 8: Session with QoS, TS 23.502 & TS 23.503
23.502, 5.2.6.9.2 Nnef_AFsessionWithQoS_Create service operation
  Description: The consumer requests the network to provide a specific QoS for an AF session for a UE or a list of UEs.
23.502, 5.2.6.33.2 Nnef_AF_request_for_QoS_Create service operation
  Description: The consumer requests the network to provide a specific QoS for a traffic flow for a UE or a group of UEs.
Inputs, Optional: … RT Latency Indication as described in clause 6.1.3.22 of TS 23.503
23.502, 6.1.3.22 AF session with required QoS
  The AF may request that a data session to a UE is set up with a specific QoS (e.g. low latency or PDV) and priority handling. The AF can request the network to provide QoS for the AF session based on the service requirements with the help of a QoS Reference parameter that refers to pre-defined QoS information. Instead of the QoS Reference, the AF may provide individual QoS parameters associated to the Flow Description.
23.502, 6.1.3.27.2 UL/DL policy control based on round-trip latency requirement
  The AF may provide a round-trip (RT) latency indication together with a single direction delay requirement between the UE and the PSA UPF expressed as the QoS Reference or the individual QoS parameters (as described in clause 6.1.3.22). The RT latency indication indicates the need to meet the RT latency requirement of the service data flow, i.e. doubling of the single direction delay requirement between the UE and the PSA UPF.

## Slide 9: EDGEAPP Service KPIs, TS 23.558
Table 8.2.3-1: AC Service KPIs
  Information Element: Response time
  Status: O
  Description: Response time (NOTE) required for the server servicing the requests.
  NOTE: The response time includes the round-trip time of the request and response packet, the processing time at the server and the time required by the server to consume 3GPP Core Network capabilities, if any.
Table 8.2.5-1: EAS Service KPIs
  Information Element: Maximum Response time (NOTE)
  Status: O
  Description: The maximum response time advertised for the AC's service requests.
  NOTE: The maximum response time includes the round-trip time of the request and response packet for communication between the AC and EAS, the processing time at the server and the time required by the server to consume 3GPP Core Network capabilities, if any.
Response time E2E between AC & EAS and therefore includes N6 component of the delay

## Slide 10: EDGEAPP: AF influence on traffic routing
[AR-5.2.8.2-a] The application layer architecture shall support AF influence on traffic routing over N6 interface.
8.6.7 Application traffic influence trigger from EAS
  To utilize this EES offered service, EAS (or CAS) request simply includes EASID and target UE(s)
  The EES then makes the request towards the CN: “the EES includes transaction ID, target DNAI, traffic descriptor information and N6 routing information at target DNAI in the Nnef_TrafficInfluence_Create Request to the NEF, or Npcf_PolicyAuthorization_Create Request to the PCF, to influence the traffic for EAS”
    The option to include “Indication of considering N6 delay” is not specified along with the prerequisite of providing EAS Deployment Information (EDI) to the CN
8.10.3 Capabilities utilized by EES and CES
  AF traffic influence functionality, including the user plane path management event notifications of the UE, from the 3GPP core network either directly (e.g. via PCF) or indirectly (i.e. NEF/SCEF+NEF)

## Slide 11: EDGEAPP: Provisioning & registration
8.3.3 Service provisioning
  “After the EEC establishes a connection to an EES using information received in step 2, the EES can issue an AF request to influence traffic routing as specified in 3GPP TS 23.501 clause 5.6.7 in order to influence the user plane path to this connected EES”
8.4.3 EAS Registration
  “For registered EAS(s), the EES can request AF traffic influence for any UE, which is implementation specific”
  Highlights that AF influence on traffic routing doesn’t have to be initiated by the EAS

## Slide 12: EDGEAPP: EAS discovery (8.5)
EES processing of the request: “If the EEC indicates that service continuity support is required, when identifying the EAS, the EES shall take the indication which ACR scenarios are supported by the AC, the EEC, the EES and the EAS and which of these are preferred by the AC into consideration. The EES may select one EAS and determine whether to perform application traffic influence for this EAS in advance based on AC's service KPI or EAS’s service KPI in desired response time, when the EAS does not perform traffic influence in advance. If the EES determines to perform application traffic influence for this EAS in advance, then the EES will applies the AF traffic influence of the EAS in the 3GPP Core Network before sending EAS discovery response”
  AC’s service KPIs are E2E, implying N6 component of delay should be accounted for
The response: “If the EES perform traffic influence for EAS(s) in step 2, then the discovered EAS(s) is with optimized traffic route. Depending on the EAS discovery filters received in the EAS discovery request, the response may include additional information regarding matched capabilities, e.g. service permissions levels, KPIs, AC locations(s) that the EASs can support, ACR scenarios supported by the EAS, etc.”
  Note that in the response (see table 8.5.3.3-1), “Traffic influence performed indication” is present only when the “EAS selection request indicator” is provided in the EAS discovery request message
  The service KPIs that an EAS can support are E2E, implying N6 component of delay should be accounted for

## Slide 13: EDGEAPP: ACR management events (8.6.3)
"ACR facilitation". This event supports to detect user plane path change for the application traffic, make the decision for ACR, discover the T-EAS(s), influence the traffic for the selected T-EAS and report the corresponding notification with the selected T-EAS.
  Highlights the relevance of notifications relating to PSA UPF reselection that can be influenced by inclusion of “Indication of considering N6 delay” (see slide 3)
8.6.3.2.2 Subscribe: d. The EAS may include the "ACR facilitation" event to request the EES to make the decision for ACR, discover the T-EAS(s), influence the traffic for the selected T-EAS and notify the S-EAS of the selected T-EAS. If required, the EAS can add an indication to request service continuity planning.
8.6.3.2.3 Notify: d. If "ACR facilitation" Event is subscribed, based on the detected user plane path change report sent from the 3GPP core network, the EES checks whether any T-EAS is available as described in steps 2-4 of clause 8.8.3.2. If a T-EAS is available, the EES selects the T-EAS from the discovered EAS list and applies the AF traffic influence with the N6 routing information of the selected T-EAS in the 3GPP Core Network. The EES also notifies the S-EAS with the selected T-EAS endpoint.
  ”N6 routing information” (another optional attribute of the AF traffic influence) highlighted, but not the option of “Indication of considering N6 delay” (similarly for Service continuity described in clause 8.8)

## Slide 14: EDGEAPP: EAS Info provisioning (8.15)
The EEC sends the EAS information provisioning request to the EES
  If the request contains selected EAS ID and selected EAS Endpoint, the EES may apply the EAS traffic influence with the N6 routing information of the EAS in the 3GPP Core Network, based on application KPIs and if the EAS traffic influence was not done before (e.g. neither in EAS discovery procedure nor the EAS perform traffic influence).
    The service KPIs that an EAS can support are E2E, implying N6 component of delay should be accounted for
  EES can also influence the EAS traffic in advance.

## Slide 15: Summary
The 5GC exposes the capability for an AF to influence traffic routing
  The AF originated request can include an indication to consider N6 delay. For that to be actioned, EAS deployment information needs to have been provided to the CN
The EES in EDGEAPP leverages the AF influence on traffic routing capability (which can be triggered by an EAS or directly by the EES) in various scenarios
  However, although providing “N6 traffic routing information” is highlighted, there is no reference to the use of “indication of considering N6 delay”
  or EAS Deployment Information (in particular, the “N6 delay measurement assistance information”) required by the 5GC to perform N6 measurements
The 5GC has the capability to perform N6 measurements
  The measurement results are leveraged within the 5GC but not exposed even to the AF that provides the assistance information necessary to perform such measurements
  Availability of N6 measurements at the enabler layer would facilitate appropriate KPI related requests towards the 5GC, e.g., AF Session with QoS in which the round-trip latency accounts only for the UE to PSA UPF portion of the AC to EAS communication path

## Slide 16: Proposal
Make explicit reference to “indication of considering N6 delay” with respect to AF influence on traffic routing
Capture the ability for an EES to provided EAS deployment information to the 5GC
Send LS to SA2 highlighting that SA6 sees benefit in exposing N6 measurement results and request SA2 to do so

## Slide 17: Backup

## Slide 18: N6 Delay Measurement and Reporting, clause 5.8.2.23 of TS 23.501
The candidate UPF(s) may be configured by the SMF, as described in clause 4.4.3 of TS 23.502 [3], to measure the N6 delay for the connection between the UPF and measurement endpoint(s) in the DN (represented by one or more IP address(es)).
NOTE 1: The measurement endpoint in the DN used for delay measurements can be a single EAS IP address, for instance when the measurement endpoint is deployed within the same IP host as the EAS itself. Alternatively, the measurement endpoint used for delay measurements can be multiple EAS IP addresses within a certain IP address prefix/subnet, for instance when the measurement endpoint is deployed in a node such as a router or load balancer on path or close to the EAS. Hence the delay from the node to any of the EAS is considered as negligible.
NOTE 2: The N6 delay measurements are per measurement endpoint, hence are independent from any UE PDU Session.
AF provides the information to support N6 delay measurement via EAS Deployment Information Management as described in clause 6.2.3.4 of TS 23.548 [130]. SMF retrieves the EDI information to configure the candidate UPF(s) for the N6 delay measurement.
AF may trigger the N6 delay measurement by providing Indication of considering N6 delay measurement through AF influence as described in clause 5.6.7. The SMF may also trigger the N6 delay measurement based on local configuration after it is provisioned with the N6 delay measurement assistance information as part of EAS Deployment Information. The SMF requests the candidate UPF(s) (via N4 association procedures described in clause 4.4.3 of TS 23.502 [3]) to perform the N6 delay measurement between the UPF and measurement endpoint and to report the N6 delay measurement to SMF. The request includes the following information: measurement endpoint address (e.g., EAS IP address and optionally port number) together with a Network Instance for N6, measurement protocol (e.g. TWAMP (IETF RFC 5357 [211]), OWAMP (IETF RFC 4656 [212]), STAMP (IETF RFC 8762 [213]), or other protocols that satisfy the security requirements given in clause T.5 of TS 33.501 [29]), protocol-specific configuration parameters. The UPF leverages the measurement protocol and Network Instance for N6 information to measure the N6 delay. Then, the candidate UPF(s) report the N6 delay measurement and the corresponding endpoint address to the SMF (via the N4 association report procedure described in clause 4.4.3 of TS 23.502 [3]. N6 delay measurement reporting is triggered based on the reporting frequency and/or reporting threshold provided as part of the configuration.
The SMF may (re)select the PSA UPF(s) or trigger EAS(es) (re)discovery by considering N6 delay measurement result as described in clause 6.2.3.2 of TS 23.548 [130].