## Slide 1: KPN 6G Proposal - Application Enablement Layer Support for Digital Twins
Yonatan Shiferaw
KPN N.V.

## Slide 2: 6G-study Proposal Overview: Application Enablement Layer Support for Digital Twins
Background/Motivation
  SA1, as part of the Study on 6G Use Cases and Service Requirements in TR 22.870, includes a use case for Real Time Digital Twins – which covers the application digital twins aspects.
  Network Digital Twins is already addressed by SA5 in Rel-19 study in TR 28.915 and being specified in TS 28.561.
  However, what remains unaddressed is application digital twins.
  ETSI addresses in TR 103 844 and TS 103 845 Digital Twins standardization opportunities and communication requirements.
  SA6 is then a right place to study the application layer digital twins consideration application requirements.
Objectives
  Analyze 6G requirements and identify enabler layer impact for enabling Digital Twins applications.
  Study the Architectural requirements for Application Layer support for Digital Twins Services
  Study architectural and functional implications on existing SA6 application enablers (Eg. ADAE, AIMLAPP, Metaverse_App)
  Identify potential solutions, including the information flows and developer-friendly application enablement APIs, where necessary to satisfy the architectural requirements and enhancements identified.

## Slide 3: What is digital twins?
Digital twins is a technology that allows a digital representation of a real-world object or system.
It can either simulate or emulate the real-world object or system.
In addition to observations, it can be part of the feedback loop of the real-world object or system.
In 3GPP, we can see Digital Twins from two aspects:
  Use of Digital Twins for 6G Network Management: Network Digital Twins
  Enabling Digital Twins for applications over 6G: Application Digital Twins

## Slide 4: Rel-19 SA5 work on Network Digital Twins
3GPP SA5 is working on Release 19 Specification on NDT - TS 28.561. The Study is found in TR 28.915 which is complete.
Network Digital Twins is a digital twin modelling of an object of a communication network.
It allows to learn how an actual mobile network would behave in certain scenarios, without causing any changes to the actual mobile network.
The implementation of an NDT can rely on simulation, emulation, AI-based modelling, or any other technique that enables the NDT to mimic the behaviour of the network.
Figure from TR 28.915

## Slide 5: Rel-20 SA1 study on 6G requirements for Application Digital Twins
SA1, as part of the Study on 6G Use Cases and Service Requirements in TR 22.870, includes a use case for Real Time Digital Twins – which covers the application digital twins aspects.
An Application Digital Twin is a digital twin modelling the characteristics and behaviour of a real-world object or system such as in industry, smart cities, or construction sectors.
It allows interaction, control, prediction, test, maintenance, and management of processes and components.
It is created using data from multiple sources: database, sensors, tags, network data, data models.

## Slide 6: Rel-20 SA1 study on 6G requirements for Application Digital Twins
SA1, as part of 6G study in TR 22.870, identifies the following digital twin applications under the Use case on Real Time Digital Twins in clause 11.3 :
  Manufacturing plant
  Water management and improved traffic management (smart cities)
  Aggregation of sub-DT to cover complex systems (e.g. full smart cities)
  Digital twins in port operations.
NOTE: The SA1 6G study is still ongoing and additional use cases are expected.

## Slide 7: ETSI – Standardization Activities
ETSI TR 103 844 - SmartM2M - Digital Twins and Standardization Opportunities in ETSI (https://www.etsi.org/deliver/etsi_tr/103800_103899/103844/01.01.01_60/tr_103844v010101p.pdf)
ETSI TS 103 845 - SmartM2M- Digital Twins Communication Requirements (https://www.etsi.org/deliver/etsi_ts/103800_103899/103845/01.01.01_60/ts_103845v010101p.pdf)
ETSI TR 103 844
ETSI TS 103 845

## Slide 8: Role of SA6 in enabling Application Digital Twins
SA6 as the Application Enablement Layer could play a vital role in supporting Application Digital Twins.
  It can play a role in registering devices and data sources, and collecting data from the devices and/or data sources that are involved in the creation of a Digital Twin.
  It can play a role in training and update of digital-twins models using existing SA6 services such as AIML and ADAE.
  It can play a role in use of the digital-twins models for inference and analytics using AIML and ADAE.
  It can play a role in creation, storing, discovery and selection of application digital twins.
Network Digital Twins is most suitable to SA5 and SA5 has already done some work in Release 19.

## Slide 9: Application Enablement Layer Support for Digital Twins (6G study proposal)
As part of SA6 6G study we propose we study the following:
  Analyze 6G requirements and identify enabler layer impact for enabling Digital Twins applications.
  Study the Architectural requirements for Application Layer support for Digital Twins Services
  Study architectural and functional implications on existing SA6 application enablers such as AIMLE and ADAE.
  Identify potential solutions, including the information flows and developer-friendly application enablement APIs, where necessary to satisfy the architectural requirements and enhancements identified.
NOTE 1: The study is dependent upon the completion of the 6G requirements in SA1.