TSG-T Working Group1 SWG SIG meeting #5	 TSGT1S#5     (99) 048

Kobe, 13-14 Sept 1999

Agenda Item:		Review of Specifications

Source: 		Anritsu Limited

Title: 		Proposal for RLC Interoperability tests

Document for:		Discussion

# Summary

| RLC process | Requirement | Core Requirements / Working assumptions | Possible Test cases / Comments |
| --- | --- | --- | --- |
| RLC State Variables | MS uses sequence numbering correctly | TS 25.322 / 9.4 7G99-010 v 250 / 43.1.2.1 & 43.1.3.1 | Sequence numbers start at 0 and wrap at 212-1. Test uplink and downlink |
|  | MS uses window correctly | TS 25.322 / 9.4 7G99-010 v 250 / 43.1.2.2 & 43.1.3.2 | MS discards PUs with N(S) VR(MR) MS does not transmit PUs with VT(S) VT(MS) Test uplink and downlink. |
| RLC Timers | Timer_Poll | TS 25.322 / 9.5 | See operation of polling |
|  | Timer_Poll_Prohibit |  | See operation of polling |
|  | Timer_EPC |  | TBD |
|  | Timer_Discard |  | Timer based discard tests |
|  | Timer_Poll_Periodic |  | See operation of polling |
|  | Timer_Status_Prohibit |  | Operation of Timer_STATUS |
|  | Timer_Status_Periodic |  | Operation of Timer_STATUS |
|  | Timer_RST |  | See protocol error recovery |
| Protocol Parameters | MaxDat | TS 25.322 / 9.6 | Timer based discard tests |
|  | Poll_PU |  | See operation of polling |
|  | Poll_SDU |  | See operation of polling |
|  | Poll_Window |  | See operation of polling |
|  | MaxRST |  | See operation of Reset mechanism |
|  | Window_Size |  | See MS uses window correctly |
| Retransmission | Acknowledgements are sent when requested | TS 25.322 / 9. | See operation of polling |
|  | Retransmission takes place when requested |  | See operation of polling |
|  | Polling occurs when it should |  | See operation of polling |
|  | SDU Discard occurs when it should |  | Timer based discard tests |
|  | The Estimated PDU counter operates correctly |  | TBD |
| Flow Control | Credit and peer-to-peer flow control | TS 25.322 |  |
|  | Local flow control |  |  |
| Error Correction | Triggering of Polling | TS 25.322 | See operation of polling |
| Protocol error detection and recovery |  | TS 25.322 | See operation of Reset mechanism |
| RLC Header compression |  | TS 25.322 |  |

## RLC testing

### Transparent mode

#### Segmentation and reassembly

##### Definition and applicability

All MS.

##### Conformance requirement

?

Reference(s)

##### Test purpose

/Are segmentation and reassembly of transparent PDUs implicitly tested by sending/receiving messages on the relevant control channels?]

##### Method of test

Initial conditions

Related ICS/IXIT Statement(s)

Test procedure

##### Test requirements

### Unacknowledged mode

#### Segmentation and reassembly

##### Definition and applicability

All MS.

##### Conformance requirement

All MS.

Reference(s)

?

##### Test purpose

/Are segmentation and reassembly of unacknowledged PDUs implicitly tested by sending/receiving messages on the relevant channels?]

Possible tests: Unacknowledged mode is correctly selected for the DTCH according to bearer/traffic type.

##### Method of test

Initial conditions

Related ICS/IXIT Statement(s)

Test procedure

##### Test requirements

### Acknowledged mode

#### Segmentation and reassembly

##### Definition and applicability

All MS.

##### Conformance requirement

?

Reference(s)

##### Test purpose

[Implicitlly tested?]

##### Method of test

Initial conditions

Related ICS/IXIT Statement(s)

Test procedure

##### Test requirements

#### Concatenation

##### Definition and applicability

All MS.

##### Conformance requirement

?

Reference(s)

##### Test purpose

[Implicitlly tested?]

##### Method of test

Initial conditions

Related ICS/IXIT Statement(s)

Test procedure

##### Test requirements

#### Correct use of Sequence Numbering on the Uplink

##### Definition and applicability

All MS that support Acknowledged mode RLC.

##### Conformance requirement

PUs are sequentially and independently numbered and may have the value 0 through n minus 1 (where n is the modulus of the sequence numbers). The modulus equals 212 for AM.

[Note: no definition for initial Sequence Number on start of Radio Bearer. This is assumed to be 0]

Reference(s)

TS 25.322 / 9.4

##### Test purpose

- To verify that the MS transmits the first PDU with the Sequence Number field equal to 0.

- To verify that the MS increments the Sequence Number field according to the number of PUs transmitted.

- To verify that the MS wraps the Sequence Number after transmitting the 212-1th PU.

##### Method of test

Initial conditions

The MS is attached to (registered on) the network and in idle mode.

Related ICS/IXIT Statement(s)

TBD

Foreseen Final State of the MS

The same as the initial conditions.

Test procedure

The MS sets up an uplink connection comprising a Radio Bearer with the following parameters:

RLC mode	Acknowledged

PU size	1 PU per PDU

RLC transmission window size	4096

Transmission RLC discard	Disabled

Polling info	TBD

The MS transfers a minimum of 4096 RLC PUs to the SS

The MS terminates the connection.

Expected sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | MS -> SS | RB ESTABLISHMENT | See generic procedures |
| 2 | MS -> SS | UPLINK RLC PDU | SN should be set to 0 |
| 3 | MS -> SS | UPLINK RLC PDU | SN should be set to 1 |
| 4 |  | SS responds to Polls normally |  |
| 5 | MS -> SS | … | Transfer of RLC PDUs continues to SN = 4095 |
| 6 | MS -> SS | UPLINK RLC PDU | SN should be set to 0 |
| 7 | MS -> SS | RB RELEASE | Optional step |

##### Test requirements

The first PDU transmitted should have the SN field set to 0. The second PDU should have the SN field set to 1, and the 4096th PDU should have the SN field set to 0.

#### Correct use of Sequence Numbering on the Downlink

##### Definition and applicability

All MS that support Acknowledged mode RLC.

##### Conformance requirement

PUs are sequentially and independently numbered and may have the value 0 through n minus 1 (where n is the modulus of the sequence numbers). The modulus equals 212 for AM.

[Note: no definition for initial Sequence Number on start of Radio Bearer. This is assumed to be 0]

Reference(s)

TS 25.322 / 9.4

##### Test purpose

- To verify that the MS correctly indicates that it failed to receive the first PU when the first PU has the Sequence Number field set to 1.

- To verify that the MS increments the Sequence Number field according to the number of PUs received.

- To verify that the MS correctly indicates that it failed to receive the a PU when the sequence of PUs runs: …, 4094, 4095, 1.

##### Method of test

Initial conditions

The MS is attached to (registered on) the network and in idle mode.

Related ICS/IXIT Statement(s)

TBD

Foreseen Final State of the MS

The same as the initial conditions.

Test procedure

- The SS sets up an downlink connection comprising a Radio Bearer with the following parameters:

RLC mode	Acknowledged

In-sequence delivery	TRUE

PU size	1 PU per PDU

Reception RLC discard timer	Disabled

RLC reception window size	4096

Downlink RLC status Info	TBD

The SS transfers the first PU with the SN field set to 1

The SS transfers the next PU with the SN set to 2, and the Polling bit set to 1.

The SS continues transferring PUs with sequential numbers until a STATUS from the MS is received indicating retransmission of PU number 0.

The SS continues transferring PUs with sequential numbers up to the following sequence: …, 4094, 4095, 1. The next PU (SN=2) is transmitted with the Polling bit set to 1.

The SS continues transferring PUs with sequential numbers until a STATUS from the MS is received indicating retransmission of PU number 0.

The SS terminates the connection.

Expected sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | SS -> MS | RB ESTABLISHMENT | See generic procedures |
| 2 | SS -> MS | DOWNLINK RLC PDU | SN = 1 |
| 3 | SS -> MS | DOWNLINK RLC PDU | SN = 2, P=1 |
| 4 | MS -> SS | STATUS PDU | Indication only SN=1 has been received |
| 5 | SS -> MS | DOWNLINK RLC PDU | Transfer of RLC PDUs continues to SN = 4095 |
|  |  | SS continues polling periodically |  |
| 6 | SS -> MS | DOWNLINK RLC PDU | SN = 1 |
| 7 | SS -> MS | DOWNLINK RLC PDU | SN = 2, P=1 |
| 8 | MS -> SS | STATUS PDU | Indication than SN=0 has not been received |
| 7 | MS -> SS | RB RELEASE | Optional step |

##### Test requirements

The MS will indicate in a STATUS PDU that the PU with SN = 0 was not received before the PU with SN = 1.

The MS will indicate in a STATUS PDU that the PU with SN = 0 was not received after the PU with SN = 4095, and before the PU with SN = 1.

#### Control of Transmit Window

##### Definition and applicability

All MS that support Acknowledged mode RLC.

##### Conformance requirement

The transmitter shall not transmit a new PU if VT(S) VT(MS).

Reference(s)

TS 25.322 / 9.4

##### Test purpose

- To verify that the MS does not transmit PUs with sequence numbers outside of the transmit window.

##### Method of test

Initial conditions

The MS is attached to (registered on) the network and in idle mode.

Related ICS/IXIT Statement(s)

TBD

Foreseen Final State of the MS

The same as the initial conditions.

Test procedure

- The MS sets up an uplink connection comprising a Radio Bearer with the following parameters:

RLC mode	Acknowledged

PU size	1 PU per PDU

RLC transmission window size	4096

Transmission RLC discard	Enabled

Polling info	TBD

The MS continually transfers PUs with the correct sequence numbers.

The SS does not respond to poll requests from the MS.

The SS continues monitoring transmissions, at minimum for 4096 transmission time intervals, not including those used for retransmissions.

The SS terminates the connection.

Expected sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | MS -> SS | RB ESTABLISHMENT | See generic procedures |
| 2 | MS -> SS | UPLINK RLC PDU | SN = 0 |
| 3 | MS -> SS | UPLINK RLC PDU | SN = 1 |
| 4 | MS -> SS | … | Transfer of RLC PDUs continues with no SS response to poll requests |
| 5 | MS -> SS | UPLINK RLC PDU | SN = 4095 |
| 6 | MS -> SS | … | Some retransmission may occur depending upon Discard setting |
| 7 | MS -> SS | RB RELEASE | Optional step |

##### Test requirements

The SS will not receive a PU with the SN field set to 0 after receiving the PU with the SN field set to 4095.

#### Control of Receive Window

##### Definition and applicability

All MS that support Acknowledged mode RLC.

##### Conformance requirement

The receiver shall discard PUs with N(S)  VR(MR).

Reference(s)

TS 25.322 / 9.4

##### Test purpose

- To verify that the MS discards PUs with sequence numbers outside of the receive window.

##### Method of test

Initial conditions

The MS is attached to (registered on) the network and in idle mode.

Related ICS/IXIT Statement(s)

TBD

Foreseen Final State of the MS

The same as the initial conditions.

Test procedure

- The SS sets up an downlink connection comprising a Radio Bearer with the following parameters:

RLC mode	Acknowledged

In-sequence delivery	TRUE

PU size	1 PU per PDU

Reception RLC discard timer	Disabled

RLC reception window size	4096

Downlink RLC status Info	TBD

The SS transmits the first PU, with the Polling bit set to 1.

The SS continues to transmit empty PUs with the Polling bit set to 1 until a STATUS PDU is received from the MS.

The SS checks that the STATUS PDU acknowledges successful reception of PU number 0, and then transmits another PU with the Polling bit set to 0.

The SS transmits PUs with sequence numbers up to 4095, with periodic polling.

The SS transmits a PU with sequence number 1 and polls the MS until a STATUS PDU is received.

The SS terminates the connection.

Expected sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | SS -> MS | RB ESTABLISHMENT | See generic procedures |
| 2 | SS -> MS | DOWNLINK RLC PDU | SN = 0, P = 1 |
| 3 | MS -> SS | STATUS PDU | Ack PU #0 |
| 4 | SS -> MS | … | Transfer of RLC PDUs normally |
| 5 | SS -> MS | DOWNLINK RLC PDU | SN = 4095 |
| 6 | SS -> MS | DOWNLINK RLC PDU | SN = 1, P = 1 |
| 7 | MS -> SS | STATUS PDU | Nack PU #0 |
| 8 | MS -> SS | RB RELEASE | Optional step |

##### Test requirements

Following the second transmission the PU with the SN field set to 1, The SS will receive a STATUS PDU indicating that the PU with its SN field set to 0 was not received.

#### Flow Control

##### Credit and peer-to-peer flow control

###### Definition and applicability

All MS that support flow control modes of AM RLC.

###### Conformance requirement

No mechanism for the operation of credit has been defined yet.

Reference

25.322 Section 9.7.4

###### Test purpose

To ensure that the MS transmitter RLC entity correctly applies credit based flow control.

##### Local flow control

###### Definition and applicability

All MS that flow control modes of AM RLC.

###### Conformance requirement

RLC events, such as reception of PDUs and external and internal signals, are normally processed in the order in which they occurred. However, events pertaining to the exchange of RLC link status information have priority over data transfer.

Reference

25.322 Section 9.7.5

###### Test purpose

To ensure that RLC link status information is given priority over data.

#### Operation of Polling using Poll_PU variable

##### Definition and applicability

All MS that support Poll_PU based polling mode of AM RLC.

##### Conformance requirement

VT(PU) should be incremented for both new and retransmitted PUs. When it reaches Poll_PU a new poll is transmitted and the state variable is set to zero.

Reference

25.322 Section 9. 4 and 9.6

##### Test purpose

To verify that a poll is performed when VT(PU) reaches Poll_PU.

To verify VT(PU) is incremented for both new and retransmitted PUs.

##### Method of test

Initial conditions

The MS is attached to (registered on) the network and in idle mode.

Related ICS/IXIT Statement(s)

TBD

Foreseen Final State of the MS

The same as the initial conditions.

Test procedure

- The MS sets up an uplink connection comprising a Radio Bearer with the following parameters:

RLC mode	Acknowledged

PU size	1 PU per PDU

RLC transmission window size	4096

Transmission RLC discard	Disabled

Polling info	Poll_PU set to [32]

The MS transmits continuous PUs, polling and retransmitting normally.

The SS counts received PUs from receipt of the first PU with the P bit set to 1.

The SS notes the count on receipt of the next PU with the P bit set to 1. This count will be recorded as C1.

The SS responds with a STATUS PDU with the PA bit set to 1, and indicating that 8 PUs were not received.

The SS starts a new count of PUs immediately, and notes the count on receipt of the next PU with the P bit set to 1. This count will be recorded as C2.

The SS terminates the connection.

Expected sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | MS -> SS | RB ESTABLISHMENT | See generic procedures |
| 5 | SS | Start counter |  |
| 2 | MS -> SS | UPLINK RLC PDUs | Normal sequence [31] PUs |
| 3 | MS -> SS | … |  |
| 4 | MS -> SS | UPLINK RLC PDU | P = 1 |
| 8 | SS | Stop counter | = C1 |
| 13 | MS -> SS | STATUS PDU | PA = 1, NACK [8] PUs |
| 9 | SS | Start counter |  |
| 10 | MS -> SS | … | [31] further PUs |
| 11 | MS -> SS | UPLINK RLC PDU | P = 1 |
| 12 | SS | Stop counter | = C2 |
| 17 | SS -> MS | RB RELEASE | Optional step |

##### Test requirements

Counts C1 and C2 should be [32].

#### Operation of Polling using Poll_SDU variable

##### Definition and applicability

All MS that support Poll_SDU based polling mode of AM RLC.

##### Conformance requirement

When VT(SDU) reaches Poll_SDU a new poll is transmitted and the state variable is set to zero. The poll bit should be set in the PU that contains the last segment of the SDU.

Reference

25.322 Section 9. 4 and 9.6

##### Test purpose

- To verify that a poll is performed when VT(PU) reaches Poll_PU.

To verify VT(PU) is incremented for both new and retransmitted PUs.

##### Method of test

Initial conditions

The MS is attached to (registered on) the network and in idle mode.

Related ICS/IXIT Statement(s)

TBD

Foreseen Final State of the MS

The same as the initial conditions.

Test procedure

- The MS sets up an uplink connection comprising a Radio Bearer with the following parameters:

RLC mode	Acknowledged

PU size	1 PU per PDU,RLC SDU = 1.5 * RLC PU

RLC transmission window size	4096

Transmission RLC discard	Disabled

Polling info	Poll_SDU set to [7]

The MS transmits continuous PUs, polling and retransmitting normally.

The SS counts received PUs from, and including the receipt of the first PU.

The SS notes the count on receipt of the first PU with the P bit set to 1. This count will be recorded as C1.

The SS responds with a STATUS PDU with the PA bit set to 1, and indicating that 2 PUs were not received.

The SS starts a new count of PUs immediately, and notes the count on receipt of the next PU with the P bit set to 1. This count will be recorded as C2.

The SS terminates the connection.

Expected sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | MS -> SS | RB ESTABLISHMENT | See generic procedures |
| 5 | SS | Start counter |  |
| 2 | MS -> SS | UPLINK RLC PDUs | Normal sequence [10] PUs |
| 3 | MS -> SS | … |  |
| 4 | MS -> SS | UPLINK RLC PDU | P = 1 |
| 8 | SS | Stop counter | = C1 |
| 13 | MS -> SS | STATUS PDU | PA = 1, NACK [2] PUs |
| 9 | SS | Start counter |  |
| 10 | MS -> SS | … | [22] further PUs |
| 11 | MS -> SS | UPLINK RLC PDU | P = 1 |
| 12 | SS | Stop counter | = C2 |
| 17 | SS -> MS | RB RELEASE | Optional step |

##### Test requirements

Count C1 should be [11] and C2 should be [23].

#### Operation of timer Timer_Poll and Timer_Poll_Periodic

##### Definition and applicability

All MS that support Timer based polling mode of AM RLC.

##### Conformance requirement

The Timer_Poll timer is stopped when receiving a STATUS PDU with the PA bit set.

If the Timer_Poll timer expires and no STATUS PDU with the PA bit set has been received the receiver is polled once more (either by the transmission of a PDU which was not yet sent, or by a retransmission) and the timer is restarted.

[If a new poll is sent when the Timer_Poll timer is running it is restarted.]

Each time the Timer_Poll_Periodic timer expires a poll is transmitted and the timer is restarted. The value of the timer is signalled by RRC.

Reference

25.322 Section 9. 5

##### Test purpose

- To verify that the MS polls the SS when the Timer_Poll_Periodic timer expires.

To verify that the Timer_Poll and Timer_Poll_Periodic timers are restarted after a poll is performed.

To verify that the Timer_Poll timer is stopped after receiving a STATUS PDU with the PA bit set.

##### Method of test

Initial conditions

The MS is attached to (registered on) the network and in idle mode.

Related ICS/IXIT Statement(s)

TBD

Foreseen Final State of the MS

The same as the initial conditions.

Test procedure

- The MS sets up an uplink connection comprising a Radio Bearer with the following parameters:

RLC mode	Acknowledged

PU size	1 PU per PDU

RLC transmission window size	4096

Transmission RLC discard	Disabled

Polling info	Timer mode, timer set to [8 block periods], Poll every [32 block periods]

The MS transmits continuous PUs, polling normally.

The SS starts a timer on receipt of the first PU with the P bit set to 1, but does not respond.

The SS stops the timer on receipt of the next PU with the P bit set to 1. This time will be recorded as T1.

The SS does not respond, but starts another timer immediately, and stops it on receipt of the next PU with the P bit set to 1. This time will be recorded as T2.

The SS starts another timer, and transmits a STATUS PDU with the PA bit set to 1.

The SS stops the timer on receipt of the next PU with the P bit set to 1. This time will be recorded as T3.

The SS terminates the connection.

Expected sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | MS -> SS | RB ESTABLISHMENT | See generic procedures |
| 2 | MS -> SS | UPLINK RLC PDUs | Normal sequence [31] PUs |
| 3 | MS -> SS | … |  |
| 4 | MS -> SS | UPLINK RLC PDU | P = 1 |
| 5 | SS | Start timer |  |
| 6 | MS -> SS | … | [7] further PUs |
| 7 | MS -> SS | UPLINK RLC PDU | P = 1 |
| 8 | SS | Stop timer | = T1 |
| 9 | SS | Start timer |  |
| 10 | MS -> SS | … | [7] further PUs |
| 11 | MS -> SS | UPLINK RLC PDU | P = 1 |
| 12 | SS | Stop timer | = T2 |
| 13 | MS -> SS | STATUS PDU | PA = 1 |
| 14 | SS | Start timer |  |
| 15 | MS -> SS | … | [31] further PUs |
| 16 | MS -> SS | UPLINK RLC PDU | P = 1 |
| 17 | SS -> MS | RB RELEASE | Optional step |

##### Test requirements

Times T1 and T2 should be [8] block periods.

Time T3 should be [32] block periods.

#### Operation of timer Timer_Poll_Prohibit

##### Definition and applicability

All MS that support Timer based polling mode of AM RLC.

##### Conformance requirement

This timer is only used when the poll prohibit function is used. It is used to prohibit transmission of polls within a certain period. If polling is taken place during this timer is active, it will be once stopped and set again. This timer will not be stopped by a STATUS PDU. When this timer expires no action is performed. The value of the timer is signalled by RRC.

Reference

25.322 Section 9. 5

##### Test purpose

[Note: Does not seem testable]

#### Operation of timers Timer_Status and Timer_Status_Periodic

##### Definition and applicability

All MS that support Timer based polling mode of AM RLC.

##### Conformance requirement

Timer_Status_Prohibit is only used when the STATUS PDU prohibit function is used. It prohibits the receiving side from sending STATUS PDUs. The timer is started when a STATUS PDU is transmitted and no new STATUS PDU can be transmitted before the timer has expired. The value of the timer is signalled by RRC.

Timer_Status_Periodic is only used when timer based STATUS PDU sending is used. The timer is started when the RLC entity is created. Each time the timer expires a STATUS PDU is transmitted and the timer is restarted. The value of the timer is signalled by RRC.

Reference

25.322 Section 9.5

##### Test purpose

[Note: This requirement is unstable at present]

#### Timer based discard, with explicit signalling

##### Definition and applicability

All MS that support Discard mode of AM RLC.

##### Conformance requirement

For every SDU received from a higher layer, timer monitoring of the transmission time of the SDU is started. If the transmission time exceeds a predefined value for a SDU in acknowledged mode RLC, this SDU is discarded in the transmitter and a Move Receiving Window (MRW) command is sent to the receiver so that AMD PDUs carrying that SDU are discarded in the receiver and the receiver window is updated accordingly. Note that when the concatenation function is active, PDUs carrying segments of other SDUs that have not timed out shall not be discarded.

Reference

25.322 Section 9.7.2.1

##### Test purpose

[Note: This requirement is unstable at present]

To ensure that:

When the timer expires the timed-out SDU is discarded by the MS, and a MRW command sent back.

PDUs carrying segments of other SDUs that have not timed out are not discarded

#### Timer based discard, without explicit signalling, Acknowledged mode

##### Definition and applicability

All MS that support Discard mode of AM RLC.

##### Conformance requirement

For acknowledged mode RLC, peer-to-peer signalling can be avoided as long as SDU discard is always performed in the transmitter before it is performed in the receiver. As long as the corresponding SDU is eventually discarded in the receiver too, possible retransmission requests of PDU of discarded SDUs can be ignored by the transmitter. The bigger the time difference is between the triggering of the discard condition at the transmitter and the receiver, the bigger the unnecessary buffering need is at the receiver and the more bandwidth is lost on the reverse link due to unnecessary retransmission requests. On the other hand, forward link bandwidth is saved, as no explicit SDU discard signalling is needed.

Reference

25.322 Section 9.7.2.1

##### Test purpose

[Note: This requirement is unstable at present]

To ensure that:

When the timer expires the timed-out SDU is discarded by the MS.

PDUs carrying segments of other SDUs that have not timed out are not discarded

#### PU (PDU?SDU?) discard after MaxDAT number of retransmissions

##### Definition and applicability

All MS that support Discard mode of AM RLC.

##### Conformance requirement

When the value of VT(DAT) comes to MaxDAT, error recovery procedure will be performed.

In case of error situations the following actions are foreseen:

- RLC entity should use RESET procedure in case of an unrecoverable error

- RLC entity should discard invalid PDU

- RLC entity should notify upper layer of unrecoverable error occurrence in case of failed retransmission

Reference

25.322 Section 9.6

##### Test purpose

To verify that appropriate error recovery is performed after an SDU has been retransmitted MaxDAT times.

[Note: No definition yet of which error procedure should be used in which circumstance. This test is only for DISCARD]

##### Method of test

Initial conditions

The MS is attached to (registered on) the network and in idle mode.

Related ICS/IXIT Statement(s)

TBD

Foreseen Final State of the MS

The same as the initial conditions.

Test procedure

- The MS sets up an uplink connection comprising a Radio Bearer with the following parameters:

RLC mode	Acknowledged

PU size	1 PU per PDU

RLC transmission window size	4096

Transmission RLC discard	Disabled

Polling info	Poll_SDU set to [4], MaxDAT set to [4]

The MS transmits continuous PUs, polling and retransmitting normally.

The SS counts each time it receives a PU with the SN field set to 1.

On receipt of the each PU with the P bit set to 1, the SS responds with a STATUS PDU with the PA bit set to 1, and indicating that the PU with sequence number 1 was not received.

The SS continues steps c) and d) until it receives a MRW command, where it notes the counter value.

The SS terminates the connection.

Expected sequence

| Step | Direction | Message | Comments |
| --- | --- | --- | --- |
| 1 | MS -> SS | RB ESTABLISHMENT | See generic procedures |
| 5 | SS | Start counter |  |
| 2 | MS -> SS | UPLINK RLC PDUs | Normal sequence [3] PUs |
| 3 | MS -> SS | … |  |
| 4 | MS -> SS | UPLINK RLC PDU | P = 1 |
| 13 | MS -> SS | STATUS PDU | PA = 1, NACK PU #[1] |
| 10 | MS -> SS | … | [11] further PUs |
| 11 | MS -> SS | UPLINK STATUS PDU | MRW Command |
| 12 | SS | Stop counter |  |
| 17 | SS -> MS | RB RELEASE | Optional step |

##### Test requirements

Count should be [4].

#### Use of RESET procedure in case of an unrecoverable error

##### Definition and applicability

All MS that support AM RLC.

##### Conformance requirement

Timer_RST is set when the RESET PDU is transmitted. And it will be stopped upon reception of RESET ACK PDU. If it expires, RESET PDU will be retransmitted.

The Max_RST parameter is an upper limit of counter VT(RST). When the value of VT(RST) comes to MaxRST, the higher layer (RRC) is notified. [Testable?]

Reference

25.322 Section 9.7.2.1

##### Test purpose

[Note: This requirement is unstable at present]

#### RLC Toolbox

[FFS]

Note: The following areas are also FFS:

QoS

Quick Repeat (UM)

Establishment and release (all modes)