| 3GPP TSG T WG1, #9 Location: Redondo Beach, USA Date: 16th - 17th November, 2000 | Tdoc TSG T1-000321 |
| --- | --- |

###### Agenda Item:

Source:		Anritsu Ltd, UK

Title:			Report from the informal ad-hoc on EMMI

Document for:	Information

Contact:		dan.fox@eu.anritsu.com

Report

Members of T1/SIG met for an ad-hoc meeting on the 16th November to review decisions made regarding the implementation and use of an electronic man-machine interface for the purposes of automated testing.

Background

Two proposals had previously been presented to T1/SIG (from Ericsson and subsequently Anritsu), and although much discussion had taken place, no resolution had been reached.

At the T1/SIG SWG in Nantaali, Finalnd, Rohde & Schwarz presented objections to the Anritsu proposal and support for following the Ericsson approach. This was agreed at the meeting.

However, it subsequently became obvious that there was widespread misunderstanding of the Ericsson proposal, and of the agreement reached, so this ad-hoc meeting was proposed to resolve the issue.

Result

The meeting was very informal, but the following resolution was reached:

The logical part of the interface; the definition of TTCN abstract service primitives (ASPs), the points of control and observation (PCO) and the use of AT commands were recognised to be critical for continuation of the production of TTCN test cases. These parts are already well defined and agreed. They are recognised as agreed, and will not be changed.

The physical part of the interface; the use of an RS232C port to allow adaptation of the AT commands will be discussed further on the T1/SIG reflector during December, together with other aspects of the EMMI interface, and a decision on this point deferred.

As only the latter part has any impact on the liaison statement to RAN2, it was decided to defer discussion on the LS until the next T1 meeting. This deferral was agreed on the understanding that any alternative solution would not place any mandatory requirements on UE implementations.