3GPP TSG-T WG1 EMC #5 meeting                Tdoc TSG T1E-990XX

# Kobe  13 September 1999

Agenda item :

Source : Panasonic (Matsushita Communication Industrial Co., Ltd.)

Title :  Comment for 3GPP EMC #5 Meeting

1. Proceeding of this meeting

I agree with making the 3GPP EMC standard which based on the Draft standard proposed by Nokia.

We should check the Draft EMC standard and complete in near future.

2. Confirmation of 3GPP EMC Schedule

We decided two stages of EMC standard schedule for conformance testing of terminals.

So, when we should complete the 3GPP EMC standard of Stage2 ?

3. About Table 1 of regional EMC standard

We should separate the item of “spurious emission” from EMC standard.

And we should put this item into the Specification of RF testing.

4. About 3GPP EMC (draft) standard(3G TS 34.124 version 0.0.1)

1) Emission

I think we should add the item “Radiated emission from Enclosure”.

(Why this draft EMC standard does not have this item ?)

In the future, terminals may have various function, for example “moving picture transmission”,

“connecting the internet and show many visible information on the terminal”, etc.

At that time terminal have same function as ordinary ITE, and may increase the clock speed of

CPU and increase the radiated emission from the digital circuit(ex. DSP).

So, we should specify the limit and test method of “Radiated emission from Enclosure”.

2) Immunity

I think “Performance criteria for Transient phenomena(6.2)”is too severe, because the judgement

criteria is exactly same as “Performance criteria for Continuous Phenomena”. It should be kept the

same level of judgement criteria compared with another EMC standard (ex. ETS300 342-1).

So I will propose to change this criteria as follows,

The EUT shall operate as intended with no loss of user control functions, and the communication

link shall be maintained after the test.

(We should delete present performance criteria of this item.)