This document provides a first attempt at a table listing the requirements for a MExE ME as mentioned in 02.57, MExE Service Description, Stage 1.

The aim of this table is to provide a requirements framework in order to allow subsequent specification work such as API definition to be performed more efficiently.

The following provides information relating to the table headings:

| Key to Requirements Table Headings |
| --- |
| Heading | Explanation |
| i.d. | A unique identifier for each requirement. An identifier can be assigned only once. This heading also contains the [i.d.] of the next requirement to be entered - embedded as a table function (F9 to update). |
| Category |

A series of broad categories into which requirements are placed.

"J" means this requirement relates directly to the specification of a Java API.

| "I" means this requirement relates to implementation, and puts the specification of a Java API into context. |
| --- |
| Requirement | The actual requirement, which should be as unambiguous (and indivisible) as possible |
| Reference | A reference into a document within which the requirement is mentioned, if applicable |
| Priority | Requirements may be mandatory or optional |
| Classmark | An indication as to which classmark the requirement is applicable or in-applicable (in which case the classmark figure is shown in brackets) |
| Release | An indication of whether the requirement is applicable to Release 98, 99 etc. |
| Comment | A general purpose comment field |
| Applicable API | Applies to Java enabled devices. A list of the APIs which satisfy the requirement |
| Chosen API | Applies to Java enabled devices. The API chosen from the "Applicable API" list. |

i.d.

| [107] | Category | Requirement | Reference | Priority | Class-mark | Release | Comment | Applicable APIs | Chosen API |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| High Level |
| 1 | J | The MExE ME shall provide a means for applications, applets and content to access the user interface |
| Mandatory |
|  | 3 | J | The MExE ME shall provide the means to allow the transfer of applications, applets or content either automatically or on demand according to MExE security requirements |

02.57

v7.0.0

| 6.1.0 | Mandatory |
| --- | --- |
|  | 4 | I | The MExE ME shall provide the means to allow the upgrade of existing applications across the GSM/UMTS network subject to MExE security requirements and user authorisation |

02.57

v7.0.0

| 6.1.0 | Mandatory |
| --- | --- |
|  | 5 | I | The MExE ME shall allow the user to personalise services |

02.57

v7.0.0

| 6.1.0 | Mandatory |
| --- | --- |
|  | FFS – relates to user profile (i.e. the way the information is displayed on the MExE ME , not the type/nature of information). DELETE FROM CLARIFICATION LIST BUT DO NOT CR |
| 6 | J | The MExE terminal shall allow the user to utilise both internet and intranet applications, applets and content according to MExE security requirements |

02.57

v7.0.0

| 6.1.0 | Mandatory |
| --- | --- |
|  | 54 | J | The MExE ME shall possess an architecture that is capable of supporting applications, applets and content in a standard execution environment independently of the MExE ME manufacturer |

02.57

v7.0.0

| 9.1.0 | Mandatory |
| --- | --- |

CR

| Classmarks |
| --- |
|  | 11 | I | MExE applications and applets conforming to a particular MExE classmark shall be supportable by all MExE MS’s of that classmark regardless of MExE MS manufacturer |

02.57

v7.0.0

| 5.3 | Mandatory |
| --- | --- |

User Interface

| Configuration Management |
| --- |
| 14 |
| 2 | I | The MExE ME shall allow the user to personalise the user interface within bounds defined by the manufacturer |

02.57

v7.0.0

| 6.1.0 | Mandatory |
| --- | --- |

The extent of "personalisation" will be limited by the terminal manufacturer. E.g. screen colours, ring patterns, screen saver

| This needs further clarification – Nash |
| --- |
| 15 | I | The user shall be able to manage the user interface configuration of the MExE MS within bounds defined by the manufacturer |

02.57

v7.0.0

| 6.2.1 | Mandatory |
| --- | --- |
|  | The extent of "personalisation" will be limited by the terminal manufacturer. |
| 16 | I | The MExE ME shall allow the user to identify the current user interface configuration within bounds defined by the manufacturer |

02.57

v7.0.0

| 6.2.1 | Mandatory |
| --- | --- |
|  | 17 | I | The MExE ME shall allow the user to add, modify or delete a particular user configuration within bounds defined by the manufacturer |

02.57

v7.0.0

| 6.2.1 | Mandatory |
| --- | --- |
|  | 18 | I | It shall be possible to obtain the user interface configuration information, subject to MExE security requirements, which is resident on the MExE ME, the SIM or the network |

02.57

v7.0.0

| 6.2.1 | Mandatory |
| --- | --- |

FFS – similar to “.dt”, “.xdefaults” in Unix. [Further contribution expected from Nash].

| Change Request |
| --- |
| 20 |
| ThHe user interface configuration management information may be stored on the MExE ME, the SIM or the network, subject to MExE security requirements. |
| Mandatory |
|  | 22 | J | Any MExE ME shall be able to access and interpret user interface configuration data, according to MExE security requirements |
| Mandatory |

Assume “user profile” means personal details i.e. name, e-mail etc.

Clarification required on defn of terms

“The user profile data shall be associated with a given user” is part of defn (req 23)

“User profile data” is a superset of “user interface configuration” – partitioning/access is FFS.

NB: “interpret” may need to be clarified!

| CR – add to end of para3.6.2.1, 02.57 |
| --- |
| Service Management |
| 25 | I | The MExE ME shall allow the user to request the range of MExE services available from the PLMN MExE service provider |

02.57

v7.0.0

| 6.2.2 | Mandatory |
| --- | --- |

Misgivings about how registration is carried out, notification messages etc.

What is the notification mechanism?

| This is perceived as a common address (e.g. URL. Same address could be used when roaming – use (e.g.) DNS to resolve actual server address). This address is used to provide the first point of access to a MExE network. The user is provided with a list of MexE services available from the PLMN service provider. MExE is allowed to stipulate only access to GSM/GPRS/UMTS MExE SPs – PLMN independent SPs lie outside of the scope of MExE standardisation. When roaming, the user could collect a number of addresses, including HPLMN and VPLMN. |
| --- |
| 26 | I | The MExE ME shall allow the user to determine which MExE applications, applets and content are currently resident on the MExE ME |

02.57

v7.0.0

| 6.2.2 | Mandatory |
| --- | --- |
|  | Resident in terminal only or also in network? |
| 103 |
| The MExE ME shall be able to determine whether or not the GSM/GPRS/UMTS connection required by an application has been broken |
| Mandatory |
|  | 102 |
| The MExE ME shall allow the user to control , via the user profile, whether or not an application is automatically executed once it has been downloaded, according to MExE security requirements |

03.57

| 4.x | Optional |
| --- | --- |
|  | Execution may in some instance include configuration |
| Bearer Services |
|  | 30 | J | The MEexE ME shall provide access to a range of one or more GSM/GPRS/UMTS bearer services, within the capabilities of the ME and network |

02.57

v7.0.0

| 7.0.0 | Mandatory |
| --- | --- |
|  | Transport protocols shall be defined in other specs (stage2,3?). Use only standard protocols (no proprietary) |
| Protocols |
| 34 | J | MExE protocols shall be independent of the type of underlying bearer |

02.57

v7.0.0

| 8.2.0 | Mandatory |
| --- | --- |

What are upper layer MExE protocols? Definition required – suggest all layers above the bearer.

| Definition accepted – CR to definition section of 02.57 |
| --- |
| 36 | J | Applications and applets shall be able to request specific bearer services and to be notified as to their availability |

02.57

v7.0.0

| 8.2.0 | Optional |
| --- | --- |
|  | 38 | J | MExE protocols shall be able to add new bearers |

02.57

v7.0.0

| 8.3.0 | Mandatory |
| --- | --- |
|  | 40 | I | It shall be possible for applications and services to install new protocols |

02.57

v7.0.0

| 8.4.0 | Optional |
| --- | --- |
|  | CR |
| 41 | I | MExE protocols shall be independent of the network nodes being communicated with |

02.57

v7.0.0

| 8.5.0 | Mandatory |
| --- | --- |
|  | 43 | I | MExE protocols shall support a generic technology independent capability negotiation, notification and enquiry mechanism between the MExE ME and the MExE service environment |

02.57

v7.0.0

| 8.6.0 | Mandatory |
| --- | --- |
|  | 100 | I | The MExE ME shall allow a MExE service provider to determine the MExE ME capabilities, according to MExE security requirements. |

02.57

v7.0.0

| 6.1.0 | Mandatory |
| --- | --- |
|  | NB: MExE Service Provider can be anybody – hence apply MExE security policy |
| 101 | I | The MExE ME shall perform capability and content negotiation according to Section 4.4. of 03.57 | 03.57 Section 4.4 | Mandatory |
|  | Table reference IN NEW VERSION |
| 48 | I | The capability negotiation mechanism shall be extensible. |

02.57

v7.0.0

| 8.6.0 | Mandatory |
| --- | --- |
|  | CR |
| 50 | I | MExE protocols shall support the capability to transfer new applications, applets and content to and from the MExE ME as required by the user according to MexE security requirements |

02.57

v7.0.0

| 8.8.0 | Mandatory |
| --- | --- |

| CR required |
| --- |
| 51 | I | The MExE protocols shall support both user initiated and MexE server initiated transfer of applications, applets and content as required by the user, according to MExE security requirements |

02.57

v7.0.0

| 8.8.0 | Mandatory |
| --- | --- |
|  | CR required to section 8.8 of 02.57v7.0.0 |
| MS Application Execution Environment |
| 55 | J | Ability to cleanly and safely install applications and associated data (e.g. icons) shall be provided. |
| Optional |
|  | 56 | J | Ability to cleanly and safely de-install applications and associated data (e.g. icons) shall be provided. |
| Optional |
|  | 57 | I | The MExE classmark 2 terminal shall be able to implement HTML |
| Mandatory |

WML for classmark 1, HTML for classmark 2

| This an an API req, relating to stage 2. |
| --- |
| 58 | I | The MExE classmark 2 terminal shall be able to implement WML and WMLScript |
| Mandatory |
|  | This an an API req, relating to stage 2. |
| 105 | I | The MExE Classmark2 device shall contain a pre-installed WAP browser |
| Mandatory |
|  | I.e. browser capable of rendering WML and WMLScript |
| 106 | I | The MExE Classmark2 device shall allow the pre-installed WAP browser to be updated |
| Mandatory |
|  | 59 | I | MExE shall define a set of standardised content coding schemes i.e. vCard, vCalendar |
| Mandatory |

Is vCard, vCalendar support required?

| This an an API req, relating to stage 2. |
| --- |
| 60 | I | The MExE ME shall be able to support HTML and/or WML |
| Mandatory |
|  | 61 | J |

MExE ME shall support the 7bit GSM default character set

Mandatory

As defined in 03.38 v6.0.1

Note: User defined 8bit scheme is not mentioned here. Should it be?

| CR to section 9.2 (last para) of 02.57v7.0.0 – replace “defined” with “identified” |
| --- |
| 104 | I | The MExE ME shall be capable of supporting the UCS2 character coding scheme |
| Optional |
|  | Unicode 16bit character coding |
| 63 | I | The MExE ME shall support a core API, known as the core MExE API |

02.57

v7.0.0

| 9.3.0 | Mandatory |
| --- | --- |
|  | The core MExE API defines the minimal API set that a MExE ME needs to support |
| 64 | I | The core MExE API shall consist of both generic and GSM/UMTS specific aspects |

02.57

v7.0.0

| 9.3.0 | Mandatory |
| --- | --- |
|  | 65 | I | The MExE ME shall support standardised MExE API extensions in addition to the core MExE API |

02.57

v7.0.0

| 9.3.0 | Optional |
| --- | --- |
|  | 66 | J | The standardised MExE API extensions shall include access to location information, according to MExE security |

02.57

v7.0.0

| 9.3.0 | Mandatory |
| --- | --- |

What is the meaning of "mobility information"?

CR

| Location |
| --- |
| 67 | J | The MExE APIs shall provice support for applications and applets to access the GSM/UMTS functionality present in the GSM/UMTS terminal according to MExE security . |
| Mandatory |
|  | Functionality includes telephony, e-mail, SMS, fax. |
| 68 | J | All Java APIs specified by MExE for use on a MExE ME shall be approved by Sun Microsystems. |
| Mandatory |
|  | 69 | J | The MExE ME shall provide local file system support, according to MExE security |

02.57

v7.0.0

| 6.1.0 | Optional |
| --- | --- |
|  | 70 | I | The MExE ME shall allow the user to identify the version number of applications, applets and content contained within it |

02.57

v7.0.0

| 6.1.0 | Optional |
| --- | --- |
|  | 71 | J | A MExE ME shall notify applications of any power state changes. |

02.57

v7.0.0

| 6.1.0 | Optional |
| --- | --- |
|  | 72 | J | A MExE ME shall support standardised access of a smartcard if a smartcard reader is present on the MExE ME |

02.57

v7.0.0

| 6.1.0 | Optional |
| --- | --- |
|  | Support of smartcard reader is not a mandatory requirement. |
| Security |
|  | 76 | I | Transferred MExE applications, applets and content shall be secure and verified |

02.57

v7.0.0

| 11.0.0 | Mandatory |
| --- | --- |
|  | “secure” – received in same state as it was sent i.e. has not been tampered with |
| 77 | I | The MExE ME shall provide support for four security levels |

02.57

v7.0.0

| 11.0.0 | Mandatory |
| --- | --- |

See Table XX in Section 9.1 of 03.57 for an elaboration of security levels.

| Multiple security levels |
| --- |
| 79 | I | The security level of applications, applets and content shall be verified by the MExE ME |

02.57

v7.0.0

| 11.0.0 | Mandatory |
| --- | --- |
|  | 81 | I | The MExE subscriber shall be able to control whether applications, applets and content of specific security levels may be transferred to the MExE ME |

02.57

v7.0.0

| 11.0.0 | Mandatory |
| --- | --- |
|  | 82 | J | An application/applet shall specifiy whether or not it can share its own files with other applications/applets |

02.57

v7.0.0

| 11.0.0 | Mandatory |
| --- | --- |
|  | More input required here |
| 83 | I | Within the constraints of the defined security levels, the user shall have ultimate control over the use of bearer services |

02.57

v7.0.0

| 11.0.0 | Mandatory |
| --- | --- |

CR

| Incorporate USSD and SS signalling (comment by K Holley at MExE security meeting, SMG4 plen 11 – 14th Dec 1998) |
| --- |
| 84 | I | A means to authenticate the MExE subscriber and MExE server shall be provided |

02.57

v7.0.0

| 11.0.0 | Mandatory |
| --- | --- |

CR

| This may be performed by the MExE ME, an intermediate entity or the GSM/UMTS network |
| --- |
| 85 | I | MExE shall continue to support the inherent security and integrity of the GSM/GPRS/UMTS network |

02.57

v7.0.0

| 11.0.0 | Mandatory |
| --- | --- |
|  | 86 | I | The integrity of the SIM and existing GSM/UMTS security mechanisms shall not be compromised by the introduction of MExE services |

02.57

v7.0.0

| 11.0.0 | Mandatory |
| --- | --- |
|  | 87 | I | All aspects relating to GSM security shall be performed by the SIM |

02.57

v7.0.0

| 6.1.0 | Mandatory |
| --- | --- |
|  | Interworking with other Network Features |
| 90 | I | All services available in the network shall continue to be offered in addition to MExE services |

02.57

v7.0.0

| 12.0.0 | Mandatory |
| --- | --- |
| Network Interworking |
| 92 | I | All services offered in co-operation with other networks shall continue to be offered in parallel with MExE services |

02.57

v7.0.0

| 13.0.0 | Mandatory |
| --- | --- |
|  | Communications |
| 93 | J | MExE MEs shall support peer to peer communication between MExE devices |

02.57

v7.0.0

| 6.1.0 | Optional |
| --- | --- |
|  | Includes e.g. IrDA, Bluetooth, USB (which are outside the scope of MExE specifications), user-to-user signalling, USSD (which are within the scope of MExE specifications) etc. |
|  | 95 | J | A MExE application shall be able to access any or all external interfaces present on the MExE ME, subject to the limitations of the MExE ME |
| Optional |
|  | Serial, parallel, infra-red etc. |
| 96 | J | The means for MExE service provider specific applications and applets on the MExE ME to communicate with other GSM network nodes shall be provided. |

02.57

v7.0.0

| 6.1.0 | Optional |
| --- | --- |
|  | USSD main bearer |

# Comments

Automatic installation of an application is scary. It is not only a security issue, but also almost like invasion of private propert.

The user interface can't be personalised, because the terminal manufacturer is the only one who knows about certain hardware parts of the UI, like buttons.

The user interface can't be personalised, because the terminal manufacturer is the only one who knows about certain hardware parts of the UI, like buttons.

I would interpret this to mean "configuration profile", but not applying really to the UI.

I don't understand…