ETSI SMG4 / 3GPP TSG-T MExE	Tdoc SMG4 4M99-056

Helsinki, Finland

17th-19th February, 1999

| CHANGE REQUEST No : |  | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
| --- | --- | --- |
| Technical Specification GSM / UMTS: | 03.57 | Version | 1.4.0 |  |
| Submitted to SMG |  | For approval |  | without presentation ("non-strategic") |  |  |
| list plenary meeting or STC here ( | for information |  | with presentation ("strategic") |  |  |
| PT SMG CR cover form. Filename: crf26_3.doc |

| Proposed change affects: | SIM |  | ME | X | Network |  |
| --- | --- | --- | --- | --- | --- | --- |

(at least one should be marked with an X)

| Work item: | MExE |
| --- | --- |

| Source: | Motorola/Nokia | Date: | 12/01/99 |
| --- | --- | --- | --- |

| Subject: | Service Management |
| --- | --- |

| Category: | F Correction |  | Release: | Phase 2 |  |
| --- | --- | --- | --- | --- | --- |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (one category | B Addition of feature |  |  | Release 97 |  |
| and one release | C Functional modification of feature | X |  | Release 98 | X |
| only shall be | D Editorial modification |  |  | Release 99 |  |
| marked with an X) |  |  |  | UMTS |  |

| Reason for change: | Update of the relevant clauses for service management. |
| --- | --- |

| Clauses affected: | 3.1, 4.7 |
| --- | --- |

| Other specs | Other releases of same spec |  | ( List of CRs: |  |
| --- | --- | --- | --- | --- |
| affected: | Other core specifications |  | ( List of CRs: |  |
|  | MS test specifications / TBRs |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |

| Other comments: |  |
| --- | --- |

[10]	Java Mail API version 1.0.2, available from http://www. java.sun.com

[11]	UMTS TR 22.70: “Universal Mobile Telecommunications System (UMTS); Service aspects; Provision of Services in UMTS - The Virtual Home Environment”.

[12]	UMTS TS 22.xx: “Universal Mobile Telecommunications System (UMTS); Provision of Services in UMTS - The Virtual Home Environment: Stage 1”.

[13]	ISO 639 International Standard - codes for the representation of language names

# 3	Definitions and abbreviations

## 3.1	Definitions

For the purposes of this TS the following definitions apply:

phonebook: a phonebook is a dataset of personal or entity attributes. The simplest form is a set of name-number pairs as supported by the current GSM SIM

service: a service (which may consist of an application, applet, and its related content) is a set of functions offered to a user by an organisation, and may be performed on the MExE MS and/or remotely

service name: service name is an identifier associated with a service, and could be a string, a fully qualified Java class name, a unique URI or other identifier.

Further definitions specific to MExE are in GSM given in 02.57 (MExE stage 1)

## 3.2	Abbreviations

For the purposes of this TS the following abbreviations apply:

API	Application Programming Interface

CGI	Common Gateway Interface

DHCP	Dynamic Host Configuration Protocol

GSM	Global System for Mobile Communication

HTTP	HyperText Transfer Protocol

IP	Internet Protocol

JNDI	Java Naming Directory Interface

JTAPI	Java Telephony Application Programming Interface

JAR file	Java Archive File

MSE	MExE Service Environment

RFC	Request For Comments

SAP	Service Access Point

SMS	Short Message Service

TLS	Transport Layer Security

UDP	User Datagram Protocol

URL	Uniform Resource Locator

USSD	Unstructured Supplementary Service Data

WAE	Wireless Application Environment

WAP	Wireless Application Protocol

WSP	Wireless Session Protocol [WSP]

WTA	Wireless Telephony Applications

WTAI	Wireless Telephony Applications Interface

WTLS	Wireless Transport Layer Security

WTP	Wireless Transaction Protocol

WWW	World Wide Web

## 4.7	Management of services

Management of services provides the user with the capability to

- configure services

- control the transfer and execution of services

- terminate or suspend executing services

on his MExE MS.

### 4.7.1	Service configuration

The user controls whether a service transferred to the MExE MS is also automatically configured in the MS.  Configuration of a service may result in changes to user interface using icons, browsers or menus as applicable depending on the capability of the MExE MS to support them.  The service name may be contained in the package in which it was received (i.e. a JAR file or script.), assigned by the user during configuration, or some other means.  If service automatic configuration is enabled, the user is notified of the automatic service configuration once it is completed.

In the event that there is no authorisation for the automatic configuration of a transferred service, the user is notified that it was not configured.

controls which

### Subsequent user modification of a service’s configuration (e.g. by modification of use profile settings) shall take effect at the earliest possible opportunity thereafter.4.7.2	Service management

The MExE MS shall support the ability to determine which services are transferred to, resident, configured or executing on the MS.  The information relating to the services includes (as a minimum) the name and version.

The user controls which services are permitted or denied to be transferred , resident, configured or executing on the MExE MS via the user profile.  The user profile permits characteristics such as security level, identification of specific services etc. to manage services on the MExE MS.

### 4.7.3	Service termination

A service may terminate by itself, or be terminated by the provider of the service or by the user. The user is in charge of the service, except when the service provider may appropriately control the service as part of user support.

- The mechanism for terminating a service is out of scope of standardisation and shall be provided on a service by service basis by the provider of the service.

### 4.7.4	Service deletion

A service may be deleted (i.e. removed) from the MExE MS with the implicit or explicit authorisation of the user.  The deletion may be initiated by the authoriser of the service or by the user. by the authoriser of the service.  Additionally, the user may delete any service which has been transferred to the MS, with the implicit or explicit authorisation of the user.

The mechanism for deleting a service is out of scope of standardisation and shall be provided on a service by service basis by the provider of the service.