ETSI SMG4	Tdoc SMG4 4M99-064

Helsinki

17-19.2.1999

| CHANGE REQUEST No : |
| --- |
| . |
| Technical Specification GSM / UMTS: | 03.57 | Version | 1.4.0 |
|  | Submitted to SMG |
| for approval | x | without presentation ("non-strategic") |
|  | for information |
| with presentation ("strategic") |
| PT SMG CR cover form. Filename: crf26_3.doc |

| Proposed change affects: | SIM |
| --- | --- |
| ME | x | Network |

(at least one should be marked with an X)

Work item:

| Source: | Nokia | Date: | 10.2.1999 |
| --- | --- | --- | --- |

| Subject: | Capability tokens |
| --- | --- |

| Category: | F Correction | x | Release: | Phase 2 |
| --- | --- | --- | --- | --- |
| A Corresponds to a correction in an earlier release |
|  | Release 96 |
|  | (one category | B Addition of feature |
|  | Release 97 |
|  | and one release | C Functional modification of feature |
|  | Release 98 | x |
| only shall be | D Editorial modification |
|  | Release 99 |
|  | marked with an X) |
| UMTS |

Reason for change:

SMS is one possible bearer, so compactness of the tokens and values should be considered. I suggest that instead of using "MExE-" as a prefix, using "M" would be sufficient, and instead of using dashes ("-") in the tokens, using uppercase to indicate the

start of a word. e.g. "MKbdId" rather than "MexE-kbd-id".

| Clauses affected: | 4.4.1 |
| --- | --- |

| Other specs | Other releases of same spec |
| --- | --- |
| ( List of CRs: |
|  | affected: | Other core specifications |
| ( List of CRs: |
| MS test specifications / TBRs |
| ( List of CRs: |
| BSS test specifications |
| ( List of CRs: |
| O&M specifications |
| ( List of CRs: |

| Other comments: | The document does not explicitly say that ISO 639 shall be used for language names. |
| --- | --- |

4.4.1	Capability negotiation characteristics

The generic set of capabilities which may be negotiated between the client and the server consists of the subsequently identified characteristics.:-

| Token | Characteristics | Optionality | Description |
| --- | --- | --- | --- |
| MS to MSE | MSE to MS |
|  | MExE-MCclass | MExE Classmark | M | O |

Classmark of the MExE device, e.g. 1, 2, etc.

Example coding:

| MExE-McClass: 1 |
| --- |
| MExE-MSpec | MExE specification | O | O |

Version of the MExE Stage 2 standard supported by the MS; represents the first two digits of the 03.57 specification version number.

Example coding:

| MExE-MSpec: 7.0 |
| --- |
| MExE-MsSrvcs | MExE services | O | O |

Identification on where information on the PLMN-provided MExE services may be found, e.g. URL

Example coding:

| MExE-MsSrvcs: http:://telco.mexe.com/services |
| --- |
| MExE-MmManuf | Device | Manufacturer | O | O |

Identification of the manufacturer, e.g. Motorola, Nokia, Ericsson, etc

Example coding:

| MExE-MmManuf: Motorola |
| --- |
| MExE-MmModel |
| Model | O | O |

Model type, e.g. 130, 8810, 688, etc.

Example coding:

| MExE-MmModel: 130 |
| --- |
| MExE-MSN |
| Serial Number | O | O |

Manufacturer’s model, e.g. 1.1.0 etc.

Example coding:

| MExE-MSN: 1.1.0 |
| --- |
| MExE-MSV |
| SoftwareVersion | O | O |

Manufacturer’s software version,  IMEISV

Example coding:

| MExE-MSV: nnnnnnnnnnnnnnn |
| --- |
| MExE-MrRes | Display | Size | resolution |

O

O

Pixel size of the display, e.g. 200x150 etc.

Example coding:

| MExE-MrResol: 1.1.0 |
| --- |
| MExE-McChars |
|  | Characters |

O

O

Number of lines and characters per line, e.g. 3x20, 4x15 etc.

Example coding:

| MExE-McChars: 3x20 |
| --- |
| MExE-McClrs |
| Colour/monochrome | Number of colours |

O

O

The number of colours supported, e.g. . 1, 256, 16,000 etc.

Example coding:

| MExE-McClrs: 256 |
| --- |
| MExE-MgGrey |
|  | Greyscale |

O

O

The number of gray scale, e.g. 2 for black and white only

Example coding:

| MExE-MgGrey: nnn |
| --- |
| MExE-MvVoice | Input mode | Voice |

O

O

Indication of whether voice capture is supported, e.g.  yes/no

Example coding:

| MExE-MvVoice: yes |
| --- |
| MExE-MkKbdIid |
| Keyboard type | Keyboard identity |

O

O

Type of keyboard supported, e.g. default, PC-AT-102

Example coding:

| MExE-MkKbdiId: default |
| --- |
| MExE-MkKbdlLg |
|  | Human language |

O

O

ISO 639 encoded lLanguage used on keyboard, i.e. EN-UK etc.

Example coding:

| MExE-MkKbdlLg: EN-UK |
| --- |
| MExE-MkKeys |
|  | Number of keys |

O

O

The number of keys supported by the keyboard, i.e. default, 15, 102, etc.

Example coding:

| MExE-MkKeys:default |
| --- |
| MExE-MpPntr |
| Pointing device | Identity |

O

O

Type of pointing device, i.e. none, touchscreen, mouse, etc.

Example coding:

| MExE-MpPntr: none |
| --- |
| MExE-MhHlLang | Human Language | O | O |

ISO 639 encoded Ppreferred language in which the user wishes to work, i.e EN-UK etc.

Example coding:

| MExE-MhHlLang: EN-UK |
| --- |
| MExE-MfFlLang | Formal Language | O | O |

Prioritised list of renditions for formal languages, e.g. HTML, WML, etc.

Example coding:

| MExE-MfFlLang: WML/HTML |
| --- |
| MExE-MaAdpPrt | Additional Protocols |

O

O

List of additionally supported protocols of the MExE device, e.g. SAT (SIM Application Toolkit)

Example coding:

| MExE-MaAdpPrt: SAT |
| --- |
| MExE-MbBear | Supported Bearers | O | O |

Prioritised list of preferred bearers, e.g. SMS, USSD, GPRS, etc.

Example coding:

| MExE-MbBear: GPRS/SMS |
| --- |
| MExE-McCldDif | Difference to base Classmark |

O

O

Identification of the devices’ components differing from the base Classmark definition

Example coding:

| MExE-McCldDif: Java.rmi |
| --- |
| MExE-MmMemtTy | User authorised available memory | Type of memory | O | O |

Type of memory, e.g. RAM, memory, hard disk, etc.

Example coding:

| MExE-MmMemtTy: RAM |
| --- |
| MExE-MmMem |
| Amount of memory | O | O |

Amount of memory authorised by the user for MExE, e.g.  1, 6, 10, etc.

Example coding:

| MExE-MmMem: 1 |
| --- |
| MExE-MaAudio | Multimedia | Audio codec type | O | O |

Prioritised list of preferred audio codecs (cf. H.323) e.g. G.711, G.723 etc.

Example coding:

| MExE-MaAudio: G.711 |
| --- |
| MExE-MvVideo |
| Video codec type | O | O |

Prioritised list of preferred video codecs (cf. H.323), e.g. H.261, H.263

Example coding:

| MExE-MvVideo: H.261 |
| --- |
| MExE-MtTsSize | Transfer limits | Size | O | O |

Maximum size of transfers in Kb, e.g. 1,2, 4, 8, etc.

Example coding:

| MExE-MtTsSize: 4 |
| --- |
| MExE-MttTTime |
| Time | O | O |

Maximum duration of transfers in minutes, eg. 1,2, 4, 8, etc.

Example coding:

| MExE-tsizeMTTime: 2 |
| --- |
| MExE-MlLoc | Location Information | Support of location information |

O

O

Type of location informationsupported, if any, e.g.

No, GPRS, cell, other E-OTD, TOA, etc.

Example coding:

| MExE-MlLoc: E-OTD |
| --- |
| MExE-MlLociIn |
| Location information | O | O |

Actual location information (as defined by type)

Example coding:

| MExE-MlLociIn: xxxxxxxxxxxxxxx |
| --- |
| MExE-MuUpProfile | User profile | O | O |

Transfer of the User Profile; individual characteristic(s) of the profile

Example coding:

| MExE-MuUpProf: nnnnnnnn |
| --- |
| MExE-MURL |
| O | O |

An indirect reference to a location where the MExE MS’s characteristics may be obtained

Example coding:

| MExE-MURL: http:://name.co.com/profile |
| --- |
| MExE-MaAddcCh | Additional characteristics | O | O |

Support of additional characteristics, e.g. none, smart card reader, docking station, etc.

Example coding:

| MExE-MaAddcCh: docking-station |
| --- |
| MExE-MaAddiIn | Additional Information | O | O |

Manufacturer defined additional characteristics; free format

Example coding:

MExE-MaAddiIn: XYZ

Table 1: Capability negotiation characteristics