ETSI SMG4	Tdoc SMG4 4M99-070

Helsinki

17-19.2.1999

| CHANGE REQUEST No : |
| --- |
| . |
| Technical Specification GSM / UMTS: | 03.57 | Version | 1.4.0 |
|  | Submitted to SMG |
| for approval | x | without presentation ("non-strategic") |
|  | for information |
| with presentation ("strategic") |
| PT SMG CR cover form. Filename: crf26_3.doc |

| Proposed change affects: | SIM |
| --- | --- |
| ME | x | Network |

(at least one should be marked with an X)

Work item:

| Source: | Nokia | Date: | 10.2.1999 |
| --- | --- | --- | --- |

| Subject: | Service Termination |
| --- | --- |

| Category: | F Correction | x | Release: | Phase 2 |
| --- | --- | --- | --- | --- |
| A Corresponds to a correction in an earlier release |
|  | Release 96 |
|  | (one category | B Addition of feature |
|  | Release 97 |
|  | and one release | C Functional modification of feature |
|  | Release 98 | x |
| only shall be | D Editorial modification |
|  | Release 99 |
|  | marked with an X) |
| UMTS |

Reason for change:

The current wording seems to indicate that in certain cases, a service can't be terminated by the user.

| Clauses affected: | 4.7.3 |
| --- | --- |

| Other specs | Other releases of same spec |
| --- | --- |
| ( List of CRs: |
|  | affected: | Other core specifications |
| ( List of CRs: |
| MS test specifications / TBRs |
| ( List of CRs: |
| BSS test specifications |
| ( List of CRs: |
| O&M specifications |
| ( List of CRs: |

Other comments:

4.7.3	Service termination

A service may terminate by itself, by the provider of the service, or by the user; but the user shall not be able to terminate certain services when the service provider may appropriately control the service as part of user support. The mechanism for terminating a service shall be provided on a service by service basis as defined by the provider of the service.or be terminated by the provider of the service or by the user. The user is in charge of the service, except when the service provider may appropriately control the service as part of user support.