ETSI SMG4 MExE	Tdoc 4M99-074

Fort Worth, Dallas

12-14.1.1999

| CHANGE REQUEST No : |  | . |
| --- | --- | --- |
| Technical Specification GSM / UMTS: | 3.57 | Version | 1.3.0 |  |
| Submitted to SMG | 4 | for approval | x | without presentation ("non-strategic") | x |  |
| list plenary meeting or STC here | for information |  | with presentation ("strategic") |  |  |
| PT SMG CR cover form. Filename: crf26_3.doc |

| Proposed change affects: | SIM |  | ME | x | Network | x |
| --- | --- | --- | --- | --- | --- | --- |

(at least one should be marked with an X)

| Work item: | MExE |
| --- | --- |

| Source: | Alcatel Business System | Date: | 14.01.1999 |
| --- | --- | --- | --- |

| Subject: | Language value coding for negotiation language token |
| --- | --- |

| Category: | F Correction | x | Release: | Phase 2 |  |
| --- | --- | --- | --- | --- | --- |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (one category | B Addition of feature |  |  | Release 97 |  |
| and one release | C Functional modification of feature |  |  | Release 98 | x |
| only shall be | D Editorial modification |  |  | Release 99 |  |
| marked with an X) |  |  |  | UMTS |  |

| Reason for change: | ISO standard has already define a language coding and country coding. This coding is already used in GSM (SMS CB language, SIM file language preference) and in HTTP |
| --- | --- |

| Clauses affected: | 2.1 and 4.4.1 |
| --- | --- |

| Other specs | Other releases of same spec |  | List of CRs: |  |
| --- | --- | --- | --- | --- |
| affected: | Other core specifications |  | List of CRs: |  |
|  | MS test specifications / TBRs |  | List of CRs: |  |
|  | BSS test specifications |  | List of CRs: |  |
|  | O&M specifications |  | List of CRs: |  |

| Other comments: |  |
| --- | --- |

2.1	Normative references

[1]	GSM 01.04 (ETR 350): “Digital cellular telecommunications system (Phase 2+); Abbreviations and acronyms”.

[2]	GSM 02.57: "Digital cellular telecommunications system (Phase 2+);MExE Stage 1 Description"

[3]	Personal Java, this specification is available from Sun Microsystems’s website at http://java.sun.com/products/personaljava/index.html.

[4]	MNCRS WG 4 specifications are still under development. When completed, MNCRS WG 4 specifications will be available at http://www.mncrs.org/.

[5]	JTAPI 1.2, this specification, currently in the ECTF approval process, is available from Sun Microsystems’s website at http://www.java.sun.com.

[6]	Wireless Application Protocol (WAP) version 1.0, this specification is available from WAP‘s website at http://www.wapforum.org.

[7]	vCard – The Electronic Business Card Exchange Format – Version 2.1, The Internet Mail Consortium (IMC), September 1996, http:/www.imc.org/pdi/vcard-21.doc.

[8]	vCalendar – The Electronic Calendaring and Scheduling Exchange Format – Version 1.0, The Internet Mail Consortium (IMC), September 1996

[9]	Hypertext Transfer Protocol – HTTP/1.1, IETF document RFC2068

[10]	Java Mail API version 1.0.2, available from http://www. java.sun.com

[11]	UMTS TR 22.70: “Universal Mobile Telecommunications System (UMTS); Service aspects; Provision of Services in UMTS - The Virtual Home Environment”.

[12]	UMTS TS 22.xx: “Universal Mobile Telecommunications System (UMTS); Provision of Services in UMTS - The Virtual Home Environment: Stage 1”.

[13]	ISO 639 International Standard code for the representation of name of languages

[14]	ISO 3166 International Standard code for the representation of name of countries

4.4.1	Capability negotiation characteristics

The generic set of capabilities which may be negotiated between the client and the server consists of the subsequently identified characteristics.:-

| Token | Characteristics | Optionality | Description |
| --- | --- | --- | --- |
|  |  | Client to MSE | MSE to Client |  |
| MExE-class | MExE Classmark | M | O | Classmark of the MExE device, e.g. 1, 2, etc. |
| MExE-manuf | Device | Manufacturer | O | O | Identification of the manufacturer, e.g. Motorola |
| MExE-model |  | Model | O | O | Model type, e.g. StarTac 130 |
| MExE-serial-no |  | Serial Number | O | O | Manufacturer’s model, e.g. 1.1.0 |
| MExE-software |  | SoftwareVersion | O | O | Manufacturer’s software version, IMEISV |
| MExE-resolution | Display | Size | resolution | O | O | Pixel size of the display, e.g. 200x150 etc. |
| MExE-chars |  |  | Characters | O | O | Number of lines and characters per line, e.g. 3x20 |
| MExE-colours |  | Colour/monochrome | Number of colours | O | O | The number of colours supported, e.g. 16,000 |
| MExE-greyscale |  |  | Greyscale | O | O | The number of gray scale, e.g. 2 for black and white only |
| MExE-voice | Input mode | Voice |  | O | O | Indication of whether voice capture is supported, i.e. yes/no |
| MExE-keyboard-id |  | Keyboard type | Keyboard identity | O | O | Type of keyboard supported |
| MExE-keyboard-lang |  |  | Human language | O | O | Language used on keyboard, i.e. English -UK, Swedish-Finland, Norwegian-Bokmal, German-Swiss etc. Example coding: MExE-kbdlg: EN-UK (see ref 13 nd 14) |
| MExE-keys |  |  | Number of keys | O | O | The number of keys supported by the keyboard, i.e. 102 |
| MExE-pointer |  | Pointing device | Identity | O | O | Type of pointing device, i.e. touchscreen, mouse |
| MExE-human-lang | Human Language | O | O | Preferred language in which the user wishes to work , i.e English-UK, Swedish-Finland, Norwegian-Bokmal, German-Swiss etc. Example coding: MExE-hlang: EN-UK (see ref 13 and 14) |
| MExE-formal-lang | Formal Language | O | O | Prioritised list of renditions for formal languages, e.g. HTML, WML |
| MExE-protocols | Additional Protocols | O | O | List of additionally supported protocols of the MExE device, e.g. SIM Toolkit |
| MExE-bearers | Supported Bearers | O | O | Prioritised list of preferred bearers, e.g. SMS, USSD, GPRS |
| MExE-classmark-differentiator | Difference to base Classmark | O | O | Identification of the devices’ components differing from the base Classmark definition |
| MExE-memory-type | User authorised available memory | Type of memory | O | O | Type of memory, e.g. RAM, flash memory, hard disk |
| MExE-memory |  | Amount of memory | O | O | Amount of memory authorised by the user for MExE, e.g. xxxKb |
| MExE-audio-codec | Multimedia | Audio codec type | O | O | Prioritised list of preferred audio codecs (cf. H.323) |
| MExE-video-codec |  | Video codec type | O | O | Prioritised list of preferred video codecs (cf. H.323) |
| MExE-trsf-size | Transfer limits | Size | O | O | Maximum size of transfers |
| MExE-trsf-time |  | Time | O | O | Maximum duration of transfers |
| MExE-loc-support | Location Information | Support of location information | O | O | How, and whether, location information is supported, e.g. No location information supported, GPRS, cell, other |
| MExE-location |  | Location information | O | O | Actual location information |
| MExE-user-profile | User profile | O | O | Transfer of the User Profile |
| MExE-add-chars | Additional characteristics | O | O | Support of additional characteristics, e.g. smart card reader, docking station, etc. |
| MExE-add-info | Additional Information | O | O | Manufacturer defined additional characteristics |

Table 1: Capability negotiation characteristics