This document provides a first attempt at a table listing the requirements for a MExE ME as mentioned in 02.57, MExE Service Description, Stage 1.

The aim of this table is to provide a requirements framework in order to allow subsequent specification work such as API definition to be performed more efficiently.

The following provides information relating to the table headings:

| Key to Requirements Table Headings |
| --- |
| Heading | Explanation |
| i.d. | A unique identifier for each requirement. An identifier can be assigned only once. This heading also contains the [i.d.] of the next requirement to be entered - embedded as a table function (F9 to update). |
| Category | A series of broad categories into which requirements are placed. "J" means this requirement relates directly to the specification of a Java API. "I" means this requirement relates to implementation, and puts the specification of a Java API into context. |
| Requirement | The actual requirement, which should be as unambiguous (and indivisible) as possible |
| Reference | A reference into a document within which the requirement is mentioned, if applicable |
| Priority | Requirements may be mandatory or optional |
| Capability in GSM 03.57 V1.4.0 | Identifies a section number in 03.57 V1.4.0 and optional comments about capabilities meeting the specified requirement |
| Comment | A general purpose comment field |

Assumption: This table accurately reflects the current thinking of the MExE group in terms of Stage 1 requirements. Currently, there are many deletions, wording changes, and additions to the current GSM 02.57 V7.0.0 Stage 1 Requirements document. I assume that 02.57 will be updated to reflect the changed requirements as listed in this table.

The security requirements section is not filled out at this time.

| i.d. [107] | Cat | Requirement | Ref | Priority | Capability in GSM 03.57 V1.4.0 | Comment |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | High Level |  |  |  |  |
| 1 | J | The MExE ME shall provide a means for applications, applets and content to access the user interface |  | Mandatory | G: [Can be inferred from 4.0 - Need a statement in 4.0 that individual classmarks must provide the means … to access the user interface] W: [5.7.1] The user interface of WAP services is realised by the Wireless Markup Language, WML and WMLScript J: [6.2.2] MExE devices shall provide APIs specified in PersonalJava 1.1, which includes java.awt |  |
| 3 | J | The MExE ME shall provide the means to allow the transfer of applications, applets or content either automatically or on demand according to MExE security requirements | 02.57 v7.0.0 6.1.0 | Mandatory | G: [4.3] and [4.4] Interaction between the MExE MS and the MSE shall be supported by the use of HTTP/1.1, or an HTTP/1.1 derived protocol. Security covered in [9.1]. W: [5.7.3] The core of WSP/B is a binary version of HTTP/1.1…WSP/B supports the push of data from server to client J: [6.2.7.1] The MS shall support the HTTP/TCP/IP protocols for transfer of services, and the MS may support other protocols for transfer of services |  |
| 4 | I | The MExE ME shall provide the means to allow the upgrade of existing applications across the GSM/UMTS network subject to MExE security requirements and user authorisation | 02.57 v7.0.0 6.1.0 | Mandatory | G: [4.7.2] supports name and versioning. Security covered in [9.1] as deleting? W: Not found J: [6.2.7.1] services must be version-controlled…HTTP transparent content negotiation facilities shall be used to accomplish version control |  |
| 5 | I | The MExE ME shall allow the user to personalise services | 02.57 v7.0.0 6.1.0 | Mandatory | G: [4.0] Content negotiation allows for flexible choice of formats available from a server or adaptation of a service to the actual classmark of a specific client device. W: Not found J: Not found | FFS – relates to user profile (i.e. the way the information is displayed on the MExE ME , not the type/nature of information). DELETE FROM CLARIFICATION LIST BUT DO NOT CR |
| 6 | J | The MExE terminal shall allow the user to utilise both internet and intranet applications, applets and content according to MExE security requirements | 02.57 v7.0.0 6.1.0 | Mandatory | G: [4.3] and [4.4] imply IP, HTTP, or a gateway to them. Security same as add or delete applet in [9.1] What about security for content? W: via WML and WTP J: [6.2.2] |  |
| 54 | J | The MExE ME shall possess an architecture that is capable of supporting applications, applets and content in a standard execution environment independently of the MExE ME manufacturer | 02.57 v7.0.0 9.1.0 | Mandatory | G: Not explicitly stated in [4.0] W: Not explicit J: Not explicit | CR |
|  |  | Classmarks |  |  |  |  |
| 11 | I | MExE applications and applets conforming to a particular MExE classmark shall be supportable by all MExE MS’s of that classmark regardless of MExE MS manufacturer | 02.57 v7.0.0 5.3 | Mandatory | G: Not explicitly stated in [4.0] W: Not explicit J: Not explicit |  |
|  |  | User Interface Configuration Management |  |  |  |  |
| 14 |  |  |  |  |  |  |
| 2 | I | The MExE ME shall allow the user to personalise the user interface within bounds defined by the manufacturer | 02.57 v7.0.0 6.1.0 | Mandatory | G: [4.5] and [4.6] support, although no means for updating user interface customisation is actually specified. Security NOT covered in [9.1] W: Not specified how WML and user profile interact J: Need to update [6.2.2] with info from JavaPhone | The extent of "personalisation" will be limited by the terminal manufacturer. E.g. screen colours, ring patterns, screen saver This needs further clarification – Nash |
| 15 | I | The user shall be able to manage the user interface configuration of the MExE MS within bounds defined by the manufacturer | 02.57 v7.0.0 6.2.1 | Mandatory | G: [4.5] implies management. [4.6.1] implies the capability to namage, but not explicit W: Need to update [6.2.2] with info from JavaPhone J: Not found | The extent of "personalisation" will be limited by the terminal manufacturer. |
| 16 | I | The MExE ME shall allow the user to identify the current user interface configuration within bounds defined by the manufacturer | 02.57 v7.0.0 6.2.1 | Mandatory | G: [4.5] implies identification W: Not found J: Need to update [6.2.2] with info from JavaPhone |  |
| 17 | I | The MExE ME shall allow the user to add, modify or delete a particular user configuration within bounds defined by the manufacturer | 02.57 v7.0.0 6.2.1 | Mandatory | G: [4.5] and [4.6] imply adding and modifying W: Not found J: Need to update [6.2.2] with info from JavaPhone |  |
| 18 | I | It shall be possible to obtain the user interface configuration information, subject to MExE security requirements, which is resident on the MExE ME, the SIM or the network | 02.57 v7.0.0 6.2.1 | Mandatory | G: [4.5] and [4.6.1] imply obtaining info is possible W: Not found J: Need to update [6.2.2] with info from JavaPhone, plus specifying where to retrieve from | FFS – similar to “.dt”, “.xdefaults” in Unix. [Further contribution expected from Nash]. Change Request |
| 20 |  | The user interface configuration management information may be stored on the MExE ME, the SIM or the network, subject to MExE security requirements. |  | Mandatory | G: No means identified for specifying where to store info. Security NOT covered in [9.1] W: Not found J: Need to update [6.2.2] with info from JavaPhone |  |
| 22 | J | Any MExE ME shall be able to access and interpret user interface configuration data, according to MExE security requirements |  | Mandatory | same as 18? | Assume “user profile” means personal details i.e. name, e-mail etc. Clarification required on defn of terms “The user profile data shall be associated with a given user” is part of defn (req 23) “User profile data” is a superset of “user interface configuration” – partitioning/access is FFS. NB: “interpret” may need to be clarified! CR – add to end of para3.6.2.1, 02.57 |
|  |  | Service Management |  |  |  |  |
| 25 | I | The MExE ME shall allow the user to request the range of MExE services available from the PLMN MExE service provider | 02.57 v7.0.0 6.2.2 | Mandatory | G: Not found. Add to [4.3] or [4.8] VHE? W: Not found. Add to [5.7]? J: Not found. Is this Jini? | Misgivings about how registration is carried out, notification messages etc. What is the notification mechanism? This is perceived as a common address (e.g. URL. Same address could be used when roaming – use (e.g.) DNS to resolve actual server address). This address is used to provide the first point of access to a MExE network. The user is provided with a list of MexE services available from the PLMN service provider. MExE is allowed to stipulate only access to GSM/GPRS/UMTS MExE SPs – PLMN independent SPs lie outside of the scope of MExE standardisation. When roaming, the user could collect a number of addresses, including HPLMN and VPLMN. |
| 26 | I | The MExE ME shall allow the user to determine which MExE applications, applets and content are currently resident on the MExE ME | 02.57 v7.0.0 6.2.2 | Mandatory | G: [4.7.2] W: Not found J: Not found | Resident in terminal only or also in network? |
| 103 |  | The MExE ME shall be able to determine whether or not the GSM/GPRS/UMTS connection required by an application has been broken |  | Mandatory | G: [4.9] W: Not found J: Not found. Check JTAPI Mobile. |  |
| 102 |  | The MExE ME shall allow the user to control , via the user profile, whether or not an application is automatically executed once it has been downloaded, according to MExE security requirements | 03.57 4.x | Optional | G: [4.7.1] <?>. Security NOT covered in [9.1] W: Not found J: [6.2.8] | Execution may in some instance include configuration |
|  |  | Bearer Services |  |  |  |  |
| 30 | J | The MExE ME shall provide access to a range of one or more GSM/GPRS/UMTS bearer services, within the capabilities of the ME and network | 02.57 v7.0.0 7.0.0 | Mandatory | G: [4.3] W: [5.1] J: [6.2.3] and [6.2.7.1] | Transport protocols shall be defined in other specs (stage2,3?). Use only standard protocols (no proprietary) |
|  |  | Protocols |  |  |  |  |
| 34 | J | MExE protocols shall be independent of the type of underlying bearer | 02.57 v7.0.0 8.2.0 | Mandatory | G: Not found. Add to [4.0] or [4.3]? W: [5.1, 5.7.3] The WSP/B and WTP protocols provide bearer-independent access to SMS, USSD, circuit- and packet-switched data services J: [6.2.7.1] “The MS shall support the HTTP/TCP/IP protocols for transfer of services” and “transfer of services is performed in a bearer-independent manner, so that any supported bearer can be used to transfer services” | What are upper layer MExE protocols? Definition required – suggest all layers above the bearer. Definition accepted – CR to definition section of 02.57 |
| 36 | J | Applications and applets shall be able to request specific bearer services and to be notified as to their availability | 02.57 v7.0.0 8.2.0 | Optional | G: [4.9] W: [5.5] <?> Is this supported by the WAP Telephony API? J: [6.2.3] “Extensions to JTAPI 1.2 are required to support … call bearer types (all GSM circuit switched data, fax, emergency)” Supported in JTAPI Mobile MobileDataCall interface |  |
| 38 | J | MExE protocols shall be able to add new bearers | 02.57 v7.0.0 8.3.0 | Mandatory | G: Not found. Add to user profile? Is this a generic or specific requirements? Security NOT covered in [9.1] W: [5.1] Since WAP is based on a scalable layered architecture, each layer can develop independently, making it possible to switch onto new bearers without major changes in other layers J: [6.2.3] <?> Would this require making change requests to the Java Telephony API Specification group? |  |
| 40 | I | It shall be possible for applications and services to install new protocols | 02.57 v7.0.0 8.4.0 | Optional | G: Not found. Security NOT covered in [9.1] W: [5.1] “Since WAP is based on a scalable layered architecture, each layer can develop independently, making it possible to use new protocols without major changes in other layers”. No means or API specified. J: [6.2.3] Generic capability via sockets interface. Nothing specific. | CR |
| 41 | I | MExE protocols shall be independent of the network nodes being communicated with | 02.57 v7.0.0 8.5.0 | Mandatory | G: [4.8] VHEsupports transparent service access. W: [5.7.2] <?> provided by WAP Gateway? [5.7.3] specifies datagram transport. J: [6.2.3] Supported via JTAPI Mobile. |  |
| 43 | I | MExE protocols shall support a generic technology independent capability negotiation, notification and enquiry mechanism between the MExE ME and the MExE service environment | 02.57 v7.0.0 8.6.0 | Mandatory | G: [4.4] and [4.4.1] W: [5.3] <?>. See also [5.7.3] Session Establishment J: [6.2.7.1] supports via HTTP |  |
| 100 | I | The MExE ME shall allow a MExE service provider to determine the MExE ME capabilities, according to MExE security requirements. | 02.57 v7.0.0 6.1.0 | Mandatory | G: [4.4.3]. Security NOT covered in [9.1] W: [5.3] may support? J: Not found | NB: MExE Service Provider can be anybody – hence apply MExE security policy |
| 101 | I | The MExE ME shall perform capability and content negotiation according to Section 4.4. of 03.57 | 03.57 Section 4.4 | Mandatory | G: [4.4] W: Not found J: Not found | Table reference IN NEW VERSION |
| 48 | I | The capability negotiation mechanism shall be extensible. | 02.57 v7.0.0 8.6.0 | Mandatory | G: [4.4.1] Table specifies MExE-addch and MExE-addin tokens W: Not found J: Not found | CR |
| 50 | I | MExE protocols shall support the capability to transfer new applications, applets and content to and from the MExE ME as required by the user according to MexE security requirements | 02.57 v7.0.0 8.8.0 | Mandatory | G: [4.7.2] <?>. Security covered in [9.1] W: [5.7.3] J: [6.2.7.1] | CR required |
| 51 | I | The MExE protocols shall support both user initiated and MexE server initiated transfer of applications, applets and content as required by the user, according to MExE security requirements | 02.57 v7.0.0 8.8.0 | Mandatory | G: How is this distinguished from capability negotiation in [4.4.3] and [4.4.4]? Security covered in [9.1], but push and pull not made explicit W: [5.7.3] J: [6.2.7.1] | CR required to section 8.8 of 02.57v7.0.0 |
|  |  | MS Application Execution Environment |  |  |  |  |
| 55 | J | Ability to cleanly and safely install applications and associated data (e.g. icons) shall be provided. |  | Optional | G: [4.7.1]. Security covered in [9.1] W: Not found J: [6.2.2] and [6.2.8] |  |
| 56 | J | Ability to cleanly and safely de-install applications and associated data (e.g. icons) shall be provided. |  | Optional | G: [4.7.4]. Security covered in [9.1] W: Not found J: Not found |  |
| 57 | I | The MExE classmark 2 terminal shall be able to implement HTML |  | Mandatory | G: Not found. Should be in 4.2? W: Not applicable? J: Not found. Should be in 6.2.6? | WML for classmark 1, HTML for classmark 2 This an an API req, relating to stage 2. |
| 58 | I | The MExE classmark 2 terminal shall be able to implement WML and WMLScript |  | Mandatory | G: Not found. Should be in 4.2? W: [5.1] J: [6.2.6] | This an an API req, relating to stage 2. |
| 105 | I | The MExE Classmark2 device shall contain a pre-installed WAP browser |  | Mandatory | G: Not found. Should be in 4.2? W: Not applicable? J: [6.2.6] | I.e. browser capable of rendering WML and WMLScript |
| 106 | I | The MExE Classmark2 device shall allow the pre-installed WAP browser to be updated |  | Mandatory | G: Not found. Should be in 4.2? W: Not applicable? WAP browser never explicitly mentioned in [5.x] J: [6.2.6] |  |
| 59 | I | MExE shall define a set of standardised content coding schemes i.e. vCard, vCalendar |  | Mandatory | G: [4.4.2] W: [5.4] J: [6.2.4] partially covers | Is vCard, vCalendar support required? This an an API req, relating to stage 2. |
| 60 | I | The MExE ME shall be able to support HTML and/or WML |  | Mandatory | G: [4.4] W: [5.4] supports WML J: [6.2.6] for WML; HTML not found. |  |
| 61 | J | MExE ME shall support the 7bit GSM default character set |  | Mandatory | G: Not found W: Not found J: Not found | As defined in 03.38 v6.0.1 Note: User defined 8bit scheme is not mentioned here. Should it be? CR to section 9.2 (last para) of 02.57v7.0.0 – replace “defined” with “identified” |
| 104 | I | The MExE ME shall be capable of supporting the UCS2 character coding scheme |  | Optional | G: Not found W: Not found J: [6.2.2] in PersonalJava spec | Unicode 16bit character coding |
| 63 | I | The MExE ME shall support a core API, known as the core MExE API | 02.57 v7.0.0 9.3.0 | Mandatory | G: “core API” never specifically mentioned. [4.0] specified WAP and Java W: [5.2] where mandatory is the same as core J: [6.2] where mandatory is the same as core | The core MExE API defines the minimal API set that a MExE ME needs to support |
| 64 | I | The core MExE API shall consist of both generic and GSM/UMTS specific aspects | 02.57 v7.0.0 9.3.0 | Mandatory | G: Not found W: [5.1] J: [6.2.2] and [6.2.3] |  |
| 65 | I | The MExE ME shall support standardised MExE API extensions in addition to the core MExE API | 02.57 v7.0.0 9.3.0 | Optional | G: Not found W: [5.2] and [5.5] call control include Network Specific libraries J: [6.2.2] |  |
| 66 | J | The standardised MExE API extensions shall include access to location information, according to MExE security | 02.57 v7.0.0 9.3.0 | Mandatory | G: Not found. Security covered in [9.1] W: Not found J: Not found | What is the meaning of "mobility information"? CR Location |
| 67 | J | The MExE APIs shall provice support for applications and applets to access the GSM/UMTS functionality present in the GSM/UMTS terminal according to MExE security . |  | Mandatory | G: Not found. Security covered in [9.1] W: [5.1] and [5.5] J: [6.2.2] and [6.2.3] | Functionality includes telephony, e-mail, SMS, fax. |
| 68 | J | All Java APIs specified by MExE for use on a MExE ME shall be approved by Sun Microsystems. |  | Mandatory | G: Not found W: Not applicable J: Not found |  |
| 69 | J | The MExE ME shall provide local file system support, according to MExE security | 02.57 v7.0.0 6.1.0 | Optional | G: Not found. Security covered in [9.1] W: Not found J: Not found |  |
| 70 | I | The MExE ME shall allow the user to identify the version number of applications, applets and content contained within it | 02.57 v7.0.0 6.1.0 | Optional | G: [4.7.2]. Security NOT covered in [9.1] W: Not found J: [6.2.7.1] partially addresses |  |
| 71 | J | A MExE ME shall notify applications of any power state changes. | 02.57 v7.0.0 6.1.0 | Optional | G: Not found. Security NOT covered in [9.1] W: Not found J: [6.2.2] states for further study; proposal in JavaPhone |  |
| 72 | J | A MExE ME shall support standardised access of a smartcard if a smartcard reader is present on the MExE ME | 02.57 v7.0.0 6.1.0 | Optional | G: Not found. Security NOT covered in [9.1] W: Not found J: mentioned in [6.2.2] | Support of smartcard reader is not a mandatory requirement. |
|  |  | Security |  |  |  |  |
| 76 | I | Transferred MExE applications, applets and content shall be secure and verified | 02.57 v7.0.0 11.0.0 | Mandatory | G: Not found W: Not found J: Not found | “secure” – received in same state as it was sent i.e. has not been tampered with |
| 77 | I | The MExE ME shall provide support for four security levels | 02.57 v7.0.0 11.0.0 | Mandatory | G: Not found W: Not found J: Not found | See Table XX in Section 9.1 of 03.57 for an elaboration of security levels. Multiple security levels |
| 79 | I | The security level of applications, applets and content shall be verified by the MExE ME | 02.57 v7.0.0 11.0.0 | Mandatory | G: Not found W: Not found J: Not found |  |
| 81 | I | The MExE subscriber shall be able to control whether applications, applets and content of specific security levels may be transferred to the MExE ME | 02.57 v7.0.0 11.0.0 | Mandatory | G: Not found W: Not found J: Not found |  |
| 82 | J | An application/applet shall specifiy whether or not it can share its own files with other applications/applets | 02.57 v7.0.0 11.0.0 | Mandatory | G: Not found W: Not found J: Not found | More input required here |
| 83 | I | Within the constraints of the defined security levels, the user shall have ultimate control over the use of bearer services | 02.57 v7.0.0 11.0.0 | Mandatory | G: Not found W: Not found J: Not found | CR Incorporate USSD and SS signalling (comment by K Holley at MExE security meeting, SMG4 plen 11 – 14th Dec 1998) |
| 84 | I | A means to authenticate the MExE subscriber and MExE server shall be provided | 02.57 v7.0.0 11.0.0 | Mandatory | G: Not found W: Not found J: Not found | CR This may be performed by the MExE ME, an intermediate entity or the GSM/UMTS network |
| 85 | I | MExE shall continue to support the inherent security and integrity of the GSM/GPRS/UMTS network | 02.57 v7.0.0 11.0.0 | Mandatory | G: Not found W: Not found J: Not found |  |
| 86 | I | The integrity of the SIM and existing GSM/UMTS security mechanisms shall not be compromised by the introduction of MExE services | 02.57 v7.0.0 11.0.0 | Mandatory | G: Not found W: Not found J: Not found |  |
| 87 | I | All aspects relating to GSM security shall be performed by the SIM | 02.57 v7.0.0 6.1.0 | Mandatory | G: Not found W: Not found J: Not found |  |
|  |  | Interworking with other Network Features |  |  |  |  |
| 90 | I | All services available in the network shall continue to be offered in addition to MExE services | 02.57 v7.0.0 12.0.0 | Mandatory | G: Not found W: [5.5] <?>The WAP Telephony API exposes telephony functions to service authors as a set of libraries. See Network Common and Network Specific library definitions. J: Not found |  |
|  |  | Network Interworking |  |  |  |  |
| 92 | I | All services offered in co-operation with other networks shall continue to be offered in parallel with MExE services | 02.57 v7.0.0 13.0.0 | Mandatory | G: Not found W: Not found J: Not found |  |
|  |  | Communications |  |  |  |  |
| 93 | J | MExE MEs shall support peer to peer communication between MExE devices | 02.57 v7.0.0 6.1.0 | Optional | G: [4.3] and Figure 1 implies support W: [5.7.1] WMLScript may be used to access the device and its peripheral functionality. J: Add Java Communications API to [6.2.2]. Does not support peer-to-peer over GSM? | Includes e.g. IrDA, Bluetooth, USB (which are outside the scope of MExE specifications), user-to-user signalling, USSD (which are within the scope of MExE specifications) etc. |
| 95 | J | A MExE application shall be able to access any or all external interfaces present on the MExE ME, subject to the limitations of the MExE ME |  | Optional | G: Add to table in [4.4.1]? W: [5.7.1] WMLScript may be used to access the device and its peripheral functionality. J: [6.2.2] Smart Card API. Add Java Communications API to [6.2.2]. | Serial, parallel, infra-red etc. |
| 96 | J | The means for MExE service provider specific applications and applets on the MExE ME to communicate with other GSM network nodes shall be provided. | 02.57 v7.0.0 6.1.0 | Optional | G: Not found W: [5.5] Network Specific Library J: [6.2.3] Extensions to JTAPI 1.2 are required to support USSD [Couldn’t find this in JTAPI Mobile 1.3] | USSD main bearer |

# Comments

Automatic installation of an application is scary. It is not only a security issue, but also almost like invasion of private propert.

The user interface can't be personalised, because the terminal manufacturer is the only one who knows about certain hardware parts of the UI, like buttons.

The user interface can't be personalised, because the terminal manufacturer is the only one who knows about certain hardware parts of the UI, like buttons.

I would interpret this to mean "configuration profile", but not applying really to the UI.

This seems like a major deviation from the original requirement, which stated “The modification in the range of services, or addition of new services, offered over the network shall not be restricted by the MExE protocols.” The implication of the new requirement seems to be that an app or service can load a new version of HTTP, WTP, UDP, IP, etc. This would also seem to require the “according to MExE security requirements” clause appended.

I don't understand…