ETSI SMG4	TSGT2#2(99)033

Boeblingen, 1926-28 May 1999

| CHANGE REQUEST No : |
| --- |
| Technical Specification GSM / UMTS: | 03.57 | Version | 1.7.0 |
|  | Submitted to SMG |
| for approval | X | without presentation ("non-strategic") |
|  | for information |
| with presentation ("strategic") |

| Proposed change affects: | SIM |
| --- | --- |
| ME | x | Network |

(at least one should be marked with an X)

| Work item: | MExE Stage 2 03.57 |
| --- | --- |

| Source: | Nokia | Date: | 3.5.1999 |
| --- | --- | --- | --- |

| Subject: | Datagram API name resolution |
| --- | --- |

| Category: | F Correction |
| --- | --- |
| Release: | Phase 2 |
| A Corresponds to a correction in an earlier release |
|  | Release 96 |
|  |  | B Addition of feature | x |
| Release 97 |
|  |  | C Functional modification of feature |
|  | Release 98 | x |
|  | D Editorial modification |
|  | Release 99 |
|  | UMTS |

| Reason for change: | The name resolution mechanism is not mandatorily or clearly specified in JavaPhone. Only an example is given. Therefore MExE needs to define at least a basic level of name resolution, otherwise it will be impossible for applications to set address values for recipient names they wish to use (as part of their initial setup.) |
| --- | --- |

| Clauses affected: | 8 |
| --- | --- |

| Other specs | Other releases of same spec |
| --- | --- |
| ( List of CRs: |
|  | Affected: | Other core specifications |
| ( List of CRs: |
| MS test specifications / TBRs |
| ( List of CRs: |
| BSS test specifications |
| ( List of CRs: |
| O&M specifications |
| ( List of CRs: |

Other comments:

6.X.X		Datagram Recipient Addressing

The Datagram API (as specified by JavaPhone) may resolve Recipient names using a name resolution service. The MExE Java implementation shall at least be able to resolve names using the addressbook.

The implementation of the Datagram API shall support use of the addressbook to resolve names: The addressbook entries shall be searched for items whose name matches the server/service name by the Datagram API implementation in order to resolve Recipient names to actual addresses. It shall look for an item which has an aggregate field of type

"X-SERVICE" with a value equal to the Recipient name, using the following syntax:

recipient_name:  *server_name ":" *service_name

server_name: *anything

service_name: *anything

anything: { any printable ASCII character except '=', ',', ':' and special characters like newline }

; e.g. "The PIZA Hut:orders".

Then it shall use the value of aggregate attributes of this field which are typed as "X-SERVICE-ADDRESS". These strings shall specify in order, the preferred and available protocols and addresses for the recipient name specified in the X-SERVICE field. The string value in each X-SERVICE-ADDRESS field shall be formatted as so:

address: *transport_protocol "=" *transport_address "," *bearer_protocol "=" *bearer_address

transport_protocol: *alphanum

transport_address: *internet_address | *phone_number | *port_number | *anything

bearer_protocol: *alphanum

bearer_address: *internet_address | *phone_number | *port_number | *anything

alphanum: {"A"-"Z"} | {"a"-"z"} | {"0"-"9"}

internet_address: *dotted_decimal_address | *dns_name

dotted_decimal: *number "." *number "." *number "." *number

dns_name: { *alphanum , "." }

number: {"0"–"9" }

phone_number: "+" *number

anything: { any printable ASCII character except '=', ',', ':' and special characters like newline }

... where at least the following transport/bearer combinations shall be supported if the device supports the bearer/transport combination. (E.g. a device which does not support SMS as a bearer will not be required to support WDP over SMS, or plain SMS.)

| Transport/bearer combination | Value of *transport_protocol | Value of *transport_address | Value of *bearer_protocol | Value of *bearer_address |
| --- | --- | --- | --- | --- |
| WDP over SMS | WDP | A port number | SMS | A phone number |
| Plain SMS | SMS | A phone number |
| WDP over HTTP | UDP | A port number | URL | A URL |
| UDP over IP | UDP | A port number | IP | An internet address |

For example:

WAP Datagram over SMS:	"WDP=358,SMS=+358503583862"

Plain SMS:			"SMS=+358503583862"

WDP over HTTP:		"UDP=80,URL=http://somewhere.on.the.web/path/name"

UDP over IP:			"UDP=80,IP=147.23.120.2"