| 3GPP TSG-T2 /ETSI SMG4 |  | T2x00085 |
| --- | --- | --- |
| Vuokatti, Finland, 26-28 September 2000 |  | e.g. for 3GPP use the format TP-99xxx or for SMG, use the format P-99-xxx |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 23.057 | CR |  | Current Version: | 3.2.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submission to: |  | for approval | X |  | strategic |  | (for SMG |
| list expected approval meeting # here ( | for information |  |  | non-strategic |  | use only) |
| Form: CR cover sheet, version 2 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CR-Form-v2.doc |
| Proposed change affects: | (U)SIM |  | ME | X | UTRAN / Radio |  | Core Network |  |
| (at least one should be marked with an X) |
| Source: | Nokia | Date: | 20/9/2000 |
| Subject: | Corrections to the way how pushed MExE executables are to be treated in a MExE device. |
| Work item: | MExE |
| Category: | F Correction |  | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature | X |  | Release 97 |  |
| shall be marked | C Functional modification of feature |  |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 |  |
|  |  |  |  | Release 00 | X |
| Reason for change: | There are no executables which will be pushed to MExE device without any prior knowledge of the user. The current text excludes pushed executables from both trusted domains and untrusted areas. If the executable is to be pushed to the device, it has to get a distinct status within MExE security framework rather than to be totally dropped out as such. |
| Clauses affected: | 8.2.1 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

### 8.2.1	MExE executable Permissions for untrusted MExE executables

Subclause 8.2 identifies the permissions for MExE executables in the 3 domains (operator, MS manufacturer and Third Party). The permissions do not apply to untrusted MExE executables which are not permitted to execute within the domains.

In order to facilitate untrusted MExE executables having some limited access to MExE MS functionality beyond their very limited privileges, the following specific access permissions in Table 3 are extended to untrusted MExE executables:

- User interface

An untrusted, uninstalled MExE executable (e.g. an applet) can access the user interface output (display) and input (keyboard, mouse, ..) without user permission, but the sending of user data to a server to which the MExE executables has a session connection (e.g. as part of a browser sesssion) requires user permission.

An installed untrusted MExE executable shall only be able to access the user interface output (display) and input (keyboard, mouse, ..) with user permission. (Clearly, for the usability of untrusted MExE executables such as games, blanket user permission should be sought and given, and this is permissible.)

- File

File access is not permitted for untrusted MExE executables, except that untrusted MExE executables can access files only in the MExE executable’s own directory.

- Initiate a voice/data connection

Untrusted MExE executables shall be able to make calls under the following conditions.

In addition to an untrusted MExE executable possibly displaying the number to be called to the user, the number to be called shall be presented to the user for permission by a provisioned functionality of the MExE MS and not by the MExE executable itself. (This facility would support, for example, "click to dial" button/links in an untrusted MExE executable, and a MExE MS provisioned functionality then represents the number to the user for confirmation.)

- Generate DTMF

Untrusted MExE executables shall be able to generate DTMF tones under the following conditions.

An untrusted MExE executable is only permitted to send DTMF tones in a currently active call. The request to generate DTMF tones in the currently active call, shall result in the characters which the tones represent being presented to the user for permission by a provisioned functionality of the MExE MS.

- Add phonebook entry

Untrusted MExE executables shall be able to add a phonebook entry (i.e. name and number only) under the following conditions.

The name and the number to be added shall be displayed to the user for permission by a provisioned functionality of the MExE MS and not by the MExE executable itself. The phonebook entry shall not be added without user permission.  The function shall not be able to modify or delete any phonebook entry.

The untrusted MExE executables permitted to use the above facilities shall be MExE executables the user has downloaded himself. MExE executables/applets on the MExE MS due to the user having visited a particular web site are considered to be MExE executables that the user had downloaded himself.

In case of push type of download, the user first receives a push message comprised of a header and a MIME/type body, which is not an executable. If this message is to inform the user about a MExE executable awaiting to be downloaded/pushed to the MExE device, the user is the one to decide either to accept this push or reject it. If the executable comes from the untrusted source, it will be treated by MExE device as untrusted and therefore all the permissions for untrusted MExE executables are to be applied.

Untrusted MExE executables shall not be permitted access to any other functions.