| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
| --- | --- |
|  | 23.057 | CR |  | Current Version: | 3.3.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submission to: |  | for approval |  |  | strategic |  | (for SMG |
| list expected approval meeting # here ( | for information |  |  | non-strategic |  | use only) |
| Form: CR cover sheet, version 2 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CR-Form-v2.doc |
| Proposed change affects: | (U)SIM |  | ME | X | UTRAN / Radio |  | Core Network |  |
| (at least one should be marked with an X) |
| Source: | Motorola | Date: | 22/9/2000 |
| Subject: | Application version number |
| Work item: | MExE |
| Category: | F Correction |  | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature |  |  | Release 97 |  |
| shall be marked | C Functional modification of feature | X |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 |  |
|  |  |  |  | Release 00 | X |
| Reason for change: | As the version number may not always be available for any downloaded application (e.g. for PersonalJava applications), the requirement is re-worded such that support of the version number is not mandated. |
| Clauses affected: |  |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

## 4.7	Management of services

The MExE ME shall be capable of supporting services in a standard (WAP or Java) execution environment independently of the MExE ME manufacturer.  Management of services provides the user with the capability to:

- discover services;

- configure services ;

- control the transfer and execution of services;

- terminate or suspend executing services

on his MExE MS.

### Service discovery

A MExE user is able to request (or be informed about), the range of MExE services available from the MExE server to which it is connected. Support for the request, and transfer, of information on MExE services from the MExE server is primarily provided by the use of the capability negotiation mechanism.

All services available in the network continue to be available to the user, in addition to MExE services.

An example of an alternative means of possibly receiving information on MExE services, is the use of an application on the MExE MS which the user interrogates to provide services information (from various sources), and which in turn then obtains such information and presents it to the user. Such an example is not subject to standardisation.

### 4.7.2	Service configuration

- The user controls whether a service transferred to the MExE MS is also automatically configured in the MS. Configuration of a service may result in changes to user interface using icons, browsers or menus as applicable depending on the capability of the MExE MS to support them. The service name may be contained in the package in which it was received (i.e. a JAR file or script), assigned by the user during configuration, or some other means. If service automatic configuration is enabled, the user is notified of the automatic service configuration once it is completed.

- In the event that there is no authorisation for the automatic configuration of a transferred service, the user is notified that it was not configured.

- The user controls which services may be automatically configured.

- Subsequent user modification of a service’s configuration (e.g. by modification of use profile settings) shall take effect at the earliest possible opportunity thereafter.

### 4.7.3	Service management

- The MExE MS shall support the ability to determine which services are transferred to, resident, configured or executing on the MS. The information relating to the services shall include the name as a minimum,and the version number if available.

- The user controls which services are permitted or denied to be transferred , resident, configured or executing on the MExE MS via the user profile, eg. AcceptDownloadableSoftware. The user profile permits characteristics such as security level, identification of specific services etc. to manage services on the MExE MS.