| 3GPP TSG-T2 /ETSI SMG4 |  | T2x00101 |
| --- | --- | --- |
| Vuokatti, Finland, 26-28 September 2000 |  | e.g. for 3GPP use the format TP-99xxx or for SMG, use the format P-99-xxx |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 23.057 | CR |  | Current Version: | 3.3.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submission to: |  | for approval | X |  | strategic |  | (for SMG |
| list expected approval meeting # here ( | for information |  |  | non-strategic |  | use only) |
| Form: CR cover sheet, version 2 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CR-Form-v2.doc |
| Proposed change affects: | (U)SIM |  | ME | X | UTRAN / Radio |  | Core Network |  |
| (at least one should be marked with an X) |
| Source: | Motorola | Date: | 22/9/2000 |
| Subject: | Core software download support |
| Work item: | MExE |
| Category: | F Correction |  | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature |  |  | Release 97 |  |
| shall be marked | C Functional modification of feature | X |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 |  |
|  |  |  |  | Release 00 | X |
| Reason for change: | Manufacturer applications may be applications for "Software Defined Radio (SDR)". The MExE security table (table 3)is updated to provide support for SDR applications. |
| Clauses affected: | Chapter 8, table 3 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

Table 3: Security domains and actions

|  | MExE Security Domains |
| --- | --- |
| Actions | Operator | Manufacturer | Third Party |
| Device core function access Start/stop radio Turn on/off device Write time and/or date Activate a user profile Modify a user profile | No |
| Support of Core Software Download e.g. Update UE software | No | Yes | No |
| SIM smart card low level access11 Send APDU Slot management (power on/off, reset, port lock…) | No |
| 11 – Access to SIM is provided using more high level API as phonebook, application launching |
| Network Security access Run algorithm Verify CHV/2 or UNBLOCK CHV/2 Activate/deactivate CHV Modify CHV/2 | No |
| Network property access Get IMSI Get home network Select network | Yes | No |
| Network services access Initiate a voice/data connection 3 Accept a voice/data connection 3 Call forward 4 Multiparty call 4 Call deflection 4 Explicit call transfer 4 Terminate an existing connection Hold an existing connection Resume an existing connection Send point-point message (e.g. SMS, USSD) 4 Generate DTMF Query network status Get signal level Get call list QoS management | Yes | Yes 6 |
| 3 – A network connection may be via any supported bearer service 4 – Multiparty, deflection, and explicit call transfer shall be permitted only to numbers explicitly supplied by the user to the MExE Executable. Modification of call forward numbers stored in the network shall only be permitted to numbers explicitly supplied by the user to the operator. 6– The Third Party domain's permission to access the networking action depends on the provisioning mechanism as described in subclause 8.15 |
| User private data access 1 Read Write Get properties Delete Get Location Information Read stored SMS Delete stored SMS Modify user preferences | Yes2 Yes2 Yes2 Yes2 Yes2 Yes2 Yes2 Yes7 |
| 1 – User private data includes user files, phonebook, etc located on the MS. 2 – The user shall be able to specify data access permissions within the capabilities of the device. It is not applied to user preferences 7 – Trusted applications only have permission to modify user preferences, and not to activate or de-activate them. The user shall be able to specify for each domain, the preferences that applications in that domain can access. All other preferences shall not be accessible to that domain. The default shall be that there is no access. Single action user permission is the only type of user permission that shall be possible for changes to User Preferences. |
| MExE security functions access Install a certificate for a given domain Uninstall a certificate for a given domain Replace a certificate for a given domain Data encryption API Verify a signature API Compute a digital signature API Hash a content API Non repudiation API | Yes 5 Yes 5 Yes 5 Yes Yes Yes Yes Yes |
| 5 – Only the organisation whose public key is certified (or the organisation that certified the public key) can add, delete or replace a particular certificate. |
| Application access Get application list Launch an application Get application status Stop, suspend, resume an application | Yes8 Yes8 Yes8 Yes9 |
| 8 – Device provisioned functionality access is limited to manufacturer domain. SIM tool kit application access is limited to operator domain. MExE executable access is limited to MExE executable issued by the same issuer (identify by the certificate) of launched MExE executable 9 – Access is limited to MExE executable which launch the application. But the end user, shall have a way to stop the launched application, MExE environment may stop the launched application or launched application may stop itself. |
| Lifecycle management Install a MExE Executable Uninstall a MExE executable | Yes |
| Terminal data access Get manufacturer software version Read time and date | Yes Yes |
| Peripheral access Sound generation to speaker (e.g. via stream) Set speaker volume printer access Monitor the power state Change the power state Activate/ access Serial port (RS232, Irda, Bluetooth, USB …) access Activate/access Parallel port Activate/access Smart card other than SIM card (Send APDU, Slot management) | Yes |
| Input output User interface access Input device (keyboard, mouse …) Output device (display ) Output notification device(smart icon, sound, light, vibrator …) | Yes10 Yes10 Yes |
| 10 – Access request no user permission. |

The lists in the groups in Table 3 are not exhaustive, and other actions which are of the same category shall be included in the group for the purposes of requesting user permission.